## Slide 1
Shi Miaomiao/swx791350

## Slide 2: Network Services and Applications

## Slide 3
The Internet has become an integral part of our lives, with a wide range of applications such as file transfer, email sending, online video, web browsing, and online gaming. Because of the layered network model, common users can use various services provided by the application layer, without knowing technical details such as communication technology implementations.
In previous courses, we have learned technologies related to the data link layer, network layer, and transport layer. This chapter will describe common network services and applications such as FTP, DHCP, and HTTP.

## Slide 4
On completion of this course, you will be able to:
  Understand FTP fundamentals.
  Understand TFTP fundamentals.
  Understand DHCP fundamentals.
  Understand Telnet fundamentals.
  Understand HTTP fundamentals.
  Understand DNS fundamentals.
  Understand NTP fundamentals.

## Slide 5
File Transfer
  FTP
  TFTP
Telnet
DHCP
HTTP
DNS
NTP

## Slide 6: File Transfer Protocols
File transfer between hosts is an important function of IP networks. Nowadays, people can conveniently transfer files using web pages and mailboxes.
However, in the early Internet era when the World Wide Web (WWW) did not come into being and operating systems used command-line interfaces, people transferred files via command-line tools. The most commonly used protocols for transferring files at that time are File Transfer Protocol (FTP) and Trivial File Transfer Protocol (TFTP).

## Slide 7: Basic Concepts of FTP
FTP adopts the typical client/server (C/S) architecture. After an FTP client establishes a TCP connection with an FTP server, files can be uploaded and downloaded.
FTP uses different transfer modes based on the file type:
  ASCII mode: When a text file (in TXT, LOG, or CFG format) is transferred, the encoding mode of the text content is converted to improve the transfer efficiency. This mode is recommended for transferring configuration files and log files of network devices.
  Binary mode: Non-text files (in CC, BIN, EXE, or PNG format), such as images and executable programs, are transferred in binary mode. This mode is recommended for transferring version files of network devices.
FTP client
FTP server
ASCII mode
Binary mode
Notes: FTP supports two transfer modes: ASCII and binary.
The ASCII mode is used to transfer text files. In this mode, the sender converts characters into the ASCII code format before sending them. After receiving the converted data, the receiver converts it back into characters. The binary mode is usually used to send image files and program files. In this mode, the sender can transfer files without converting the file format.
CC: VRP system file extension

## Slide 8: FTP Transfer Process - Active Mode
FTP client
FTP server
The FTP client initiates a TCP three-way handshake with TCP port 21 on the FTP server to set up a control connection.
User login authentication
The FTP client sends the PORT command to the FTP server, instructing it to open port P (random port; P > 1024).
The FTP server (port 20) initiates a TCP three-way handshake with TCP port P on the FTP client to set up a TCP connection.
File transfer
  FTP works in two modes: active mode (PORT) and passive mode (PASV).
Notes: In active mode, the FTP client uses a random port (with the number greater than 1024) to send a connection request to port 21 of the FTP server. After receiving the request, the FTP server sets up a control connection with the FTP client to transmit control messages. In the meantime, the FTP client starts to listen on port P (another random port with the number greater than 1024) and uses the PORT command to notify the FTP server. When data needs to be transmitted, the FTP server sends a connection request from port 20 to port P of the FTP client to establish a TCP connection for data transmission.

## Slide 9: FTP Transfer Process - Passive Mode
The FTP client initiates a TCP three-way handshake with TCP port 21 on the FTP server to set up a control connection.
User login authentication
The FTP client sends the PASV command.
The FTP client initiates a TCP three-way handshake with TCP port N on the FTP server to set up a TCP connection.
File transfer
The FTP server sends the Enter PASV command to the FTP client, instructing it to open port N (random port; N > 1024).
FTP client
FTP server
Notes: In passive mode, the FTP client uses a random port (with the number greater than 1024) to send a connection request to port 21 of the FTP server. After receiving the request, the FTP server sets up a control connection with the FTP client to transmit control messages. In the meantime, the FTP client starts to listen on port P (another random port with the number greater than 1024) and uses the PASV command to notify the FTP server. After receiving the PASV command, the FTP server enables port N (a random port with the number greater than 1024) and uses the Enter PASV command to notify the FTP client of the opened port number. When data needs to be transmitted, the FTP client sends a connection request from port P to port N on the FTP server to establish a transmission connection for data transmission.
The active mode and passive mode differ in data connection methods and have their own advantages and disadvantages.
  In active mode, if the FTP client is on a private network and a NAT device is deployed between the FTP client and the FTP server, the port number and IP address carried in the PORT packet received by the FTP server are not those of the FTP client converted using NAT. Therefore, the FTP server cannot initiate a TCP connection to the private IP address carried in the PORT packet. In this case, the private IP address of the FTP client is not accessible on the public network.
  In passive mode, the FTP client initiates a connection to an open port on the FTP server. If the FTP server lives in the internal zone of a firewall and inter-zone communication between this internal zone and the zone where the FTP client resides is not allowed, the client-server connection cannot be set up. As a result, FTP transfer fails.

## Slide 10: Configuration Commands (Device as FTP Server)
[Huawei]ftp [ ipv6 ] server enable
Enable the FTP server function.
By default, the FTP server function is disabled.
[Huawei]aaa
[Huawei]local-user user-name password irreversible-cipher password
[Huawei]local-user user-name privilege level level
[Huawei]local-user user-name service-type ftp
[Huawei]local-user user-name ftp-directory directory
Configure a local FTP user.
The privilege level must be set to level 3 or higher. Otherwise, the FTP connection fails.
A user accesses a device through FTP.

## Slide 11: Configuration Commands (Device as FTP Client)
<FTP Client>ftp 10.1.1.1
Trying 10.1.1.1 ...
Press CTRL+K to abort
Connected to 10.1.1.1.
220 FTP service ready.
User(10.1.1.1:(none)):ftp
331 Password required for ftp.
Enter password:
230 User logged in.
A VRP device that functions as an FTP client accesses an FTP server.
Common commands used when the VRP device functions as an FTP client.
ascii Set the file transfer type to ASCII, and it is the default type
binary Set the file transfer type to support the binary image
ls List the contents of the current or remote directory
passive Set the toggle passive mode, the default is on
get Download the remote file to the local host
put Upload a local file to the remote host

## Slide 12: Configuration Example
FTP server
10.1.1.1
FTP client
10.1.1.2
<Huawei> system-view
[Huawei] sysname FTP_Server
[FTP_Server] ftp server enable
[FTP_Server] aaa
[FTP_Server-aaa] local-user admin1234 password irreversible-cipher Helloworld@6789
[FTP_Server-aaa] local-user admin1234 privilege level 15
[FTP_Server-aaa] local-user admin1234 service-type ftp
[FTP_Server-aaa] local-user admin1234 ftp-directory flash:
Configurations on the FTP server:
<FTP Client>ftp 10.1.1.1
[FTP Client-ftp]get sslvpn.zip
200 Port command okay.
FTP: 828482 byte(s) received in 2.990 second(s) 277.08Kbyte(s)/sec.
Operations on the FTP client:
One router functions as the FTP server, and the other as the FTP client.
Enable the FTP service on the FTP server and create an FTP login account. Then, the FTP client logs in to the FTP server and runs the get command to download a file.

## Slide 13
File Transfer
  FTP
  TFTP
Telnet
DHCP
HTTP
DNS
NTP

## Slide 14: Basic Concepts of TFTP
Compared with FTP, TFTP is designed to transfer small files and is easier to implement.
  Using UDP (port 69) for transmission
  Authentication not required
  You can only request a file from or upload a file to the server, but cannot view the file directory on the server.
TFTP client
TFTP server
TFTP
UDP
IP

## Slide 15: TFTP Transfer Example
Download a File
TFTP client
TFTP server
Request for writing a file
File write confirmation
DATA 1
TFTP client
TFTP server
Request for reading a file
File read confirmation
Client confirmation
DATA 1
DATA 1 ACK
DATA 1 ACK
.
.
.
DATA n
DATA n ACK
.
.
.
Upload a File
Notes: TFTP supports five packet formats:
  RRQ: read request packet
  WRQ: write request packet
  DATA: data transmission packet
  ACK: acknowledgment packet, which is used to acknowledge the receipt of a packet from the peer end
  ERROR: error control packet

## Slide 16: Configuration Commands (Device as TFTP Client)
<HUAWEI> tftp tftp_server get filename
Download a file (VRP device functioning as a TFTP client).
You do not need to log in to the TFTP server, and only need to enter the IP address of the TFTP server and the corresponding command.
<HUAWEI> tftp tftp_server put filename
Upload a file (VRP device functioning as a TFTP client).
You do not need to log in to the TFTP server, and only need to enter the IP address of the TFTP server and the corresponding command.
Currently, VRP devices can function only as TFTP clients.

## Slide 17
File Transfer
Telnet
DHCP
HTTP
DNS
NTP

## Slide 18: Application Scenario of Telnet
To facilitate device management using commands, you can use Telnet to manage devices.
Device management through Telnet is different from that using the console port. In Telnet-based device management mode, no dedicated cable is required to directly connect to the console port of the Telnet server, as long as the Telnet server’s IP address is reachable and Telnet clients can communicate with the Telnet server’s TCP port 23.
The device that can be managed through Telnet is called the Telnet server, and the device connecting to the Telnet server is called the Telnet client. Many network devices can act as both the Telnet server and Telnet client.
Telnet client
IP network
AP
Router
Switch
Firewall
Server
...
Telnet server
TCP connection
Notes: Currently, mainstream network devices, such as access controllers (ACs), access points (APs), firewalls, routers, switches, and servers, can function as both the Telnet server and Telnet client.

## Slide 19: VTY User Interface
When a user logs in to a device using the console port or Telnet, the system allocates a user interface to manage and monitor the current session between the device and the user. A series of parameters can be set in each user interface view to specify the authentication mode and user privilege level after login. After a user logs in to a device, user operations that can be performed depend on the configured parameters.
The user interface type of Telnet is virtual type terminal (VTY) user interface.
Telnet client
Establish a Telnet connection
IP network
User interface
Telnet server
VTY 0
VTY 1
VTY 2
VTY 3
Authentication mode: local
User privilege: Level 15
Allocate an idle user interface with the smallest number from the VTY user interfaces.
Authenticate the Telnet connection using the VTY configuration.
1
2
3

## Slide 20: Configuration Commands (1)
[Huawei] telnet server enable
Enable the Telnet server function.
The Telnet server function is enabled on the device (disabled by default). To disable this function, run the undo telnet server enable command.
[Huawei] user-interface vty first-ui-number [ last-ui-number ]
Enter the user view.
The VTY user interface view is displayed. VTY user interfaces may vary according to device models.
[Huawei-ui-vty0-4]] protocol inbound { all | telnet | ssh}
Configure protocols supported by the VTY user interface.
By default, the VTY user interface supports Secure Shell (SSH) and Telnet.

## Slide 21: Configuration Commands (2)
[Huawei-ui-vty0-4] authentication-mode {aaa | none | password}
[Huawei-ui-vty0-4] set authentication password cipher
Configure the authentication mode and the authentication password in password authentication mode.
By default, no default authentication mode is available. You need to manually configure an authentication mode.
The set authentication password cipher command implementation varies according to VRP versions. In some versions, you need to press Enter and then enter the password. In other versions, you can directly enter the password after the command.

## Slide 22: Configuration Example (1)
Telnet client
10.1.1.1
Telnet connection
IP network
Telnet server
10.1.1.2
Configure the router at 10.1.1.2 as the Telnet server and set the authentication mode to AAA local authentication. Create an account named huawei, set the password to Huawei@123, and set the privilege level to 15.
Log in to and manage the Telnet server through the Telnet client.
<Huawei> system-view
[Huawei] telnet server enable
[Huawei] aaa
[Huawei-aaa] local-user huawei password irreversible-cipher Huawei@123
[Huawei-aaa] local-user huawei privilege level 15
[Huawei-aaa] local-user huawei service-type telnet
[Huawei-aaa] quit
[Huawei] user-interface vty 0 4
[Huawei-ui-vty0-4] authentication-mode aaa
Configurations on the Telnet server:

## Slide 23: Configuration Example (2)
Telnet client
10.1.1.1
IP network
Telnet server
10.1.1.2
<Host>telnet 10.1.1.2
Login authentication
Username:huawei
Password:
Info: The max number of VTY users is 5, and the number
of current VTY users on line is 1.
The current login time is 2020-01-08 15:37:25.
<Huawei>
Operations on the Telnet client:
Telnet connection
Configure the router at 10.1.1.2 as the Telnet server and set the authentication mode to AAA local authentication. Create an account named huawei, set the password to Huawei@123, and set the privilege level to 15.
Log in to and manage the Telnet server through the Telnet client.

## Slide 24
File Transfer
Telnet
DHCP
HTTP
DNS
NTP

## Slide 25: Issues Faced by Manual Network Parameter Configuration (1)
Mask
Address
Gateway
Work Plan of This Week
Address allocation
Address allocation
Address configuration
Address configuration
Network administrator
Huge Workload
Common users are not familiar with network parameters and misconfiguration often occurs, resulting in network access failure. Random IP address configuration may cause IP address conflicts.
Network administrators centrally configure network parameters, with heavy workloads and repetitive tasks.
Network administrators need to plan and allocate IP addresses to users in advance.
IP address
Mask
Gateway
. | . | . | 
. | . | . | 
. | . | . | 
IPv4 address configuration:
Too Many Hard-to-Understand Parameters

## Slide 26: Issues Faced by Manual Network Parameter Configuration (2)
Moving between offices
Offline user
Online user
Poor Flexibility
On an enterprise network, each user uses a fixed IP address. As a result, the IP address utilization is low, and some IP addresses may remain unused for a long time.
Wireless local area networks (WLANs) allow for flexible station (STA) access locations. When a STA moves from one wireless coverage area to another, the IP address of the STA may need to be reconfigured.
Office A
Office B
Low Utilization

## Slide 27: Basic Concepts of DHCP
DHCP server
Assign IP addresses
Request IP addresses
DHCP client
DHCP Working Principle
To overcome the disadvantages of the traditional static IP configuration mode, the Dynamic Host Configuration Protocol (DHCP) is developed to dynamically assign suitable IP addresses to hosts.
DHCP adopts the client/server (C/S) architecture. Hosts do not need to be configured and can automatically obtain IP addresses from a DHCP server. DHCP enables host plug-and-play after they are connected to the network.

## Slide 28: DHCP Advantages
DHCP client
DHCP client
DHCP server
DHCP address request
Pool-No 1
DNS-server 10.1.1.2 | Gateway 10.1.2.1
Network 10.1.2.0 | Mask 255.255.255.0
Total Used
252 2
DHCP client
DHCP server
DHCP address request
DHCP address response
IP:192.168.1.10
Network mask:24
Gateway:192.168.1.1
DNS: 114.114.114.114
Lease: 8 hour
IP Address Lease
IP addresses are obtained from the address pool on the DHCP server. The DHCP server records and maintain the usage status of IP addresses for unified IP address assignment and management.
DHCP defines the lease time to improve IP address utilization.
Unified Management
Notes: If a DHCP client does not renew the lease of an assigned IP address after the lease expires, the DHCP server determines that the DHCP client no longer needs to use this IP address, reclaims it, and may assign it to another client.

## Slide 29: DHCP Working Principle
Question: Why does a DHCP client need to send a DHCP Request packet to the DHCP server to notify its use of a particular IP address after receiving a DHCP Offer packet?
DHCP server
DHCP client
Sent by the DHCP client
Sent by the DHCP server
DHCP Discover (broadcast): used to discover the DHCP server on the current network.
DHCP Offer (unicast): carries the IP address assigned to the client.
DHCP Request (broadcast): informs the server that it will use this IP address.
DHCP ACK (unicast): acknowledges the client’s use of this IP address.
Layer 2 broadcast domain
Pool-No | 1
Total Address | 255
Used Address | 2
Notes: A client's DHCP Request packet is broadcast, so other DHCP servers on the network know that the client has selected a particular IP address assigned by the DHCP server. This ensures that other DHCP servers can release this IP address assigned to the client through the unicast DHCP Offer packet.

## Slide 30: DHCP Lease Renewal
If the DHCP client fails to receive a response from the original DHCP server at 50% of the lease (known as T1), the DHCP client waits until 87.5% of the lease (known as T2) has passed. At T2, the client enters the rebinding state, and broadcasts a DHCP Request packet, to which any DHCP server can respond.
DHCP server
DHCP client
DHCP Request (unicast): requests the server for an IP address lease renewal.
DHCP ACK (unicast): notifies the client that the IP address can be renewed and the lease is updated.
50% of the lease
Layer 2 broadcast domain
Pool-No | 1
Total Address | 255
Used Address | 2
Lease | 8 Hours
Sent by the DHCP client
Sent by the DHCP server

## Slide 31: Configuration Commands (1)
[Huawei] dhcp enable
Enable DHCP.
[Huawei-Gigabitthernet0/0/0]dhcp select interface
Enable the interface to use the interface address pool to provide the DHCP server function.
[Huawei-Gigabitthernet0/0/0]dhcp server dns-list ip-address
Specify a DNS server IP address for the interface address pool.
[Huawei-Gigabitthernet0/0/0]dhcp server excluded-ip-address start-ip-address [ end-ip-address ]
Configure the range of IP addresses that cannot be automatically assigned to clients from the interface address pool.
[Huawei-Gigabitthernet0/0/0]dhcp server lease { day day [ hour hour [ minute minute ] ] | unlimited }
Configure the lease of IP addresses in the interface address pool of the DHCP server.
By default, the IP address lease is one day.

## Slide 32: Configuration Commands (2)
[Huawei]ip pool ip-pool-name
Create a global address pool.
[Huawei-ip-pool-2]network ip-address [ mask { mask | mask-length } ]
Specify the range of IP addresses that can be assigned dynamically in the global address pool.
[Huawei-ip-pool-2]gateway-list ip-address
Configure the gateway address for DHCP clients.
[Huawei-ip-pool-2]dns-list ip-address
Specify the DNS server IP address that the DHCP server delivers to DHCP clients.
[Huawei-ip-pool-2] lease { day day [ hour hour [ minute minute ] ] | unlimited }
Set the IP address lease.
[Huawei-Gigabitthernet0/0/0]dhcp select global
Enable the DHCP server function on the interface.

## Slide 33: DHCP Interface Address Pool Configuration
[Huawei]dhcp enable
[Huawei]interface GigabitEthernet0/0/0
[Huawei-GigabitEthernet0/0/0]dhcp select interface
[Huawei-GigabitEthernet0/0/0]dhcp server dns-list 10.1.1.2
[Huawei-GigabitEthernet0/0/0]dhcp server excluded-ip-address 10.1.1.2
[Huawei-GigabitEthernet0/0/0]dhcp server lease day 3
Configuration on the DHCP server:
Enable the DHCP service globally, enter the interface view, associate the current interface with the DHCP address pool, configure the DNS address and excluded IP address (excluding the interface IP address) in the interface view, and configure the lease of the IP addresses assigned to clients.
Requirement:
Configure a router as the DHCP server, configure the subnet to which GE0/0/0 belongs as the address pool of DHCP clients, set the IP address of GE0/0/0 to that of the DNS server, and set the lease to three days.
DHCP server
DHCP client
GE0/0/0
10.1.1.1/24
Layer 2 broadcast domain

## Slide 34: DHCP Global Address Pool Configuration
[Huawei]dhcp enable
[Huawei]ip pool pool2
Info: It's successful to create an IP address pool.
[Huawei-ip-pool-pool2]network 1.1.1.0 mask 24
[Huawei-ip-pool-pool2]gateway-list 1.1.1.1
[Huawei-ip-pool-pool2]dns-list 1.1.1.1
[Huawei-ip-pool-pool2]lease day 10
[Huawei-ip-pool-pool2]quit
[Huawei]interface GigabitEthernet0/0/0
[Huawei-GigabitEthernet0/0/1]dhcp select global
Configuration on the DHCP server:
Enable the DHCP service globally and configure the global address pool pool2. Configure the address range, gateway address, DNS address, and lease for pool2.
Select the global address pool on a specific interface (GE0/0/0). When GE0/0/0 receives a DHCP request, it assigns an IP address from the global address pool.
DHCP server
DHCP client
GE0/0/0
10.1.1.1/24
Requirement:
Configure a router as the DHCP server and configure the global address pool pool2 to assign IP addresses (on the subnet 1.1.1.0/24) to DHCP clients. Set both the gateway address and DNS address to 1.1.1.1, set the lease to 10 days, and enable GE0/0/0 to use the global address pool.
Layer 2 broadcast domain

## Slide 35
File Transfer
Telnet
DHCP
HTTP
DNS
NTP

## Slide 36: Web Page Access Using a Browser
www.huawei.com
When you enter a uniform resource locator (URL) in a browser, the browser can obtain data from a web server and display the content on the page.
Hypertext Transfer Protocol (HTTP): an application layer protocol for communication between a client browser or another program and a web server
HTTP adopts the typical C/S architecture, and uses TCP for transmission.
HTTP request
HTTP response
The browser sends an HTTP request to the server to obtain page resources.
The server returns the corresponding page content through an HTTP response.
Web server
Notes: URL: uniquely identifies the location of a web page or other resources on the Internet. A URL can contain more detail, such as the name of a page of hypertext, usually identified by the file name extension .html or .htm.

## Slide 37: Background
WWW
In the early days of the Internet, World Wide Web (WWW) was proposed to share documents.
The WWW consists of three parts: Hypertext Markup Language (HTML) for displaying document content in a browser, HTTP for transmitting documents on the network, and URLs for specifying document locations on the network.
WWW was actually the name of a client application for browsing HTML documents, and now represents a collection of technologies (HTML + HTTP + URL) and is commonly known as the Web.
The WWW is comprised of the web servers and clients all over the world.

## Slide 38: Transfer Example (1)
Web server
Web client
Internet
www.servs_app.com/web/index.html
GET /web/index.html HTTP /1.0
HOST:www.servs_app.com
HTTP request
HTTP response
The URL www.servs_app.com/web/index.html is entered in the address box of a browser. After obtaining the IP address corresponding to the domain name through DNS resolution, the client sends an HTTP request to the server to request the page.

## Slide 39: Transfer Example (2)
www.servs_app.com/web/index.html
Web Server
Host:www.servs_app.com
├── bin
├── etc
├── sbin
├── share
└── web
└── index.html
File System
The server finds the locally stored page file based on the URL and sends the page file to the client.
HTTP /1.1 200 ok
Index.html
GET /web/index.html HTTP /1.0
HOST:www.servs_app.com
Welcome to servs_app.com
This is an HTML Example Page
After receiving the HTTP response, the browser parses and renders the received HTML file, and then displays the page to the user.
Web server
Web client
Internet
HTTP request
HTTP response

## Slide 40
File Transfer
Telnet
DHCP
HTTP
DNS
NTP

## Slide 41: Birth of DNS
When you enter a domain name in your browser to access a website, the domain name is resolved to an IP address. The browser actually communicates with this IP address.
The protocol used for resolving domain names to IP addresses is Domain Name System (DNS).
Each node on the network has a unique IP address, and nodes can communicate with one another through IP addresses. However, if all nodes communicate through IP addresses, it is difficult to remember so many IP addresses. Therefore, DNS is proposed to map IP addresses to alphanumeric character strings (domain names).
Web server
1.2.3.4
Web client
192.168.1.1
Internet
www.huawei.com
1.2.3.4
Domain name resolution
HTTP
Source IP: 192.168.1.1
Destination IP: 1.2.3.4
1
HTTP access request
2
Notes: Advanced Research Projects Agency Network (ARPANET), the predecessor of the Internet, provides the mappings between host names and IP addresses. However, the number of hosts was small at that time. Only one file (HOSTS.txt) is required to maintain the name-to-address mapping. The HOSTS.txt file is maintained by the network information center (NIC). Users who change their host names send their changes to the NIC by email, and the NIC periodically updates the HOSTS.txt file.
However, after ARPANET uses TCP/IP, the number of network users increases sharply, and it seems difficult to manually maintain the HOSTS.txt file. The following issues may occur:
  Name conflict: Although the NIC can ensure the consistency of host names that it manages, it is difficult to ensure that the host names are not randomly changed to be the same as those being used by others.
  Consistency: As the network scale expands, it is hard to keep the HOSTS.txt file consistent. The names of other hosts may have been changed several times before the HOSTS.txt file of the current host is updated.
Therefore, DNS is introduced.

## Slide 42: DNS Components
Domain name: a sequence of characters to identify hosts. In most cases, the URL entered in the browser when you visit a website is the domain name of the website.
DNS server: maintains the mappings between domain names and IP addresses and responds to requests from the DNS resolver.
Internet
DNS client
DNS server
Domain name info
Row 1
Row 2
Row 3
DNS request
DNS response
DNS query: domain name A
UDP
DNS reply: IP of domain name A is 1.1.1.1
UDP
Notes: The DNS adopts a distributed architecture. The database on each server stores only the mapping between some domain names and IP addresses.

## Slide 43: Domain Name Format
The domain name is in the format of hostname.second-level domain.top-level domain.root domain. The root domain is represented by a dot (.). Generally, the root domain is denoted by an empty name (that is, containing no characters).
.
Root domain
.com
.net
.cn
.edu
.org
.gov
Top-level domain
huawei
Second-level domain
www
Hostname
The domain name of the host is www.huawei.com.

## Slide 44: DNS Query Modes
The DNS is a distributed system. The database of most DNS servers does not have all domain name records. When a client queries a domain name from a DNS server but the DNS server does not have the record of the domain name, the client can continue the query in either of the following ways:
  Recursive query: The DNS server queries other DNS servers and returns the query result to the DNS client.
  Iterative query: The DNS server informs the DNS client of the IP address of another DNS server, from which the DNS client queries the domain name.
Recursive Query
Iterative Query
DNS client
DNS server 1
DNS server 2
DNS request
DNS response
1
2
3
4
DNS request
DNS response
DNS client
DNS server 2
DNS server 1
1
2
3
4
Notes: The iterative query is different from the recursive query in that the DNS response returned by DNS server 1 contains the IP address of another DNS server (DNS server 2).

## Slide 45
File Transfer
Telnet
DHCP
HTTP
DNS
NTP

## Slide 46: Time Synchronization Requirements
Consistent clock of all devices is required in many scenarios on enterprise campus networks:
  Network management: Analysis of logs or debugging messages collected from different routers needs time for reference.
  Charging system: The clocks of all devices must be consistent.
  Several systems working together on the same complicate event: Systems have to take the same clock for reference to ensure a proper sequence of implementation.
  Incremental backup between a backup server and clients: Clocks on the backup server and clients should be synchronized.
  System time: Some applications need to know the time when users log in to the system and the time when files are modified.

## Slide 47: NTP Overview
If the administrator manually enters commands to change the system time for time synchronization, the workload is heavy and the accuracy cannot be ensured. Therefore, the Network Time Protocol (NTP) is designed to synchronize the clocks of devices.
NTP is an application layer protocol belonging to the TCP/IP suite and synchronizes time between a group of distributed time servers and clients. NTP is based on IP and UDP, and NTP packets are transmitted using UDP on port number 123.
NTP client
AP
Router
Switch
Firewall
Server
...
NTP server
PC
Time synchronization
Notes: Currently, mainstream network devices, such as access controllers (ACs), access points (APs), firewalls, routers, switches, and servers, basically serve as NTP clients, and some of the network devices can also serve as NTP servers.

## Slide 48: NTP Network Structure
Primary time server: directly synchronizes its clock with a standard reference clock through a cable or radio. Typically, the standard reference clock is either a radio clock or the Global Positioning System (GPS).
Stratum-2 time server: synchronizes its clock with either the primary time server or other stratum-2 time servers within the network. Stratum-2 time servers use NTP to send time information to other hosts in a Local Area Network (LAN).
Stratum: is a hierarchical standard for clock synchronization. It represents the precision of a clock. The value of a stratum ranges from 1 to 15. A smaller value indicates higher precision. The value 1 indicates the highest clock precision, and the value 15 indicates that the clock is not synchronized.
NTP client
AP
Router
Switch
Firewall
Server
PC
Primary time server 1
Stratum-2 time server
Stratum-2 time server
Stratum 1
Stratum 2
Stratum 3
...

## Slide 49
Which FTP mode is recommended for transferring log and configuration files on network devices? Why?
Why does a DHCP client need to send a DHCP Request packet to the DHCP server to notify its use of a particular IP address after receiving a DHCP Offer packet?
What are the functions of HTML, URL, and HTTP?
Notes: ASCII mode; The binary mode is more applicable to the transmission of non-text files that cannot be converted, such as EXE, BIN, and CC (VRP version file extension) files.
A client's DHCP Request packet is broadcast, so other DHCP servers on the network know that the client has selected a particular IP address assigned by the DHCP server. This ensures that other DHCP servers can release this IP address assigned to the client through the unicast DHCP Offer packet.
HTML is used to display page content, URL is used to locate the network location of a document or file, and HTTP is used for requesting and transferring files.

## Slide 50
FTP is used to transfer files. You are advised to use different transfer modes for different files. FTP is based on TCP and therefore can ensure the reliability and efficiency of file transfer.
Dynamically assigning IP addresses through DHCP reduces the workload of the administrator and avoids IP address conflicts caused by manual configuration of network parameters.
As the document transfer protocol of WWW, HTTP is widely used in today's network for encoding and transporting information between a client (such as a web browser) and a web server.