## Slide 1: STP Concept, Principles and Improvements
Ali Dayoub

## Slide 2
Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement

## Slide 3: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Redundancy and Loops on a Layer 2 Switching Network.
A network without redundancy design
The access switch has only one uplink, and no redundancy is available. If a fault occurs, the downstream PC will be disconnected.
Access switch
Aggregation switch
There is only one aggregation switch, and no redundancy is available. If a fault occurs, the downstream host will be disconnected.

## Slide 4: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Redundancy and Loops on a Layer 2 Switching Network.
Layer 2 loops introduced along with redundancy
Aggregation switch
Aggregation switch
Access switch
Layer 2
loop
The network redundancy is enhanced, but a Layer 2 loop occurs.

## Slide 5: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Layer 2 Loops Caused by Human Errors
Case 1
Layer 2
loop
Incorrect operations: For example, connections of cables between devices are incorrect.

## Slide 6: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Layer 2 Loops Caused by Human Errors
Case 2
Layer 2
loop
Incorrect manual configurations: For example, the network administrator does not bind the link between SW1 and SW2 to a logical link (aggregation link), causing Layer 2 loops.
SW1
SW2

## Slide 7: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Issues Caused by Layer 2 Loops
BUM frame
1
2
2
3
3
4
4
Typical Issue 1: Broadcast Storm
When SW3 receives the BUM frames, it floods the frames. After SW1 and SW2 receive the BUM frames, they flood the frames again. As a result, network resources are exhausted and the network is unavailable.
SW1
SW2
SW3

## Slide 8: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Issues Caused by Layer 2 Loops
Typical Issue 2: MAC Address Flapping
BUM frame
Source MAC address: 5489-98EE-788A
1
SW1
SW2
SW3
GE0/0/1
GE0/0/2
SW1 is used as an example. The MAC address of 5489-98EE-788A is frequently switched between GE0/0/1 and GE0/0/2, causing MAC address flapping.

## Slide 9: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Introduction to STP
STP
STP
STP
BPDUs
SW1
(Root)
SW1
SW2
SW3
SW2
SW3
Eliminate Layer 2 loop
Port blocked

## Slide 10: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Can Dynamically Respond to Network Topology Changes and Adjust Blocked Ports
Blocked port
SW1
SW2
SW3
1
Link fault
SW1
SW2
SW3
Restored port
2
3

## Slide 11
Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement

## Slide 12: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: BID (Bridge ID )
SW1
SW2
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
SW3
Bridge priority
Bridge MAC address
BID
Root Bridge
Cost
RPC
PID
BPDU
The bridge priority occupies the leftmost 16 bits and the MAC address occupies the rightmost 48 bits.

## Slide 13: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: Root Bridge
BID
Root Bridge
Cost
RPC
PID
BPDU
SW1
SW2
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
SW3
Root bridge
The root bridge is the root of an STP network.
On an STP network, the device with the smallest BID acts as the root bridge.

## Slide 14: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: Cost
BID
Root Bridge
Cost
RPC
PID
BPDU
SW1
SW2
SW3
Cost = 500
Cost = 500
Cost = 20000
Cost = 20000
Cost = 20000
Cost = 20000
Each STP-enabled port maintains a cost. The cost of a port is used to calculate the root path cost (RPC), that is, the cost of the path to the root.

## Slide 15: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: RPC
BID
Root Bridge
Cost
RPC
PID
BPDU
SW1
SW2
SW3
Cost=500
Cost=500
Cost=20000
Cost=20000
Cost=20000
Cost=20000
1
2
GE0/0/1
RPC=500+20000
Root bridge
The cost from a switch port to the root bridge, that is, RPC, is important during STP topology calculation.

## Slide 16: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: PID (Port ID )
BID
Root Bridge
Cost
RPC
PID
BPDU
An STP-enabled switch uses PIDs to identify ports. A PID is used to elect a designated port in a specific scenario.
SW1
SW2
SW3
PID=128.24
PID=128.24
PID=128.23
PID=128.21
PID=128.23
PID=128.22

## Slide 17: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Basic Concepts: BPDU (Bridge Protocol Data Unit)
BID
Root Bridge
Cost
RPC
PID
BPDU
STP-enabled switches exchange BPDUs that carry important information.
There are two types of BPDUs:
  Configuration BPDU
  Topology Change Notification (TCN) BPDU
Configuration BPDU
SW1
SW2
SW3

## Slide 18: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Format of Configuration BPDUs
PID | PVI | BPDU Type | Flags | Root ID | RPC | Bridge ID | Port ID | Message Age | Max Age | Hello Time | Forward Delay
Field
Protocol Identifier
Protocol Version Identifier
BPDU Type
Flags
Root Identifier
Root Path Cost
Bridge Identifier
Port Identifier
Message Age
Max Age
Hello Time
Forward Delay
The Root Identifier, Root Path Cost, Bridge Identifier, and Port Identifier fields are the main fields of a configuration BPDU. STP-enabled switches compare the four fields.
STP selects the optimal configuration BPDU in the following sequence:
Smallest BID of the root bridge
Smallest RPC
Smallest BID of the network bridge
Smallest PID

## Slide 19: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Calculation (1)
Select a Root Bridge on the Switching Network
Configuration BPDU
SW1
SW2
SW3
4096.4c1f-aabc-102a
4096.4c1f-aabc-102c
Root bridge
After STP starts to work on a switching network, each switch sends configuration BPDUs to the network. The configuration BPDU contains the BID of a switch.
The switch with the smallest bridge ID becomes the root bridge.
Only one root bridge exists on a contiguous STP switching network.

## Slide 20: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Calculation (2)
Select a Root Port on Each Non-root Bridge
SW1
SW2
SW3
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
Configuration BPDU
Root port
R
R
R
Each non-root bridge selects a root port from its ports.
A non-root bridge has only one root port.
The root port is located on each non-root bridge and has the shortest distance away from the root bridge.

## Slide 21: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Calculation (3)
A designated port is elected on each link.
Configuration BPDU
Root port
D
Designated port
SW1
SW2
SW3
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
D
D
D
R
R
R
After the root port is elected, the non-root bridge uses the optimal BPDU received on the port to calculate the configuration BPDU and compares the calculated configuration BPDU with the configuration BPDUs received by all ports except the root port.
  If the former is better, the port is a designated port.
  If the latter is better, the port is not a designated port.
In most cases, all ports on the root bridge are designated ports.

## Slide 22: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
STP Calculation (4)
Block Non-designated Port
On a switch, a port that is neither a root port nor a designated port is called a non-designated port.
The last step of STP operations is to block the non-designated port on the network. After this step is complete, the Layer 2 loop on the network is eliminated.
Configuration BPDU
R
Root port
D
Designated port
SW1
SW2
SW3
R
R
D
D
D
Blocked port

## Slide 23: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Topology Change: Root Bridge Fault
SW1 (root bridge) is faulty and stops sending BPDUs.
SW2 waits for the Max Age timer (20s) to expire. SW2 learns that the upstream device is faulty.
Non-root bridges send configuration BPDUs to each other to elect a new root bridge.
SW1
SW2
SW3
A
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
Root Bridge Fault Rectification Process

## Slide 24: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Topology Change: Direct Link Fault
On a stable network, when SW2 detects that the link of the root port is faulty, the alternate port of SW2 enters the Forwarding state after twice the value of the Forward Delay timer (the default value is 15s).
After SW2 detects a fault on the direct link, it switches the alternate port to the root port.
If a direct link fails, the alternate port restores to the Forwarding state after 30s.
SW1
SW2
SW3
A
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
A
Direct Link Fault Rectification Process

## Slide 25: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Topology Change: Indirect Link Fault
SW1
SW2
SW3
A
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
D
SW1
SW2
SW3
4096.4c1f-aabc-102a
4096.4c1f-aabc-102b
4096.4c1f-aabc-102c
D
R
When the indirect link fails, the alternate port on SW3 restores to the Forwarding state. It takes about 50s to recover from an indirect link failure.

## Slide 26
Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement

## Slide 27: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Disadvantages of STP
If the network topology changes frequently, connections on the STP network are frequently torn down, causing frequent service interruption.
STP does not differentiate between port roles according to their states, making it difficult for less experienced administrators to learn about and deploy this protocol.
The STP algorithm does not determine topology changes until the timer expires, delaying network convergence.
The STP algorithm requires the root bridge to send configuration BPDUs after the network topology becomes stable, and other devices process and spread the configuration BPDUs through the entire network. This also delays convergence.

## Slide 28: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Improvements Made in RSTP (Rapid Spanning Tree Protocol)
RSTP processes configuration BPDUs differently from STP.
When the topology becomes stable, the mode of sending configuration BPDUs is optimized.
RSTP uses a shorter timeout interval of BPDUs.
RSTP optimizes the method of processing inferior BPDUs.
RSTP changes the configuration BPDU format and uses the Flags field to describe port roles.
RSTP topology change processing: Compared with STP, RSTP is optimized to accelerate the response to topology changes.

## Slide 29: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Port Roles in RSTP
R
Root port
D
Designated port
A
Alternate port
B
Backup port
SW1 (root bridge)
SW2
SW3
D
D
R
R
A
B
SW1 (root bridge)
SW2
SW3
D
D
R
R
A
D
D
RSTP adds port roles to help understand RSTP and simplify RSTP deployment.

## Slide 30
Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement

## Slide 31: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
Defects of STP/RSTP: All VLANs Share One Spanning Tree
STP and RSTP both have a defect: All VLANs on a LAN share one spanning tree. As a result, inter-VLAN load balancing cannot be performed, and blocked links cannot transmit any traffic, which may lead to VLAN packet transmission failures.
SW3
SW1
SW2
GE0/0/2
VLAN 1, 2, 3…
Blocked port
Data from all VLANs

## Slide 32: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
VBST
Huawei provides the VLAN-based Spanning Tree (VBST). VBST constructs a spanning tree in each VLAN so that traffic from different VLANs is load balanced along different spanning trees.
SW3
SW1
SW2
VLAN 1, 2, 3…
Data in an odd-numbered VLAN
Blocked port in an even-numbered VLAN
Blocked port in an odd-numbered VLAN
Data in an even-numbered VLAN
Root
Spanning tree
of VLAN 1
Root
Spanning tree
of VLAN 2
Root
Spanning tree
of VLAN 3
Independent spanning trees are formed for different VLANs.

## Slide 33: Content:
STP Overview
Basic Concepts and Working Mechanism of STP
Improvements Made in RSTP
STP Advancement
MSTP
To fix the defects, the IEEE released the 802.1s standard that defines the Multiple Spanning Tree Protocol (MSTP) in 2002.
MSTP is compatible with STP and RSTP, and can rapidly converge traffic and provides multiple paths to load balance VLAN traffic.
SW3
SW1
SW2
VLAN 1, 2, 3…
Data in an odd-numbered VLAN
Blocked port in MSTI 1
Blocked port in MSTI 2
Data in an even-numbered VLAN
Root
Spanning tree
of MSTI 1
Root
Spanning tree
of MSTI 2

## Slide 34: thank you for your attention