## Slide 1
Zhang Linrui /zwx570554

## Slide 2: Typical Campus Network Architectures and Practices

## Slide 3
A broad range of places, such as campuses, office spaces, and shopping malls, are covered by networks. You can access internal resources of your school, access internal printers of your company to print documents, or access the Internet to browse news through the networks.
These networks belong to campus networks and are generally constructed by enterprises or organizations. Campus networks not only improve the operational efficiency of enterprises, but also provide network access services for external users.
This chapter describes the basic architecture of a campus network and details how to build a campus network.

## Slide 4
Upon completion of this course, you will be able to:
  Understand the definition of campus networks.
  Understand the typical networking architectures of campus networks.
  Master the planning and design methods of small campus networks.
  Master the deployment and implementation methods of small campus networks.
  Understand the small campus network O&M concepts.
  Understand the small campus network optimization concepts.
  Independently complete a campus network project.

## Slide 5
Basic Concepts of Campus Networks
Typical Campus Network Construction Process

## Slide 6: What Is a Campus Network?
A campus network is a local area network (LAN) that connects people and things in a specified area. Typically, a campus network has only one management entity. If there are multiple management entries in an area, the area is considered to have multiple campus networks.
Branch
Other campuses
Remote access user
Private and public clouds
Internet/Wide area network (WAN)
Outside a campus
Inside a campus
Campus egress layer
Core layer
Aggregation layer
Access layer
Network
management
Data center
Demilitarized zone (DMZ)
Network security
Terminal layer
Typical scenario
Office building
Government
Enterprise
Campus
Factory
Bank
Notes: The campus network scale is flexible depending on actual requirements. It can be a small office home office (SOHO), a school campus, enterprise campus, park, or shopping center. However, the campus network cannot be scaled out infinitely. Typically, large campuses, such as university campuses and industrial campuses, are limited within several square kilometers. Such campus networks can be constructed using local area network (LAN) technology. A campus network beyond this scope is usually considered as a metropolitan area network (MAN) and is constructed using the WAN technology.
Typical LAN technologies used on campus networks include IEEE 802.3-compliant Ethernet (wired) technologies and IEEE 802.11-compliant Wi-Fi (wireless) technologies.

## Slide 7: Typical Campus Network Architecture
WAN
Internet
IPS
Firewall
Anti-DDoS
AC
eLog
Typically, a campus network is designed in a hierarchical and modular manner.
Campus networks can be classified into small, midsize, and large campus networks based on the number of terminals or NEs.
Access layer
Aggregation layer
Core layer
Egress zone
Data center
Network management zone
Traveling employees
Branch campus
Notes: Typical layers and areas of a campus network:
  Core layer: is the backbone area of a campus network, which is the data switching core. It connects various parts of the campus network, such as the data center, management center, and campus egress.
  Aggregation layer: is a middle layer of a campus network, and completes data aggregation or switching. Some fundamental network functions, such as routing, QoS, and security, are also provided at this layer.
  Access layer: As the edge of a campus network, this layer connects end users to the campus network.
  Egress area: As the edge that connects a campus network to an external network, this area enables mutual access between the two networks. Typically, a large number of network security devices, such as intrusion prevention system (IPS) devices, anti-DDoS devices, and firewalls, are deployed in this area to defend against attacks from external networks.
  Data center area: has servers and application systems deployed to provide data and application services for internal and external users of an enterprise.
  Network management area: Network management systems, including the SDN controller, WAC, and eLog (log server), are deployed in this area to manage and monitor the entire campus network.

## Slide 8: Typical Architecture of Small Campus Networks
Small campus networks are typically deployed in scenarios where the number of access users is small (several or dozens of users). A small campus network can cover only one location, has a simple architecture, and is constructed to enable mutual access between internal resources.
Characteristics of small campus networks:
  Small number of users
  Only one location
  Simple network architecture
  Simple network requirements
Number of terminals | < 200
Number of NEs | < 25
Network topology of a chain cafe
Host
Fat AP
Internet

## Slide 9: Typical Architecture of Midsize Campus Networks
A midsize campus network supports access of hundreds to thousands of users.
The modular design is introduced to midsize campus networks, that is, the networks can be partitioned by function. However, the number of function modules is small. In most cases, a midsize campus network is flexibly partitioned based on service requirements.
Characteristics of midsize campus networks:
  Midsize network scale
  Most commonly used
  Function partition
  Typical three-layer network architecture: core, aggregation, and access
Number of terminals | 200 to 2000
Number of NEs | 25 to 100
Internet
Access layer
Aggregation layer
Core layer
Egress layer
AP
AC
Network topology of a foreign trade company

## Slide 10: Typical Architecture of Large Campus Networks
A large campus network can cover multiple buildings and connect to multiple campuses in a city through WANs. Typically, a large campus network provides access services and allows traveling employees to access their company's internal network through technologies such as Virtual Private Network (VPN).
Characteristics of large campus networks:
  Wide coverage
  Large number of users
  Complex network requirements
  Comprehensive function modules
  Complex network architecture
Number of terminals | > 2000
Number of NEs | > 100
Traveling employees
HQ campus
Branch campus
Internet/WAN
Cloud DC
Network management
Network topology of a large enterprise

## Slide 11: Main Protocols and Technologies of Campus Networks
Common protocols/technologies
Egress zone
Core layer
Aggregation layer
Access layer
VLAN, spanning tree, link aggregation, and AAA
DHCP, stacking, link aggregation, spanning tree protocol, OSPF, and static routing
Stacking, OSPF, static routing, and ACL
NAT, OSPF, static routing, and PPPoE
WLAN protocols/technologies
SNMP/
NETCONF
AC
NMS

## Slide 12
Basic Concepts of Campus Networks
Campus Network Project Practice

## Slide 13: Networking Requirements
A company (with about 200 employees) plans to build a brand-new campus network to meet service development requirements. The network requirements are as follows:
  Meet the current services requirements of the company.
  Use a simple network topology for easy O&M.
  Provide wired access for employees and wireless access for guests.
  Implement simple network traffic management.
  Ensure network security.

## Slide 14: Campus Network Project Lifecycle
Planning and design
Device model selection
Physical topology
Logical topology
Technologies and protocols
Deployment and implementation
Device installation
Single UPS commissioning
Joint commissioning test
Network migration and integration
Network O&M
Routine maintenance
Software and configuration backup
Centralized monitoring via the network management system (NMS)
Software upgrade
Network optimization
Network security improvement
Software and configuration backup
User experience improvement
1
2
3
4
Notes: A campus network project starts from network planning and design. Comprehensive and detailed network planning will lay a solid foundation for subsequent project implementation.
Project implementation is a specific operation procedure for engineers to deliver projects. Systematic management and efficient process are critical to successful project implementation.
Routine O&M and troubleshooting are required to ensure the normal running of network functions and support smooth provisioning of user services.
As users' services develop, the users' requirements on network functions increase. If the current network cannot meet service requirements, or potential problems are found while the network is running, the network needs to be optimized.

## Slide 15: Small Campus Network Design
1. Networking solution design
Device model selection
Physical topology
3. Security design
Egress security
Intranet wired security
Intranet wireless security
4. Network O&M and management design
Basic network management
Intelligent O&M
2. Network design
Basic service
WLAN
Layer 2 loop prevention
Network reliability
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 16: Networking Solution Design
The physical topology is designed upon full consideration of the budget and service requirements. The following figure shows the topology.
AC1
Internet
CORE-R1
Agg-S1
AP1
AP2
Guest reception center
Acc-S1
R&D department
FTP server
Printer
Acc-S2
Marketing department
Printer
Acc-S3
Administrative department
Administrator
Acc-S4
Printer
GE0/0/1
GE0/0/2
GE0/0/1
GE0/0/3
E0/0/1
E0/0/1
E0/0/1
E0/0/1
Naming and interface selection rules
The names should be easy to remember and can be extended.
The interfaces should meet the bandwidth requirements of services.
GE0/0/1
GE0/0/0
GE0/0/4
GE0/0/5
GE0/0/6
E0/0/10
E0/0/11
GE0/0/0
GE0/0/0
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization
Notes: The entire network uses a three-layer architecture.
  The S3700 is deployed as the access switch to provide 100 Mbit/s network access for employees' PCs and printers.
  The S5700 is deployed at the aggregation layer as the gateway of the Layer 2 network.
  The AR2240 is deployed at the core and egress of a campus network.
Note: Agg is short for aggregation, indicating a device at the aggregation layer. Acc is short for Access, indicating an access device.

## Slide 17: Basic Service Design: VLAN Design
You are advised to assign consecutive VLAN IDs to ensure proper use of VLAN resources.
VLANs can be classified into service VLANs, management VLANs, and interconnection VLANs as required.
Typically, VLANs are assigned based on interfaces.
Service VLAN design
Management VLAN design
VLAN assignment by geographic area
VLAN assignment by logical area
VLAN assignment by personnel structure
VLAN assignment by service type
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
In most cases, Layer 2 switches use VLANIF interface addresses as management addresses. It is recommended that all switches on the same Layer 2 network use the same management VLAN and their management IP addresses be on the same network segment.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 18: VLAN Planning
A management VLAN is reserved for Layer 2 devices.
VLANs are classified into the guest VLAN, R&D department VLAN, marketing department VLAN, and administrative department VLAN.
Layer 3 switches need to be connected to routers through VLANIF interfaces. Therefore, interconnection VLANs need to be reserved.
A VLAN is established for CAPWAP tunnels between APs and ACs.
VLAN ID | VLAN Description
1 | Guest VLAN or WLAN service VLAN
2 | R&D department VLAN
3 | Marketing department VLAN
4 | Administrative department VLAN
100 | Management VLAN of Layer 2 devices
101 | Management VLAN of WLAN services
102 | Interconnection VLAN between Agg-S1 and CORE-R1
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 19: Basic Service Design: IP Address Design
Management IP address
Layer 2 devices use VLANIF interface IP addresses as the management IP addresses. It is recommended that all Layer 2 switches connected to a gateway use on the same network segment.
IP address for network device interconnection
It is recommended that the interconnection IP addresses use a 30-bit mask, and core devices use smaller host IP addresses.
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
Service IP address
The service IP addresses are the IP addresses of servers, hosts, or gateways.
It is recommended that the gateway IP addresses use the same rightmost digits, such as .254.
The IP address ranges of different services must be clearly distinguished. The IP addresses of each type of service terminals must be continuous and can be aggregated.
An IP address segment with a 24-bit mask is recommended.
Employee
192.168.1.0/24
Partner
192.168.5.0/24
Guest
192.168.100.0/24
192.168.1.254
192.168.5.254
192.168.100.254
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 20: IP Address Planning
Reserve sufficient IP addresses based on the number of clients to be accessed and plan network segments and gateway addresses for each type of service.
Plan network segments for management IP addresses.
Divide network segments for interconnection IP addresses.
IP Network Segment/Mask | Gateway Address | Network Segment Description
192.168.1.0/24 | 192.168.1.254 | Network segment to which wireless access guests belong, with the gateway located on Agg-S1
192.168.2.0/24 | 192.168.2.254 | Network segment to which the R&D department belongs, with the gateway located on Agg-S1
192.168.3.0/24 | 192.168.3.254 | Network segment to which the marketing department belongs, with the gateway located on Agg-S1
192.168.4.0/24 | 192.168.4.254 | Network segment to which the administrative department belongs, with the gateway located on Agg-S1
192.168.100.0/24 | 192.168.100.254 | Management network segment of Layer 2 devices, with the gateway located on Agg-S1
192.168.101.0/24 | N/A | Management network segment of WLAN services
192.168.102.0/30 | N/A | Network segment between Agg-S1 and CORE-R1
1.1.1.1/32 | N/A | Loopback interface address on CORE-R1, which is used as the management IP address
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 21: Basic Service Design: IP Address Allocation Mode Design
Egress gateway
Internet
Carrier device
Egress gateway
WAN interface: static IP address, DHCP, or PPPoE
IP addresses of WAN interfaces are assigned by the carrier in static, DHCP, or PPPoE mode. The IP addresses of the egress gateways need to be obtained from the carrier in advance.
Devices such as servers and printers
It is recommended that servers and special terminals (such as punch-card machines, printing servers, and IP video surveillance devices) use statically bound IP addresses.
End users
Internet
AP
Egress gateway
It is recommended that IP addresses of end users are allocated by gateways through DHCP.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization
Notes: Dynamic IP address assignment or static IP address binding can be used for IP address assignment. On a small or midsize campus network, IP addresses are assigned based on the following principles:
IP addresses of WAN interfaces on egress gateways are assigned by the carrier in static, DHCP, or PPPoE mode. The IP addresses of the egress gateways need to be obtained from the carrier in advance.
It is recommended that servers and special terminals (such as punch-card machines, printing servers, and IP video surveillance devices) use statically bound IP addresses.
User terminal: It is recommended that the DHCP server be deployed on the gateway to dynamically assign IP addresses to user terminals such as PCs and IP phones using DHCP.

## Slide 22: IP Address Allocation Mode Planning
The egress gateway obtains an IP address through PPPoE.
All terminals obtain IP addresses through DHCP. The servers and printers are assigned fixed IP addresses.
IP addresses of all network devices (except APs) are statically configured.
IP Network Segment/Interface | Allocation Mode | Allocation Mode Description
192.168.1.0/24 192.168.2.0/24 192.168.3.0/24 192.168.4.0/24 | DHCP | Allocated by Agg-S1. Agg-S1 allocates fixed IP addresses to fixed devices such as servers and printers.
192.168.100.0/24 | Static | Device management IP addresses, which are statically configured
192.168.101.0/24 | DHCP | IP addresses of ACs are statically configured, and IP addresses of APs are allocated by Agg-S1.
192.168.102.0/30 | Static | Interconnection IP address, which is statically configured
GE0/0/0 on CORE-R1 | PPPoE | IP address assigned by the carrier
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 23: Basic Service Design: Routing Design
Routing design inside a campus network:
  Intra-network segment: After an IP address is allocated using DHCP, a default route is generated by default and Agg-S1 functions as a Layer 3 gateway.
  Inter-network segment: The current network topology is simple. You can deploy static routes on all devices that need to forward Layer 3 data to meet the requirements. No complex routing protocol needs to be deployed.
Routing design at the campus egress: Configure static default routes.
Internet
Administrative department
Marketing department
Printer
R&D department
FTP server
Printer
Guest reception center
Administrator
Printer
Layer 3 network
Layer 2 network
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization
Notes: The routing design of a small or midsize campus network includes design of internal routes and the routes between the campus egress and the Internet or WAN devices.
The internal routing design of a small or midsize campus network must meet the communication requirements of devices and terminals on the campus network and enable interaction with external routes. As the campus network is small in size, the network structure is simple.
  AP: After an IP address is assigned through DHCP, a default route is generated by default.
  Switch and gateway: Static routes can be used to meet requirements. No complex routing protocol needs to be deployed.
The egress routing design meets the requirements of intranet users for accessing the Internet and WAN. When the egress device is connected to the Internet or WAN, you are advised to configure static routes on the egress device.

## Slide 24: WLAN Design
WLAN networking design
WLAN data forwarding design
Based on the IP addresses of the AC and APs and whether data traffic passes through the AC, the networking can be divided into:
  Inline Layer 2 networking
  Bypass Layer 2 networking
  Inline Layer 3 networking
  Bypass Layer 3 networking
This example uses the bypass Layer 2 networking.
Network
192.168.101.1/24
192.168.101.X/24
192.168.101.Y/24
DHCP server
Control packets and data packets are transmitted on a WLAN.
  Control packets are forwarded through CAPWAP tunnels.
  User data packets are forwarded in tunnel or direct mode.
This example uses the direct forwarding mode.
CAPWAP tunnel
Network
User data
Control data
AC
AC
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization
Notes: In addition to planning the networking and data forwarding mode, you also need to perform the following operations:
  Network coverage design: You need to design and plan areas covered by Wi-Fi signals to ensure that the signal strength in each area meets user requirements and to minimize co-channel interference between neighboring APs.
  Network capacity design: You need to design the number of APs required based on the bandwidth requirements, number of terminals, user concurrency rate, and per-AP performance. This ensures that the WLAN performance can meet the Internet access requirements of all terminals.
  AP deployment design: Based on the network coverage design, modify and confirm the actual AP deployment position, deployment mode, and power supply cabling principles based on the actual situation.
  In addition, WLAN security design and roaming design are required.

## Slide 25: WLAN Data Plan
Item | Value
Management VLAN for APs | VLAN 101
Service VLAN for STAs | VLAN 1
DHCP server | Agg-S1 functions as a DHCP server to allocate IP addresses to APs and STAs. The default gateway address of STAs is 192.168.1.254.
IP address pool for APs | 192.168.101.2 to 192.168.101.253/24
IP address pool for STAs | 192.168.1.1 to 192.168.1.253/24
Source interface address of the AC | VLANIF 101: 192.168.101.1/24
AP group | Name: ap-group1 Referenced profiles: VAP profile WLAN-Guest and regulatory domain profile default
Regulatory domain profile | Name: default Country code: CN
SSID profile | Name: WLAN-Guest SSID name: WLAN-Guest
Security profile | Name: WLAN-Guest Security policy: WPA-WPA2+PSK+AES Password: WLAN@Guest123
VAP profile | Name: WLAN-Guest Forwarding mode: direct forwarding Service VLAN: VLAN 1 Referenced profiles: SSID profile WLAN-Guest and security profile WLAN-Guest
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 26: Reliability Design
Internet
Administrative department
Marketing department
Printer
R&D department
FTP server
Printer
Guest reception center
Administrator
Printer
Port-level reliability:
  Eth-Trunk is used to improve reliability between access switches and aggregation switches and increase link bandwidth.
Device-level reliability
  iStack or cluster switch system (CSS) technology can be used, which is not involved in this networking.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 27: Layer 2 Loop Prevention
Misconnection
Question: Although no redundant link is introduced to the current network segment, how can we prevent Layer 2 network loops caused by misoperations of office personnel?
Suggestion: Use spanning tree technology on the Layer 2 network to prevent loops. In addition, you are advised to manually configure Agg-S1 as the root bridge.
Internet
Administrative department
Marketing department
Printer
R&D department
FTP server
Printer
Guest reception center
Administrator
Printer
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 28: Egress NAT Design
1.2.3.4
Network egress
NAT mapping table
------------------------------------------------
Private IP Address | Public IP Address
192.168.1.1 | 1.2.3.1
192.168.1.2 | 1.2.3.2
Network egress
NAT address pool
-----------------------------------
1.2.3.1 | Not in use
1.2.3.2 | Not in use
1.3.3.3 | Not in use
Static NAT
Dynamic NAT
NAT mapping table
------------------------------------------------
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.10:80 | 1.2.3.4:10335
NAPT and Easy IP
Static NAT applies to scenarios where a large number of static IP addresses are configured and clients need to use fixed IP addresses.
NAT Server
Network egress
NAT mapping table
------------------------------------------------
Private IP Address:Port Number | Public IP Address:Port Number
192.168.1.1:10321 | 1.2.3.4:1025
192.168.1.2:17087 | 1.2.3.4:1026
The NAT server applies to scenarios where a server on the intranet needs to externally provide services.
Dynamic NAT introduces the address pool concept. Available IP addresses in the address pool are allocated to clients for Internet access.
NAPT translates port numbers based on dynamic NAT to improve public address usage.
Easy IP applies to scenarios where IP addresses of outbound network interfaces are dynamically allocated.
Server providing services externally
Network egress
1.2.3.4
1.2.3.4
1.2.3.4
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 29: Security Design
LAN
Traffic Control
Administrative department
Marketing department
R&D department
Internet
Guest network
Internal network
Internal traffic
Guest data
Different departments can access each other but cannot access the Internet.
Guests can access the Internet but cannot access the internal network.
You can use technologies such as traffic policing and traffic filtering to isolate the internal network from the external network and use NAT to control the internal network's access to the Internet.
DHCP Security
On a campus network, employees often connect unauthorized DHCP-enabled wireless routers to the network, causing private address disorders, address conflicts, and Internet access failures.
In most cases, DHCP snooping is enabled on access switches to prevent this issue.
DHCP-enabled home router
Network Management Security
When network devices are managed through Telnet or the web system, you can use access control list (ACL) technology to allow only users with fixed IP addresses to log in to the devices.
For the centralized NMS, SNMPv3 supports identity authentication and encryption, significantly enhancing the NMS security.
Access switch
DHCP server
Trusted port
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization
Notes: Note: Security design in this case is implemented depending only on routers or switches.

## Slide 30: Network O&M and Management Design
Traditional Device Management
When the network administrator and devices' IP addresses are routable to each other, you can manage the devices through Telnet, the web system, or SSH.
When there are a large number of devices on a network, you can deploy an SNMP-based unified NMS for network O&M and management.
SNMP
WEB
SSH/Telnet
Management Based on iMaster NCE
NETCONF
OpenFlow
Telemetry
In addition to the SNMP-based traditional NMS, Huawei iMaster NCE can also be used for network management and O&M to implement autonomous network driving.
LAN
Network
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 31: Small Campus Network Deployment and Implementation
The project deployment and implementation process must include:
  Solution formulation
  Device installation
  Network commissioning
  Network migration and integration
  Transfer-to-maintenance (ETM) training
  Project acceptance
The specific process is determined based on the actual situation.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 32: Configuration Scheme (1)
Connect network devices using physical cables, configure link aggregation, and add interface description. For details, see the following two tables.
Device | Interface | Configuration
Acc-S1 | Eth-trunk 1 | Mode: LACP-static Trunkport: GE0/0/1, GE0/0/2, GE0/0/3 Description: to Agg-S1's eth-trunk 1
 | E0/0/10 | Description: to AP1
 | E0/0/11 | Description: to AP2
Acc-S2 | Eth-trunk 1 | Mode: LACP-static Trunkport: GE0/0/1, GE0/0/2, GE0/0/3 Description: to Agg-S1's eth-trunk 2
Acc-S3 | Eth-trunk 1 | Mode: LACP-static Trunkport: GE0/0/1, GE0/0/2, GE0/0/3 Description: to Agg-S1's eth-trunk 3
Acc-S4 | Eth-trunk 1 | Mode: LACP-static Trunkport: GE0/0/1, GE0/0/2, GE0/0/3 Description: to Agg-S1's eth-trunk 4
AC1 | GE0/0/1 | Description: to Agg-S1's GE0/0/2
CORE-R1 | GE0/0/1 | Description: to Agg-S1's GE0/0/1
Device | Interface | Configuration
Agg-S1 | Eth-trunk 1 | Mode: LACP-static Trunkport: GE0/0/3, GE0/0/7, GE0/0/8 Description: to Acc-S1's eth-trunk 1
 | Eth-trunk 2 | Mode: LACP-static Trunkport: GE0/0/4, GE0/0/9, GE0/0/10 Description: to Acc-S2's eth-trunk 1
 | Eth-trunk 3 | Mode: LACP-static Trunkport: GE0/0/5, GE0/0/11, GE0/0/12 Description: to Acc-S3's eth-trunk 1
 | Eth-trunk 4 | Mode: LACP-static Trunkport: GE0/0/6, GE0/0/13, GE0/0/14 Description: to Acc-S4's eth-trunk 1
 | GE0/0/1 | Description: to CORE-R1's GE0/0/1
 | GE0/0/2 | Description: to AC1's GE0/0/1
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 33: Configuration Scheme (2)
Assign VLANs based on interfaces. For details, see the following two tables.
Device | Interface | Type | Configuration
Acc-S1 | Eth-trunk 1 | Trunk | PVID:100 Allow-pass VLAN 1, 100, 101
 | E0/0/10 |  | PVID:101 Allow-pass VLAN 1, 101
 | E0/0/11 |  | 
Acc-S2 | Eth-trunk 1 | Trunk | PVID:100 Allow pass VLAN 2, 100
 | Other ports | Access | Default VLAN 2
Acc-S3 | Eth-trunk 1 | Trunk | PVID:100 Allow pass VLAN 3, 100
 | Other ports | Access | Default VLAN 3
Acc-S4 | Eth-trunk 1 | Trunk | PVID:100 Allow pass VLAN 4, 100
 | Other ports | Access | Default VLAN 4
Device | Interface | Type | Configuration
Agg-S1 | Eth-trunk 1 | Trunk | PVID:100 Allow-pass VLAN 1, 100, 101
 | Eth-trunk 2 | Trunk | PVID:100 Allow pass VLAN 2, 100
 | Eth-trunk 3 | Trunk | PVID:100 Allow pass VLAN 3, 100
 | Eth-trunk 4 | Trunk | PVID:100 Allow pass VLAN 4, 100
 | GE0/0/2 | Access | Default VLAN 101
 | GE0/0/1 | Access | Default VLAN 102
AC1 | GE0/0/1 | Access | Default VLAN 101
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 34: Configuration Scheme (3)
Allocate IP addresses to STAs and APs using DHCP and statically configure IP addresses for network devices. For details, see the following two tables.
Device | Interface | Address/Mask
Agg-S1 | VLANIF 1 | 192.168.1.254/24
 | VLANIF 2 | 192.168.2.254/24
 | VLANIF 3 | 192.168.3.254/24
 | VLANIF 4 | 192.168.4.254/24
 | VLANIF 100 | 192.168.100.254/24
 | VLANIF 101 | 192.168.101.254/24
 | VLANIF 102 | 192.168.102.2/30
CORE-R1 | GE0/0/1 | 192.168.102.1/30
 | GE0/0/0 | Automatic obtaining via PPPoE
 | Loopback0 | 1.1.1.1/32
Device | Interface | Address/Mask
Acc-S1 | VLANIF 100 | 192.168.100.1/24
Acc-S2 | VLANIF 100 | 192.168.100.2/24
Acc-S3 | VLANIF 100 | 192.168.100.3/24
Acc-S4 | VLANIF 100 | 192.168.100.4/24
AC1 | VLANIF 101 | 192.168.1.101/24
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 35: Configuration Scheme (4)
Configure the IP address allocation mode. For details about DHCP, see the following table.
Network Segment | Other Parameters | Remarks
192.168.1.0/24 | Gateway:192.168.1.254 DNS:192.168.1.254 | Agg-S1 functions as a DHCP server.
192.168.2.0/24 | Gateway:192.168.2.254 DNS:192.168.2.254 | Agg-S1 functions as a DHCP server. Fixed IP addresses are allocated to printer (1) and the FTP server.
192.168.3.0/24 | Gateway:192.168.3.254 DNS:192.168.3.254 | Agg-S1 functions as a DHCP server. A fixed IP address is allocated to printer (2).
192.168.3.0/24 | Gateway:192.168.4.254 DNS:192.168.4.254 | Agg-S1 functions as a DHCP server. Fixed IP addresses are allocated to printer (3) and the network administrator.
192.168.101.0/24 | N/A | Agg-S1 functions as a DHCP server. The IP address (192.168.101.1) occupied by the AC is not allocated.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 36: Configuration Scheme (5)
Configure routes. Static routes are used because the network scale is small and the number of NEs is also small. For details, see the following table.
Device | Route Configuration | Remarks
Acc-S1 | 0.0.0.0 0 192.168.100.254 | Route that enables the network administrator to access Layer 2 switches across network segments.
Acc-S2 |  | 
Acc-S3 |  | 
Acc-S4 |  | 
AC1 | 0.0.0.0 0 192.168.101.254 | Route that enables the administrator to access AC1 across network segments.
Agg-S1 | 0.0.0.0 0 192.168.102.1 | Route that matches the traffic destined for the Internet
CORE-R1 | 192.168.0.0 20 192.168.102.2 | Aggregated route for the core router to access the intranet
 | Default route | Route pointing to an interface on the external network
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 37: Configuration Scheme (6)
Configure network management. Set the network management mode to Telnet-based remote management and authentication mode to Authentication, Authorization, and Accounting (AAA). For details, see the following table.
Device | Management Mode | Authentication Mode | Remarks
Acc-S1 | Telnet | AAA | The user name and password must be complex and different. In addition, record them.
Acc-S2 |  |  | 
Acc-S3 |  |  | 
Acc-S4 |  |  | 
Agg-S1 |  |  | 
CORE-R1 |  |  | 
AC1 |  |  | 
AP1&AP2 | Centralized control and management by the AC | N/A | N/A
Network egress configuration
Device | Interface | Access Mode | NAT Mode | Remarks
CORE-R1 | GE0/0/0 | PPPoE | Easy IP | User name: PPPoEUser123 Password: Huawei@123
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 38: Configuration Scheme (7)
Configure the WLAN as planned.
Perform security-related configurations. For details, see the following table.
Module | Related Technology | Configuration
Traffic monitoring | Traffic policy, NAT, and ACL | Configure an advanced ACL to block the traffic from 192.168.1.0/24 to the service network segment on the intranet and allow other traffic to pass through. Configure a traffic filtering policy to reference this ACL and apply the policy to an interface. Configure a basic ACL to permit only the traffic from 192.168.1.0/24 and apply this ACL to the NAT configuration on an outbound network interface.
Network management security | AAA and ACL | Configure a basic ACL to permit only the packets whose source IP address is the administrator's IP address and wildcard mask is 0, and apply the ACL to the VTY interfaces of all managed devices.
DHCP security | DHCP snooping | Enable DHCP snooping on all access switches and configure the uplink interfaces as trusted interfaces.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 39: Small Campus Network Commissioning
3. Service Performance Test
Service traffic test
Access control test
2. High Reliability Commissioning
Loop prevention function test
Path switchover test
Hot Standby (HSB) test
1. Connectivity Test
Basic link interconnection test
Layer 2 interoperability test
Layer 3 interoperability test
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 40: Small Campus Network O&M
After a small campus network is provisioned, it enters the O&M phase. Common O&M methods include:
  Device environment check
  Basic device information check
  Device running status check
  Service check
  Alarm handling
When the network scale reaches a certain level, the network management software can be used for network management and O&M to improve efficiency.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 41: Small Campus Network Optimization
Network optimization can comprehensively improve the reliability and robustness of networks and better support the development of enterprise services. Common network optimization solutions include but are not limited to:
  Device performance optimization, such as hardware upgrade and software version update
  Basic network optimization, such as network architecture optimization and routing protocol adjustment
  Service quality optimization, such as preferential forwarding of voice and video services
Formulate an appropriate network optimization solution based on network requirements and actual conditions.
Planning and Design
Deployment and Implementation
Network O&M
Network Optimization

## Slide 42
What is the complete lifecycle of a campus network?
What is the function of a management IP address?
Notes: Network planning and design, deployment and implementation, O&M, and optimization
IP address used by the network administrator to manage a device

## Slide 43
This chapter describes the concepts, types, and common technologies of campus networks.
Understand the lifecycle of campus networks:
  Planning and design
  Deployment and implementation
  Network O&M
  Network optimization
Based on the previous courses, this course focuses on the planning, design, deployment, and implementation of campus networks and details how to establish a small campus network.