## Slide 1
Zhang Linrui/zwx570554
2019.10.30
Li Xianzhi/00354681
New
Update
Update
Update
Update
Update

## Slide 2: Network Reference Model

## Slide 3
In the digital era, various information is presented as data in our life. What is data? How is data transmitted?
In this course, we will use the network reference model to understand the "life" of data.

## Slide 4
On completion of this course, you will be able to:
  Understand the data definition and transmission process.
  Understand the concepts and advantages of the network reference model.
  Understand common standard protocols.
  Understand the data encapsulation and decapsulation processes.

## Slide 5
Applications and Data
Network Reference Model and Standard Protocols
Data Communication Process

## Slide 6: Origin of the Story - Applications
Applications are used to meet various requirements of people, such as web page access, online gaming, and online video playback.
Information is generated along with applications. Texts, pictures, and videos are all information presentation modes.
Application
Information

## Slide 7: Application Implementation - Data
Data generation
  In the computer field, data is the carrier of all kinds of information.
Data transmission
  Data generated by most applications needs to be transmitted between devices.
Does an application need to complete the entire process from data generation to data transmission?
Data
Network
Notes: A computer can identify only digital data consisting of 0s and 1s. It is incapable of reading other types of information, so the information needs to be translated into data by certain rules.
However, people do not have the capability of reading electronic data. Therefore, data needs to be converted into information that can be understood by people.
A network engineer needs to pay more attention to the end-to-end data transmission process.

## Slide 8
Applications and Data
Network Reference Model and Standard Protocols
Data Communication Process

## Slide 9: OSI Reference Model
7. Application Layer | Provides interfaces for applications.
6. Presentation Layer | Translates data formats to ensure that the application-layer data of one system can be identified by the application layer of another system.
5. Session Layer | Establishes, manages, and terminates sessions between communicating parties.
4. Transport Layer | Establishes, maintains, and cancels an end-to-end data transmission process; controls transmission speeds and adjusts data sequences.
3. Network Layer | Defines logical addresses and transfers data from sources to destinations.
2. Data Link Layer | Encapsulates packets into frames, transmits frames in P2P or P2MP mode, and implements error checking.
1. Physical Layer | Transmits bitstreams over transmission media and defines electrical and physical specifications.
Notes: The Open Systems Interconnection Model (OSI) was included in the ISO 7489 standard and released in 1984. ISO stands for International Organization for Standardization.
The OSI reference model is also called the seven-layer model. The seven layers from bottom to top are as follows:
  Physical layer: transmits bit flows between devices and defines physical specifications such as electrical levels, speeds, and cable pins.
  Data link layer: encapsulates bits into octets and octets into frames, uses MAC addresses to access media, and implements error checking.
  Network layer: defines logical addresses for routers to determine paths and transmits data from source networks to destination networks.
  Transport layer: implements connection-oriented and non-connection-oriented data transmission, as well as error checking before retransmission.
  Session layer: establishes, manages, and terminates sessions between entities at the presentation layer. Communication at this layer is implemented through service requests and responses transmitted between applications on different devices.
  Presentation layer: provides data encoding and conversion so that data sent by the application layer of one system can be identified by the application layer of another system.
  Application layer: provides network services for applications and the OSI layer closest to end users.

## Slide 10: TCP/IP Reference Model
The OSI protocol stack is complex, and the TCP and IP protocols are widely used in the industry. Therefore, the TCP/IP reference model becomes the mainstream reference model of the Internet.
Application Layer
Host-to-Host Layer
Internet Layer
Network Access Layer
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Standard TCP/IP model
OSI model
Equivalent TCP/IP model
Notes: The TCP/IP model is similar to the OSI model in structure and adopts a hierarchical architecture. Adjacent TCP/IP layers are closely related.
The standard TCP/IP model combines the data link layer and physical layer in the OSI model into the network access layer. This division mode is contrary to the actual protocol formulation. Therefore, the equivalent TCP/IP model that integrates the TCP/IP standard model and the OSI model is proposed. Contents in the following slides are based on the equivalent TCP/IP model.

## Slide 11: Common TCP/IP Protocols
The TCP/IP protocol stack defines a series of standard protocols.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Telnet | FTP | TFTP | SNMP
HTTP | SMTP | DNS | DHCP
TCP | UDP
ICMP | IGMP
IP | 
PPPoE | 
Ethernet | PPP
...
Notes: Application Layer
  Hypertext Transfer Protocol (HTTP): is used to access various pages on web servers.
  File Transfer Protocol (FTP): provides a method for transferring files. It allows data to be transferred from one host to another.
  Domain name service (DNS): translates from host domain names to IP addresses.
Transport layer
  Transmission Control Protocol (TCP): provides reliable connection-oriented communication services for applications. Currently, TCP is used by many popular applications.
  User Datagram Protocol (UDP): provides connectionless communication and does not guarantee the reliability of packet transmission. The reliability can be ensured by the application layer.
Network layer
  Internet Protocol (IP): encapsulates transport-layer data into data packets and forwards packets from source sites to destination sites. IP provides a connectionless and unreliable service.
  Internet Group Management Protocol (IGMP): manages multicast group memberships. Specifically, IGMP sets up and maintains memberships between IP hosts and their directly connected multicast routers.
  Internet Control Message Protocol (ICMP): sends control messages based on the IP protocol and provides information about various problems that may exist in the communication environment. Such information helps administrators diagnose problems and take proper measures to resolve the problems.

## Slide 12
Notes: Data link layer
  Point-to-Point Protocol (PPP): is a data link layer protocol that works in point-to-point mode. PPP is mainly used on wide area networks (WANs).
  Ethernet: is a multi-access and broadcast protocol at the data link layer, which is the most widely used local area network (LAN) technology.
  Point-to-Point Protocol over Ethernet (PPPoE): connects multiple hosts on a network to a remote access concentrator through a simple bridge device (access device). Common applications include home broadband dialup access.

## Slide 13: Common Protocol Standardization Organizations
Internet Engineering Task Force (IETF)
  IETF is a voluntary organization responsible for developing and promoting Internet protocols (especially protocols that constitute the TCP/IP protocol suite), and releasing new or replacing old protocol standards through RFCs.
Institute of Electrical and Electronics Engineers (IEEE)
  IEEE has formulated about 30% of standards in the electronics, electrical, and computer science fields worldwide. Those standards include well-known IEEE802.3 (Ethernet) and IEEE802.11 (Wi-Fi).
International Organization for Standardization (ISO)
  ISO is an international organization that plays an important role in the formulation of computer network standards, such as the OSI model defined in ISO/IEC 7498-1.

## Slide 14: Application Layer
The application layer provides interfaces for application software so that applications can use network services. The application layer protocol designates transport layer protocols and ports.
PDUs transmitted at the network layer are called data.
Application Layer (Data)
Transport Layer
Network Layer
Data Link Layer
Physical Layer
HTTP 80 (TCP) Hypertext transfer protocol, which provides web browsing services.
Telnet 23 (TCP) Remote login protocol, which provides remote management services.
FTP 20 and 21 (TCP) File transfer protocol, which provides Internet file resource sharing services.
SMTP 25 (TCP) Simple mail transfer protocol, which provides Internet email services.
TFTP 69 (UDP) Simple file transfer protocol, which provides simple file transfer services.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: The TCP/IP suite enables data to be transmitted over a network. The layers use packet data units (PDUs) to exchange data, implementing communication between network devices.
PDUs transmitted at different layers contain different information. Therefore, PDUs have different names at different layers.

## Slide 15: Common Application Layer Protocols - FTP
The File Transfer Protocol (FTP) transfers files from one host to another to implement file download and upload. This protocol adopts the client/server (C/S) structure.
FTP client
FTP server
FTP server: a device that runs the FTP service. It provides the access and operation functions for remote clients, allowing users to access the FTP server through the FTP client program and access files on the server.
FTP client: provides commands for local users to operate files on a remote server. A user can install an FTP client program on a PC and set up a connection with an FTP server to operate files on the server.
Network
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 16: Common Application Layer Protocols - Telnet
Telnet is a standard protocol that provides remote login services on a network. It provides users with the ability to operate remote devices through local PCs.
A user connects to a Telnet server through the Telnet client program. The commands entered on the Telnet client are executed on the server, as if the commands were entered on the console of the server.
Telnet client
AP
Router
SW
Firewall
Server
...
Telnet server
Network
Telnet connection
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 17: Common Application Layer Protocols - HTTP
Hypertext Transfer Protocol (HTTP): is one of the most widely used network protocols on the Internet. HTTP was originally designed to provide a method for publishing and receiving HTML pages.
HTTP client
HTTP server
Visits www.huawei.com.
Returns the HTML file of the page.
Network
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 18: Transport Layer
A transport layer protocol receives data from an application layer protocol, encapsulates the data with the corresponding transport layer protocol header, and helps establish an end-to-end (port-to-port) connection.
PDUs transmitted at the transport layer are called segments.
Transport layer protocols:
  TCP: a connection-oriented reliable protocol defined by IETF in RFC 793.
  UDP: a simple connectionless protocol defined by IETF in RFC 768.
Application Layer
Transport Layer (Segment)
Network Layer
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 19: TCP and UDP - Header Formats
TCP header
20 bytes
UDP header
8 bytes
Source Port (16) |  |  | Destination Port (16)
Sequence Number (32) |  |  | 
Acknowledgement Number (32) |  |  | 
Header Length (4) | Reserved (6) | Control Bits (6) | Window (16)
Checksum (16) |  |  | Urgent (16)
Options |  |  | 
Data (varies) |  |  | 
Source Port (16) | Destination Port (16)
Length (16) | Checksum (16)
Data (if any) | 
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: TCP header:
  Source Port: identifies the application that sends the segment. This field is 16 bits long.
  Destination Port: identifies the application that receives the segment. This field is 16 bits long.
  Sequence Number: Every byte of data sent over a TCP connection has a sequence number. The value of the Sequence Number field equals the sequence number of the first byte in a sent segment. This field is 32 bits long.
  Acknowledgment Number: indicates the sequence number of the next segment's first byte that the receiver is expecting to receive. The value of this field is 1 plus the sequence number of the last byte in the previous segment that is successfully received. This field is valid only when the ACK flag is set. This field is 32 bits long.
  Header Length: indicates the length of the TCP header. The unit is 32 bits (4 bytes). If there is no option content, the value of this field is 5, indicating that the header contains 20 bytes.
  Reserved: This field is reserved and must be set to 0. This field is 6 bits long.
  Control Bits: control bits, includes FIN, ACK, and SYN flags, indicating TCP data segments in different states.
  Window: used for TCP flow control. The value is the maximum number of bytes that are allowed by the receiver. The maximum window size is 65535 bytes. This field is 16 bits long.
  Checksum: a mandatory field. It is calculated and stored by the sender and verified by the receiver. During checksum computation, the TCP header and TCP data are included, and a 12-byte pseudo header is added before the TCP segment. This field is 16 bits long.

## Slide 20
Notes:   Urgent: indicates the urgent pointer. The urgent pointer is valid only when the URG flag is set. The Urgent field indicates that the sender transmits data in emergency mode. The urgent pointer indicates the number of urgent data bytes in a segment (urgent data is placed at the beginning of the segment). This field is 16 bits long.
  Options: This field is optional. This field is 0 to 40 bytes long.
UDP header:
  Source Port: identifies the application that sends the segment. This field is 16 bits long.
  Destination Port: identifies the application that receives the segment. This field is 16 bits long.
  Length: specifies the total length of the UDP header and data. The possible minimum length is 8 bytes because the UDP header already occupies 8 bytes. Due to the existence of this field, the total length of a UDP segment does not exceed 65535 bytes (including an 8-byte header and 65527-byte data).
  Checksum: checksum of the UDP header and UDP data. This field is 16 bits long.

## Slide 21: TCP and UDP - Port Numbers
HTTP client
HTTP server
Network
TCP port 1024
TCP port 1231
HTTP application
Telnet
House number: 2.2.2.2 (IP address)
TCP port 80
TCP port 23
HTTP application
Telnet
Generally, the source port used by a client is randomly allocated, and the destination port is specified by the application of a server.
The system generally selects a source port number that is greater than 1023 and is not being used.
The destination port number is the listening port of the application (service) enabled on the server. For example, the default port number for HTTP is 80.
Web browser
HTTP server
HTTP
Payload
Source IP address: 1.1.1.1
Destination IP address: 2.2.2.2
Source port number: 1024
Destination port number: 80
IP header
TCP header
House number: 1.1.1.1 (IP address)
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 22: TCP Connection Setup - Three-Way Handshake
PC1
1.1.1.1:1024
PC2
2.2.2.2:23
Source = 1.1.1.1
Destination=2.2.2.2
Seq=a Ack=0
(Flags: SYN is set.)
Source = 2.2.2.2
Destination=1.1.1.1
Seq=b Ack=a+1
(Flags: SYN is set, and ACK is set.)
Source = 1.1.1.1
Destination=2.2.2.2
Seq=a+1 Ack=b+1
(Flags: ACK is set.)
IP header
TCP header
Before sending data, a TCP-based application needs to establish a connection through three-way handshake.
A TCP connection is established.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: The TCP connection setup process is as follows:
  The TCP connection initiator (PC1 in the figure) sends the first TCP segment with SYN being set. The initial sequence number a is a randomly generated number. The acknowledgment number is 0 because no segment has ever been received from PC2.
  After receiving a valid TCP segment with the SYN flag being set, the receiver (PC2) replies with a TCP segment with SYN and ACK being set. The initial sequence number b is a randomly generated number. Because the segment is a response one to PC1, the acknowledgment number is a+1.
  After receiving the TCP segment in which SYN and ACK are set, PC1 replies with a segment in which ACK is set, the sequence number is a+1, and the acknowledgment number is b+1. After PC2 receives the segment, a TCP connection is established.

## Slide 23: TCP Sequence Number and Acknowledgment Number
TCP uses the Sequence Number and Acknowledgment Number fields to implement reliable and ordered data transmission.
PC1
1.1.1.1:1024
PC2
2.2.2.2:23
Source = 2.2.2.2
Destination = 1.1.1.1
Seq=b+1
Ack=a+1+12
Payload
Length =0 bytes
Source = 1.1.1.1
Destination = 2.2.2.2
Seq=a+13
Ack=b+1
Payload
Length = 66 bytes
Source = 2.2.2.2
Destination = 1.1.1.1
Seq=b+1
Ack=a+12+66
Payload
Length = 0 bytes
Source = 1.1.1.1
Destination = 2.2.2.2
Seq=a+1
Ack=b+1
Payload
Length = 12 bytes
IP header
TCP header
Question: Why does the value of the Acknowledgment Number field in the segment sent by PC1 not increase?
Data to be sent
1
2
3
4
5
6
……
A TCP connection is established.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: Assume that PC1 needs to send segments of data to PC2. The transmission process is as follows:
  PC1 numbers each byte to be sent by TCP. Assume that the number of the first byte is a+1. Then, the number of the second byte is a+2, the number of the third byte is a+3, and so on.
  PC1 uses the number of the first byte of each segment of data as the sequence number and sends out the TCP segment.
  After receiving the TCP segment from PC1, PC2 needs to acknowledge the segment and request the next segment of data. How is the next segment of data determined? Sequence number (a+1) + Payload length = Sequence number of the first byte of the next segment (a+1+12)
  After receiving the TCP segment sent by PC2, PC1 finds that the acknowledgment number is a+1+12, indicating that the segments from a+1 to a+12 have been received and the sequence number of the upcoming segment to be sent should be a+1+12.
To improve the sending efficiency, multiple segments of data can be sent at a time by the sender and then acknowledged at a time by the receiver.

## Slide 24: TCP Window Sliding Mechanism
TCP uses the sliding window mechanism to control the data transmission rate.
seq=100 win=3 flags=SYN
seq=200 Ack=101 win=3 flags=SYN,ACK
Buffer of the receiver
seq=101 Ack=201 win=3 flags=ACK
seq=101 win=3
seq=102 win=3
seq=103 win=3
Ack=104 win=1 ctl=ACK
seq=104 win=3
Three-way handshake
Data transmission
PC1
PC2
Question: Why does the Window field of the segment sent by PC1 remain unchanged?
Data to be sent
1
2
3
4
5
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: During the TCP three-way handshake, both ends notify each other of the maximum number of bytes (buffer size) that can be received by the local end through the Window field.
After the TCP connection is set up, the sender sends data of the specified number of bytes based on the window size declared by the receiver.
After receiving the data, the receiver stores the data in the buffer and waits for the upper-layer application to obtain the buffered data. After the data is obtained by the upper-layer application, the corresponding buffer space is released.
The receiver notifies the current acceptable data size (window) according to its buffer size.
The sender sends a certain amount of data based on the current window size of the receiver.

## Slide 25: TCP Shutdown - Four-Way Handshake
After data transmission is complete, TCP needs to use the four-way handshake mechanism to disconnect the TCP connection and release system resources.
PC1
1.1.1.1:1024
PC2
2.2.2.2:23
Source = 1.1.1.1
Destination = 2.2.2.2
Seq=101 Ack=301
(Flags: FIN is set, and ACK is set.)
IP header
TCP header
Sends a connection teardown request with FIN being set.
Source = 2.2.2.2
Destination = 1.1.1.1
Seq=301 Ack=102
(Flags: ACK is set.)
Sends ACK.
Source = 2.2.2.2
Destination = 1.1.1.1
Seq=301 Ack=102
(Flags: FIN is set, and ACK is set.)
Sends a connection teardown request with FIN being set.
Source = 1.1.1.1
Destination = 2.2.2.2
Seq=102 Ack=302
(Flags: ACK is set.)
Sends ACK.
A TCP connection is established.
TCP segment exchange
The TCP connection is torn down.
1
2
3
4
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: TCP supports data transmission in full-duplex mode, which means that data can be transmitted in both directions at the same time. Before data is transmitted, TCP sets up a connection in both directions through three-way handshake. Therefore, after data transmission is complete, the connection must be closed in both directions. This is shown in the figure.
  PC1 sends a TCP segment with FIN being set. The segment does not carry data.
  After receiving the TCP segment from PC1, PC2 replies with a TCP segment with ACK being set.
  PC2 checks whether data needs to be sent. If so, PC2 sends the data, and then a TCP segment with FIN being set to close the connection. Otherwise, PC2 directly sends a TCP segment with FIN being set.
  After receiving the TCP segment with FIN being set, PC1 replies with an ACK segment. The TCP connection is then torn down in both directions.

## Slide 26: Network Layer
The transport layer is responsible for establishing connections between processes on hosts, and the network layer is responsible for transmitting data from one host to another.
PDUs transmitted at the network layer are called packets.
The network layer is also called the Internet layer.
    It sends packets from source hosts to destination hosts.
Functions of the network layer:
    Provides logical addresses for network devices.
    Routes and forwards data packets.
    Common network layer protocols include IPv4, IPv6, ICMP, and IGMP.
Application Layer
Transport Layer
Network Layer (Packet)
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: Internet Protocol Version 4 (IPv4) is the most widely used network layer protocol.

## Slide 27: Working Process of a Network Layer Protocol
Packet Encapsulation
Packet Forwarding Based on Network Layer Addresses
PC1
PC2
The PC encapsulates the IP header (envelope).
The key information is about source and destination IP addresses.
The network layer header of a packet sent by a source device carries the network layer addresses of the source and destination devices.
Each network device (such as a router) that has the routing function maintains a routing table (like a map of the network device).
After receiving a packet, the network device reads the network layer destination address of the packet, searches the routing table for the matching entry of the destination address, and forwards the packet according to the instruction of the matching entry.
Router 1
G0/0/0
G0/0/1
Network A
Routing table of Router 1 | 
Network | Outbound Interface
Network A | G0/0/1
… | …
… | …
Letter: data sent by an upper layer (for example, the transport layer)
Envelope: IP packet header
Sender: source IP address
Receiver: destination IP address
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: When IP is used as the network layer protocol, both communication parties are assigned a unique IP address to identify themselves. An IP address can be written as a 32-bit binary integer. To facilitate reading and analysis, an IP address is usually represented in dot-decimal notation, consisting of four decimal numbers, each ranging from 0 to 255, separated by dots, such as, 192.168.1.1.
Encapsulation and forwarding of IP data packets:
  When receiving data from an upper layer (such as the transport layer), the network layer encapsulates an IP packet header and adds the source and destination IP addresses to the header.
  Each intermediate network device (such as a router) maintains a routing table that guides IP packet forwarding like a map. After receiving a packet, the intermediate network device reads the destination address of the packet, searches the local routing table for a matching entry, and forwards the IP packet according to the instruction of the matching entry.
  When the IP packet reaches the destination host, the destination host determines whether to accept the packet based on the destination IP address and then processes the packet accordingly.
When the IP protocol is running, routing protocols such as OSPF, IS-IS, and BGP are required to help routers build routing tables, and ICMP is required to help control networks and diagnose network status.

## Slide 28: Data Link Layer
The data link layer is located between the network layer and the physical layer and provides services for protocols such as IP and IPv6 at the network layer. PDUs transmitted at the data link layer are called frames.
Ethernet is the most common data link layer protocol.
The data link layer is located between the network layer and the physical layer.
  The data link layer provides intra-segment communication for the network layer.
  The functions of the data link layer include framing, physical addressing, and error control.
  Common data link layer protocols include Ethernet, PPPoE, and PPP.
Application Layer
Transport Layer
Network Layer
Data Link Layer (Frame)
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 29: Ethernet and Source MAC Addresses
Name: Host A
MAC address/Ethernet address/physical address:
Ethernet Definition
Host A
Host B
Host C
Host D
Switch A
Switch B
Network A
Ethernet is a broadcast multiple access protocol that works at the data link layer protocol.
The network interfaces of PCs comply with the Ethernet standard.
Generally, a broadcast domain corresponds to an IP network segment.
Ethernet Source MAC Addresses
Host A
A media access control (MAC) address uniquely identifies a NIC on a network. Each NIC requires and has a unique MAC address.
MAC addresses are used to locate specific physical devices in an IP network segment.
A device that works at the data link layer, such as an Ethernet switch, maintains a MAC address table to guide data frame forwarding.
I have a MAC address when I leave the factory.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: A MAC address is recognizable as six groups of two hexadecimal digits, separated by hyphens, colons, or without a separator. Example: 48-A4-72-1C-8F-4F

## Slide 30: ARP
Address Resolution Protocol (ARP):
  Discovers the MAC address associated with a given IP address.
192.168.1.1/24
3C-52-82-49-7E-9D
192.168.1.2/24
48-A4-72-1C-8F-4F
Host A
Host B
ARP request
ARP reply
Destination IP address: 192.168.1.2
Destination MAC address: ?
Source IP address: 192.168.1.2
Source MAC address: 48-A4-72-1C-8F-4F
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: The Address Resolution Protocol (ARP) is a TCP/IP protocol that discovers the data link layer address associated with a given IP address.
ARP is an indispensable protocol in IPv4. It provides the following functions:
  Discovers the MAC address associated with a given IP address.
  Maintains and caches the mapping between IP addresses and MAC addresses through ARP entries.
  Detects duplicate IP addresses on a network segment.

## Slide 31: ARP Implementation Principles (1)
Host 1>arp -a
Internet Address Physical Address Type
GE 0/0/1
GE 0/0/2
Host 1
Host 2
IP 1: 192.168.1.1/24
MAC 1: 3C-52-82-49-7E-9D
IP 2:192.168.1.2/24
MAC 2: 48-A4-72-1C-8F-4F
Step 1:
Before sending a datagram, a device searches its ARP table for the destination MAC address of the datagram.
If the destination MAC address exists in the ARP table, the device encapsulates the MAC address in the frame and sends out the frame. If the destination MAC address does not exist in the ARP table, the device sends an ARP request to discover the MAC address.
GE 0/0/3
Host 1 checks cached ARP entries.
Host 1 sends an ARP request.
Host 2 adds an ARP entry.
Host 2 sends an ARP reply.
Host 1 adds an ARP entry.
The ARP cache table is empty.
1
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: Generally, a network device has an ARP cache. The ARP cache stores the mapping between IP addresses and MAC addresses.
Before sending a datagram, a device searches its ARP table. If a matching ARP entry is found, the device encapsulates the corresponding MAC address in the frame and sends out the frame. If a matching ARP entry is not found, the device sends an ARP request to discover the MAC address.
The learned mapping between the IP address and MAC address is stored in the ARP table for a period. Within the validity period (180s by default), the device can directly search this table for the destination MAC address for data encapsulation, without performing ARP-based query. After the validity period expires, the ARP entry is automatically deleted.
If the destination device is located on another network, the source device searches the ARP table for the gateway MAC address of the destination address and sends the datagram to the gateway. Then, the gateway forwards the datagram to the destination device.

## Slide 32: ARP Implementation Principles (2)
Step 3:
The ARP request message is a broadcast data frame. After receiving the ARP request message, the switch floods it.
GE 0/0/1
GE 0/0/2
GE 0/0/3
Host 1
Host 2
IP 1: 192.168.1.1/24
MAC 1: 3C-52-82-49-7E-9D
IP 2: 192.168.1.2/24
MAC 2:48-A4-72-1C-8F-4F
Eth_II | ARP Request | FCS
Destination MAC address:
FF-FF-FF-FF-FF-FF
Source MAC address:
MAC 1
Operation type: ARP request
MAC address of the sender: MAC 1
IP address of the sender: IP 1
Destination MAC address: 00-00-00-00-00-00
Destination IP address: IP 2
Step 2:
Host 1 sends an ARP request to discover the MAC address of Host 2.
The destination MAC address in the ARP request is 0 because the destination MAC address is unknown.
Host 1 checks cached ARP entries.
Host 1 sends an ARP request.
Host 2 adds an ARP entry.
Host 2 sends an ARP reply.
Host 1 adds an ARP entry.
3
2
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: In this example, the ARP table of Host 1 does not contain the MAC address of Host 2. Therefore, Host 1 sends an ARP request message to discover the destination MAC address.
The ARP request message is encapsulated in an Ethernet frame. The source MAC address in the frame header is the MAC address of Host 1 at the transmit end. Because Host 1 does not know the MAC address of Host 2, the destination MAC address is the broadcast address FF-FF-FF-FF-FF-FF.
The ARP request message contains the source MAC address, source IP address, destination MAC address, and destination IP address. The destination MAC address is all 0s. The ARP request message is broadcast to all hosts on the network, including gateways.

## Slide 33: ARP Implementation Principles (3)
Host 2>arp -a
Internet Address Physical Address Type
192.168.1.1 3C-52-82-49-7E-9D Dynamic
GE 0/0/1
GE 0/0/2
GE 0/0/3
Host 1
Host 2
IP 1: 192.168.1.1/24
MAC 1: 3C-52-82-49-7E-9D
IP 2: 192.168.1.2/24
MAC 2: 48-A4-72-1C-8F-4F
Step 4:
After receiving the ARP request message, each host checks whether it is the destination of the message based on the carried destination IP address.
Host 2 finds that it is the destination of the message and then records the mapping between the sender's MAC and IP addresses in its ARP table.
4
Host 1 checks cached ARP entries.
Host 1 sends an ARP request.
Host 2 adds an ARP entry.
Host 2 sends an ARP reply.
Host 1 adds an ARP entry.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: After receiving the ARP request message, each host checks whether it is the destination of the message based on the carried destination IP address. If not, the host does not respond to the ARP request message. If so, the host adds the sender's MAC and IP addresses carried in the ARP request message to the ARP table, and then replies with an ARP reply message.

## Slide 34: ARP Implementation Principles (4)
GE 0/0/1
GE 0/0/2
GE 0/0/3
Host 1
Host 2
IP 1: 192.168.1.1/24
MAC 1: 3C-52-82-49-7E-9D
IP 2: 192.168.1.2/24
MAC 2: 48-A4-72-1C-8F-4F
Eth_II | ARP Reply | FCS
Destination MAC address: MAC-1
Source MAC address: MAC 2
Operation type: ARP reply
Sender's MAC address: MAC 2
Sender's IP address: IP 2
Receiver's MAC address: MAC 1
Receiver's IP address: IP 1
Step 6:
After receiving the unicast data frame, the switch forwards the frame.
Step 5:
Host 2 sends an ARP reply to Host 1.
In this step, Host 2 has discovered the MAC address of Host 1, so the ARP reply is a unicast data frame.
Host 1 checks cached ARP entries.
Host 1 sends an ARP request.
Host 2 adds an ARP entry.
Host 2 sends an ARP reply.
Host 1 adds an ARP entry.
5
6
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: Host 2 sends an ARP reply message to Host 1.
In the ARP reply message, the sender's IP address is the IP address of Host 2 and the receiver's IP address is the IP address of Host 1. The receiver's MAC address is the MAC address of Host 1 and the sender's MAC address is the MAC address of Host 2. The operation type is set to reply.
ARP reply messages are transmitted in unicast mode.

## Slide 35: ARP Implementation Principles (5)
Host 1>arp -a
Internet Address Physical Address Type
192.168.1.2 48-A4-72-1C-8F-4F Dynamic
GE 0/0/1
GE 0/0/2
GE 0/0/3
Host 1
Host 2
IP 1: 192.168.1.1/24
MAC 1: 3C-52-82-49-7E-9D
IP 2: 192.168.1.2/24
MAC 2: 48-A4-72-1C-8F-4F
Step 7:
After receiving the ARP reply message, Host 1 checks whether it is the destination of the message based on the carried destination IP address.
If so, Host 1 records the carried sender's MAC and IP addresses in its ARP table.
Host 1 checks cached ARP entries.
Host 1 sends an ARP request.
Host 2 adds an ARP entry.
Host 2 sends an ARP reply.
Host 1 adds an ARP entry.
7
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: After receiving the ARP reply message, Host 1 checks whether it is the destination of the message based on the carried destination IP address. If so, Host 1 records the carried sender's MAC and IP addresses in its ARP table.

## Slide 36: Physical Layer
After data arrives at the physical layer, the physical layer converts a digital signal into an optical signal, an electrical signal, or an electromagnetic wave signal based on the physical media.
PDUs transmitted at the physical layer are called bitstreams.
The physical layer is at the bottom of the model.
  This layer transmits bitstreams on media.
  It standardizes physical features such as cables, pins, voltages, and interfaces.
  Common transmission media include twisted pairs, optical fibers, and electromagnetic waves.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer (Bitstream)
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 37: Common Transmission Media
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
1
2
3
4
Data transmission between terminal and wireless routers through wireless signals
Data transmission through twisted pairs
Data transmission through serial cables
RJ45 connector
Twisted pair
Fiber
Optical module
Synchronous/asynchronous serial cable: V.24 on the left and V.35 on the right
Mobile phone
Laptop
PAD
Wireless router
Data transmission through optical fibers
Notes: Twisted pairs: most common transmission media used on Ethernet networks. Twisted pairs can be classified into the following types based on their anti-electromagnetic interference capabilities:
  STP: shielded twisted pairs
  UTP: unshielded twisted pairs
Optical fiber transmission can be classified into the following types based on functional components:
  Fibers: optical transmission media, which are glass fibers, used to restrict optical transmission channels.
  Optical modules: convert electrical signals into optical signals to generate optical signals.
Serial cables are widely used on wide area networks (WANs). The types of interfaces connected to serial cables vary according to WAN line types. The interfaces include synchronous/synchronous serial interfaces, ATM interfaces, POS interfaces, and CE1/PRI interfaces.
Wireless signals may be transmitted by using electromagnetic waves. For example, a wireless router modulates data and sends the data by using electromagnetic waves, and a wireless network interface card of a mobile terminal demodulates the electromagnetic waves to obtain data. Data transmission from the wireless router to the mobile terminal is then complete.

## Slide 38
Applications and Data
Network Reference Model and Standard Protocols
Data Communication Process

## Slide 39: Data Encapsulation on the Sender
www.huawei.com
Application Layer
DATA
Physical Layer
Transport Layer
TCP Header | DATA
Network Layer
IP Header | Payload
Data Link Layer
Eth Header | Payload | FCS
 |  |  |  |  |  |  |  |  |  | ...
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | ...
Transmission Media
Segment
Packet
Frame
Bit
Data
Transmission Media
Notes: Assume that you are using a web browser to access Huawei's official website. After you enter the website address and press Enter, the following events occur on your computer:
  The browser (application program) invokes HTTP (application layer protocol) to encapsulate the application layer data. (The DATA in the figure should also include the HTTP header, which is not shown here.)
  HTTP uses TCP to ensure reliable data transmission and transmits encapsulated data to the TCP module.
  The TCP module adds the corresponding TCP header information (such as the source and destination port numbers) to the data transmitted from the application layer. At the transport layer, the PDU is called a segment.
  On an IPv4 network, the TCP module sends the encapsulated segment to the IPv4 module at the network layer. (On an IPv6 network, the segment is sent to the IPv6 module for processing.)
  After receiving the segment from the TCP module, the IPv4 module encapsulates the IPv4 header. At this layer, the PDU is called a packet.

## Slide 40
Notes:   Ethernet is used as the data link layer protocol. Therefore, after the IPv4 module completes encapsulation, it sends the packet to the Ethernet module (such as the Ethernet NIC) at the data link layer for processing.
  After receiving the packet from the IPv4 module, the Ethernet module adds the corresponding Ethernet header and FCS frame trailer to the packet. At this layer, the PDU is called a frame.
  After the Ethernet module completes encapsulation, it sends the data to the physical layer.
  Based on the physical media, the physical layer converts digital signals into electrical signals, optical signals, or electromagnetic (wireless) signals.
  The converted signals start to be transmitted on the network.

## Slide 41: Data Transmission on the Intermediate Network
Encapsulated data is transmitted on the network.
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Data Link Layer
Physical Layer
Network Layer
Data Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Data
Data
Notes: In most cases:
  A Layer 2 device (such as an Ethernet switch) only decapsulates the Layer 2 header of the data and performs the corresponding switching operation according to the information in the Layer 2 header.
  A Layer 3 device (such as a router) decapsulates the Layer 3 header and performs routing operations based on the Layer 3 header information.
  Note: The details and principles of switching and routing will be described in subsequent courses.

## Slide 42: Data Decapsulation on the Receiver
DATA
 |  |  |  |  |  |  |  |  |  | ……
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | ...
Payload
Eth Header
FCS
Payload
IP Header
DATA
TCP Header
Web server
Application Layer
Physical Layer
Transport Layer
Network Layer
Data Link Layer
Segment
Packet
Frame
Bit
Data
Transmission Media
Notes: After being transmitted over the intermediate network, the data finally reaches the destination server. Based on the information in different protocol headers, the data is decapsulated layer by layer, processed, transmitted, and finally sent to the application on the web server for processing.

## Slide 43
Both the OSI reference model and the TCP/IP reference model adopt the layered design concept.
  Clear division of functions and boundaries between layers facilitates the development, design, and troubleshooting of each component.
  The functions of each layer can be defined to impel industry standardization.
  Interfaces can be provided to enable communication between hardware and software on various networks, improving compatibility.
Data generation and transmission require collaboration between modules. Meanwhile, each module must fulfill its own responsibilities.

## Slide 44
What are the benefits of the layered model?
What are the common protocols at the application layer, transport layer, network layer, and data link layer?
Notes: Answer:
  Clear division of functions and boundaries between layers facilitates the development, design, and troubleshooting of each component.
  The functions of each layer can be defined to impel industry standardization.
  Interfaces can be provided to enable communication between hardware and software on various networks, improving compatibility.
Answer:
  Application layer: HTTP, FTP, Telnet, and so on
  Transport layer: UDP and TCP
  Network layer: IP, ICMP, and so on
  Data link layer: Ethernet, PPP, PPPoE, and so on