## Slide 1
Luyueyue/lWX445705

## Slide 2: VLAN Principles and Configuration

## Slide 3
Ethernet technology implements data communication over shared media based on carrier sense multiple access with collision detection (CSMA/CD). If there are a large number of PCs on the Ethernet, security risks and broadcast storms may occur, deteriorating network performance and even causing network breakdowns.
The virtual local area network (VLAN) technology is therefore introduced to solve the preceding problem.
This course describes basic VLAN principles, working principles of different Layer 2 interfaces, VLAN applications, data forwarding principles, and basic VLAN configuration methods.

## Slide 4
On completion of this course, you will be able to:
  Understand the background of the VLAN technology.
  Identify the VLAN to which data belongs.
  Master different VLAN assignment modes.
  Describe how data communication is implemented through VLANs.
  Master basic VLAN configuration methods.

## Slide 5
What Is VLAN
VLAN Principles
VLAN Applications
VLAN Configuration Examples

## Slide 6: Issues Facing a Traditional Ethernet
On a typical switching network,broadcast frames or unknown unicast frames sent by a PC are flooded in the entire broadcast domain.
The larger the broadcast domain is, the more serious network security and junk traffic problems are.
Unicast frame
PC1
PC2
Valid traffic
Junk traffic
SW1
SW2
SW3
SW4
SW5
SW6
SW7
(Note: This example assumes that the MAC address entry of PC2 exists in the MAC address tables of SW1, SW3, and SW7 rather than SW2 and SW5.)
Layer 2 broadcast domain
Notes: Broadcast domain:
  The preceding figure shows a typical switching network with only PCs and switches. If PC1 sends a broadcast frame, the switches flood the frame on the network. As a result, all the other PCs receive the frame.
  The range that broadcast frames can reach is called a Layer 2 broadcast domain (broadcast domain for short). A switching network is a broadcast domain.
Network security and junk traffic problems:
  Assume that PC1 sends a unicast frame to PC2. The MAC address entry of PC2 exists in the MAC address tables of SW1, SW3, and SW7 rather than SW2 and SW5. In this case, SW1 and SW3 forward the frame in point-to-point mode, SW7 discards the frame, and SW2 and SW5 flood the frame. As a result, although PC2 receives the unicast frame, other PCs on the network also receive the frame that should not be received.
The larger the broadcast domain is, the more serious network security and junk traffic problems are.

## Slide 7: VLAN
PC2
SW1
SW2
SW3
SW4
SW5
SW6
SW7
PC1
VLAN
(multiple broadcast domains)
Broadcast frame
The VLAN technology isolates broadcast domains.
Characteristics:
  Geographically independent.
  Only devices in the same VLAN can directly communicate at Layer 2.
Notes: The VLAN technology is introduced to solve the problems caused by large broadcast domains.
  By deploying VLANs on switches, you can logically divide a large broadcast domain into several small broadcast domains. This effectively improves network security, lowers junk traffic, and reduces the number of required network resources.
VLAN characteristics:
  Each VLAN is a broadcast domain. Therefore, PCs in the same VLAN can directly communicate at Layer 2. PCs in different VLANs, by contrast, can only communicate at Layer 3 instead of directly communicating at Layer 2. In this way, broadcast packets are confined to a VLAN.
  VLAN assignment is geographically independent.
Advantages of the VLAN technology:
  Allows flexible setup of virtual groups. With the VLAN technology, terminals in different geographical locations can be grouped together, simplifying network construction and maintenance.
  Confines each broadcast domain to a single VLAN, conserving bandwidth and improving network processing capabilities.
  Enhances LAN security. Frames in different VLANs are separately transmitted, so that PCs in a VLAN cannot directly communicate with those in another VLAN.
  Improves network robustness. Faults in a VLAN do not affect PCs in other VLANs.
Note: Layer 2 refers to the data link layer.

## Slide 8
What Is VLAN
VLAN Principles
VLAN Applications
VLAN Configuration Examples
Notes: This part describes VLAN principles from the following three aspects: VLAN identification, VLAN assignment, and VLAN frame processing on switches.

## Slide 9: VLAN Implementation
Switch1 and Switch2 belong to the network of the same enterprise. VLANs are planned for the network, with VLAN 10 for department A and VLAN 20 for department B. Employees in departments A and B are connected to both Switch1 and Switch2.
Assume that a frame sent from PC1 reaches Switch2 through the link between Switch1 and Switch2. If no processing is implemented, Switch2 can neither identify the VLAN to which the frame belongs nor determine the local VLAN to which the frame should be sent.
PC3
VLAN 20
PC2
PC1
1
2
3
Switch1
4
5
5
4
3
Switch2
2
1
Frame
Frame
VLAN 10
VLAN 20
PC4
VLAN 10
VLAN Identification
VLAN Assignment
VLAN Frame Processing

## Slide 10: VLAN Tag
How does a switch identify the VLAN to which a received frame belongs?
VLAN 10
VLAN 20
Which VLAN does the received frame belong to?
20
VLAN Tag
IEEE 802.1Q defines a 4-byte VLAN tag for Ethernet frames, enabling switches to identify the VLANs to which received frames belong.
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: As shown in the figure, after receiving a frame and identifying the VLAN to which the frame belongs, SW1 adds a VLAN tag to the frame to specify this VLAN. Then, after receiving the tagged frame sent from SW1, another switch, such as SW2, can easily identify the VLAN to which the frame belongs based on the VLAN tag.
Frames with a 4-byte VLAN tag are called IEEE 802.1Q frames or VLAN frames.

## Slide 11: VLAN Frame
TPID (0x8100)
PRI
CFI
VLAN ID
16 bits
3 bits
1 bit
12 bits
Destination MAC address
Source MAC address
Length/
Type
Data
FCS
Original Ethernet frame
(untagged frame)
802.1Q tag
802.1Q frame
(tagged frame)
Destination MAC address
Source MAC address
Length/
Type
Data
FCS
Tag
802.1Q tag inserted between the two fields
Tag protocol identifier (TPID): identifies the type of a frame. The value 0x8100 indicates an IEEE 802.1Q frame.
PRI: identifies the priority of a frame, which is mainly used for QoS.
Canonical format indicator (CFI): indicates whether a MAC address is in the canonical format. For Ethernet frames, the value of this field is 0.
VLAN ID: identifies the VLAN to which a frame belongs.
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: Ethernet frames in a VLAN are mainly classified into the following types:
  Tagged frames: Ethernet frames for which a 4-byte VLAN tag is inserted between the source MAC address and length/type fields according to IEEE 802.1Q
  Untagged frames: frames without a 4-byte VLAN tag
Main fields in a VLAN frame:
  TPID: a 16-bit field used to identify the type of a frame.
    The value 0x8100 indicates an IEEE 802.1Q frame. A device that does not support 802.1Q discards 802.1Q frames.
    Device vendors can define TPID values for devices. To enable a device to identify the non-802.1Q frames sent from another device, you can change the TPID on the device to be the same as that device.
  PRI: a 3-bit field used to identify the priority of a frame. It is mainly used for QoS.
    The value of this field is an integer ranging from 0 to 7. A larger value indicates a higher priority. If congestion occurs, a switch preferentially sends frames with the highest priority.

## Slide 12
Notes:   CFI: a 1-bit field indicating whether a MAC address is encapsulated in the canonical format. This field is mainly used to differentiate Ethernet frames, fiber distributed digital interface (FDDI) frames, and token ring frames.
    The value 0 indicates that the MAC address is encapsulated in the canonical format, and the value 1 indicates that the MAC address is encapsulated in a non-canonical format.
    For Ethernet frames, the value of this field is 0.
  VLAN ID: also called VID, a 12-bit field used to identify the VLAN to which a frame belongs.
    The value of this field is an integer ranging from 0 to 4095. Values 0 and 4095 are reserved. Therefore, only VLAN IDs from 1 to 4094 can be used.
    A switch uses the VID contained in the VLAN tag to identify the VLAN that a frame belongs. Broadcast frames are forwarded only in the local VLAN.
Method of identifying frames with VLAN tags:
  Value of the Length/Type field of frames = 0x8100
Note: PCs cannot identify tagged frames and therefore can send or process only untagged frames. By contrast, all frames processed by switches are tagged ones, improving processing efficiency.

## Slide 13: VLAN Implementation
The link between Switch1 and Switch2 carries data of multiple VLANs. In this situation, a VLAN-based data tagging method is required to distinguish the frames of different VLANs.
IEEE 802.1Q, often referred to as Dot1q, defines a system of VLAN tagging for Ethernet frames by inserting an 802.1Q tag into the frame header to carry VLAN information.
PC3
VLAN 20
PC2
PC1
1
2
3
Switch1
4
5
5
4
3
Switch2
2
1
VLAN 10
VLAN 20
PC4
VLAN 10
Original frame 1
Original frame 2
Original frame 2
Original frame 1
Tagged frame
Tagged frame
VLAN Identification
VLAN Assignment
VLAN Frame Processing

## Slide 14: VLAN Assignment Methods
How are VLANs assigned on a network?
SW1
PC1
PC2
PC3
PC4
GE 0/0/1
GE 0/0/2
GE 0/0/3
GE 0/0/4
10.0.1.1
MAC 1
10.0.2.1
MAC 2
10.0.1.2
MAC 3
10.0.2.2
MAC 4
VLAN Assignment Method | VLAN 10 | VLAN 20
Interface-based assignment | GE 0/0/1 and GE 0/0/3 | GE 0/0/2 and GE 0/0/4
MAC address-based assignment | MAC 1 and MAC 3 | MAC 2 and MAC 4
IP subnet-based assignment | 10.0.1.* | 10.0.2.*
Protocol-based assignment | IP | IPv6
Policy-based assignment | 10.0.1.* + GE 0/0/1 + MAC 1 | 10.0.2.* + GE 0/0/2 + MAC 2
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: PCs send only untagged frames. After receiving such an untagged frame, a switch that supports the VLAN technology needs to assign the frame to a specific VLAN based on certain rules.
Available VLAN assignment methods are as follows:
  Interface-based assignment: assigns VLANs based on switch interfaces.
    A network administrator preconfigures a port VLAN ID (PVID) for each switch interface. When an untagged frame arrives at an interface of a switch, the switch adds a tag carrying the PVID of the interface to the frame. The frame is then transmitted in the specified VLAN.
  MAC address-based assignment: assigns VLANs based on the source MAC addresses of frames.
    A network administrator preconfigures the mapping between MAC addresses and VLAN IDs. After receiving an untagged frame, a switch adds the VLAN tag mapping the source MAC address of the frame to the frame. The frame is then transmitted in the specified VLAN.

## Slide 15
Notes:   IP subnet-based assignment: assigns VLANs based on the source IP addresses and subnet masks of frames.
    A network administrator preconfigures the mapping between IP addresses and VLAN IDs. After receiving an untagged frame, a switch adds the VLAN tag mapping the source IP address of the frame to the frame. The frame is then transmitted in the specified VLAN.
  Protocol-based assignment: assigns VLANs based on the protocol (suite) types and encapsulation formats of frames.
    A network administrator preconfigures the mapping between protocol (suite) types and VLAN IDs. After receiving an untagged frame, a switch adds the VLAN tag mapping the protocol (suite) type of the frame to the frame. The frame is then transmitted in the specified VLAN.
  Policy-based assignment: assigns VLANs based on a specified policy, such as a policy combining the preceding methods.
    A network administrator preconfigures a policy. After receiving an untagged frame that matches the policy, a switch adds a specified VLAN tag to the frame. The frame is then transmitted in the specified VLAN.

## Slide 16: Interface-based VLAN Assignment
SW1
SW2
PC1
PC2
PC3
PC4
VLAN 10
VLAN 20
PVID 10
PVID 10
PVID 20
PVID 20
PVID 1
PVID 1
The VLAN needs to be reconfigured if PCs move.
10
Interface-based VLAN Assignment
Principles
VLANs are assigned based on interfaces.
A network administrator preconfigures a PVID for each switch interface and assigns each interface to a VLAN corresponding to the PVID.
After an interface receives an untagged frame, the switch adds a tag carrying the PVID of the interface to the frame. The frame is then transmitted in the specified VLAN.
Port Default VLAN ID: PVID
Default VLAN ID for an interface
Value range: 1–4094
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: Assignment rules:
  VLAN IDs are configured on physical interfaces of a switch. All PC-sent untagged frames arriving at a physical interface are assigned to the VLAN corresponding to the PVID configured for the interface.
Characteristics:
  VLAN assignment is simple, intuitive, and easy to implement. Currently, it is the most widely used VLAN assignment method.
  If the switch interface to which a PC is connected changes, the VLAN to which frames sent from the PC to the interface are assigned may also change.
Port Default VLAN ID: PVID
  A PVID needs to be configured for each switch interface. All untagged frames arriving at an interface are assigned to the VLAN corresponding to the PVID configured for the interface.
  The default PVID is 1.

## Slide 17: MAC Address-based VLAN Assignment
MAC Address | VLAN ID
MAC 1 | 10
MAC 2 | 10
... | ...
Mapping Between MAC Addresses and VLAN IDs on SW1
MAC Address-based VLAN Assignment
Principles
VLANs are assigned based on the source MAC addresses of frames.
A network administrator preconfigures the mapping between MAC addresses and VLAN IDs.
After receiving an untagged frame, a switch adds the VLAN tag mapping the source MAC address of the frame to the frame. The frame is then transmitted in the specified VLAN.
Mapping table
Records the mapping between MAC addresses and VLAN IDs.
SW1
SW2
PC1
MAC 1
PC2
MAC 2
PC3
MAC 3
PC4
MAC 4
VLAN 10
VLAN 20
GE 0/0/1
GE 0/0/2
The VLAN does not need to be reconfigured even if PCs move.
10
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: Assignment rules:
  Each switch maintains a table recording the mapping between MAC addresses and VLAN IDs. After receiving a PC-sent untagged frame, a switch analyzes the source MAC address of the frame, searches the mapping table for the VLAN ID mapping the MAC address, and assigns the frame to the corresponding VLAN according to the mapping.
Characteristics:
  This assignment method is a bit complex but more flexible.
  If the switch interface to which a PC is connected changes, the VLAN to which frames sent from the PC to the interface are assigned remains unchanged because the PC's MAC address does not change.
  However, as malicious PCs can easily forge MAC addresses, this assignment method is prone to security risks.

## Slide 18: Layer 2 Ethernet Interface Types
Access interface
Trunk interface
Interface Types
Access interface
An access interface is used to connect a switch to a terminal, such as a PC or server. In general, the NICs on such a terminal receive and send only untagged frames. An access interface can be added to only one VLAN.
Trunk interface
A trunk interface allows frames that belong to multiple VLANs to pass through and differentiates the frames using the 802.1Q tag. This type of interface is used to connect a switch to another switch or a sub-interface on a device, such as a router or firewall.
Hybrid interface
Similar to a trunk interface, a hybrid interface also allows frames that belong to multiple VLANs to pass through and differentiates the frames using the 802.1Q tag. You can determine whether to allow a hybrid interface to carry VLAN tags when sending the frames of one or more VLANs.
VLAN10
VLAN10
VLAN20
VLAN20
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: The interface-based VLAN assignment method varies according to the switch interface type.
Access interface
  An access interface often connects to a terminal (such as a PC or server) that cannot identify VLAN tags, or is used when VLANs do not need to be differentiated.
Trunk interface
  A trunk interface often connects to a switch, router, AP, or voice terminal that can receive and send both tagged and untagged frames.
Hybrid interface
  A hybrid interface can connect to a user terminal (such as a PC or server) that cannot identify VLAN tags or to a switch, router, AP, or voice terminal that can receive and send both tagged and untagged frames.
  By default, hybrid interfaces are used on Huawei devices.

## Slide 19: Access Interface
GE 0/0/1
Access (VLAN 10)
Inside a switch
Frame receiving
Frame sending
10
Untagged frame
After receiving an untagged frame:
The interface permits the frame and adds a VLAN tag carrying the PVID of the interface.
GE 0/0/1
Access (VLAN 10)
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is the same as the PVID of the interface, the interface permits the frame.
If the VLAN ID of the frame is different from the PVID of the interface, the interface discards the frame.
GE 0/0/1
Access (VLAN 10)
Inside a switch
Untagged frame
If the VLAN ID of the frame is the same as the PVID of the interface:
The interface removes the VLAN tag from the frame and then sends the frame.
GE 0/0/1
Access (VLAN 10)
Inside a switch
20
If the VLAN ID of the frame is different from the PVID of the interface:
The interface discards the frame.
10
10
Untagged frame
Tagged frame
10
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: How do switch interfaces process tagged and untagged frames? First, let's have a look at access interfaces.
Characteristics of access interfaces:
  An access interface permits only frames whose VLAN ID is the same as the PVID of the interface.
Frame receiving through an access interface:
  After receiving an untagged frame, the access interface adds a tag with the VID being the PVID of the interface to the frame and then floods, forwards, or discards the tagged frame.
  After receiving a tagged frame, the access interface checks whether the VID in the tag of the frame is the same as the PVID. If they are the same, the interface forwards the tagged frame. Otherwise, the interface directly discards the tagged frame.
Frame sending through an access interface:
  After receiving a tagged frame sent from another interface on the same switch, the access interface checks whether the VID in the tag of the frame is the same as the PVID.
    If they are the same, the interface removes the tag from the frame and sends the untagged frame out.
    Otherwise, the interface directly discards the tagged frame.

## Slide 20: Trunk interface
GE 0/0/1
Trunk (PVID = 10)
Inside a switch
10
Untagged frame
After receiving an untagged frame:
The interface adds a VLAN tag with the VID being the PVID of the interface to the frame and permits the frame only when the VID is in the list of VLAN IDs permitted by the interface. If the VID is not in the list, the interface discards the frame.
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface permits the frame. Otherwise, the interface discards the frame.
Inside a switch
Untagged frame
If the VLAN ID of the frame is the same as the PVID of the interface:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface removes the tag from the frame and sends the frame out. Otherwise, the interface discards the frame.
Inside a switch
20
If the VLAN ID of the frame is different from the PVID of the interface:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface sends the frame out without removing the tag of the frame. Otherwise, the interface discards the frame.
10
10
Permitted VLAN ID: 10
GE 0/0/1
Trunk (PVID = 1)
Permitted VLAN ID: 10
GE 0/0/1
Trunk (PVID = 10)
Permitted VLAN ID: 10
GE 0/0/1
Trunk (PVID = 10)
Permitted VLAN ID: 20
20
Frame receiving
Frame sending
Untagged frame
Tagged frame
10
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: For a trunk interface, you need to configure not only a PVID but also a list of VLAN IDs permitted by the interface. By default, VLAN 1 exists in the list.
Characteristics of trunk interfaces:
  A trunk interface allows only frames whose VLAN IDs are in the list of VLAN IDs permitted by the interface to pass through.
  It allows tagged frames from multiple VLANs but untagged frames from only one VLAN to pass through.
Frame receiving through a trunk interface:
  After receiving an untagged frame, the trunk interface adds a tag with the VID being the PVID of the interface to the frame and then checks whether the VID is in the list of VLAN IDs permitted by the interface. If the VID is in the list, the interface forwards the tagged frame. Otherwise, the interface directly discards the tagged frame.
  After receiving a tagged frame, the trunk interface checks whether the VID in the tag of the frame is in the list of VLAN IDs permitted by the interface. If the VID is in the list, the interface forwards the tagged frame. Otherwise, the interface directly discards the tagged frame.

## Slide 21
Notes: Frame sending through a trunk interface:
  After receiving a tagged frame sent from another interface on the same switch, the trunk interface checks whether the VID in the tag of the frame is in the list of VLAN IDs permitted by the interface. If the VID is not in the list, the interface directly discards the frame.
  After receiving a tagged frame sent from another interface on the same switch, the trunk interface checks whether the VID in the tag of the frame is in the list of VLAN IDs permitted by the interface. If the VID is in the list, the interface checks whether the VID is the same as the PVID of the interface.
    If they are the same, the interface removes the tag from the frame and sends the untagged frame out.
    If they are different, the interface directly sends the frame out without removing the tag from the frame.

## Slide 22: Example for Frame Processing on Access and Trunk Interfaces
Describe how inter-PC access is implemented in this example.
Trunk Interfaces on SW1 and SW2
SW1
PC1
PC2
PC3
PC4
VLAN 10
VLAN 10
VLAN 20
VLAN 20
SW2
PVID 10
PVID 20
PVID 10
PVID 20
PVID 1
PVID 1
10
20
Access interface
Trunk interface
List of Permitted VLAN IDs | 
VLAN ID | 1
 | 10
 | 20
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: In this example, SW1 and SW2 connect to PCs through access interfaces. PVIDs are configured for the interfaces, as shown in the figure. SW1 and SW2 are connected through trunk interfaces whose PVIDs are all set to 1. The table lists the VLAN IDs permitted by the trunk interfaces.
Describe how inter-PC access is implemented in this example.

## Slide 23: Hybrid Interface
GE 0/0/1
Hybrid (PVID = 10)
Inside a switch
10
After receiving an untagged frame:
The interface adds a VLAN tag with the VID being the PVID of the interface to the frame and permits the frame only when the VID is in the list of VLAN IDs permitted by the interface. If the VID is not in the list, the interface discards the frame.
Inside a switch
10
After receiving a tagged frame:
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface, the interface permits the frame. Otherwise, the interface discards the frame.
Inside a switch
Untagged frame
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface:
If the interface has been configured not to carry VLAN tags when sending frames, it removes the tag from the frame and then sends the frame out.
Inside a switch
20
If the VLAN ID of the frame is in the list of VLAN IDs permitted by the interface:
If the interface has been configured to carry VLAN tags when sending frames, it sends the frame out without removing the tag of the frame.
10
10
Permitted VLAN ID: 10
GE 0/0/1
Hybrid (PVID = 1)
Permitted VLAN ID: 10
GE 0/0/1
Hybrid (PVID = 10)
Permitted VLAN ID: 10
GE 0/0/1
Hybrid (PVID = 10)
Permitted VLAN ID: 20
20
Untagged frame
Untagged frame
Tagged frame
10
Frame receiving
Frame sending
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: For a hybrid interface, you need to configure not only a PVID but also two lists of VLAN IDs permitted by the interface: one untagged VLAN ID list and one tagged VLAN ID list. By default, VLAN 1 is in the untagged VLAN ID list. Frames from all the VLANs in the two lists are allowed to pass through the hybrid interface.
Characteristics of hybrid interfaces:
  A hybrid interface allows only frames whose VLAN IDs are in the lists of VLAN IDs permitted by the interface to pass through.
  It allows tagged frames from multiple VLANs to pass through. Frames sent out from a hybrid interface can be either tagged or untagged, depending on the VLAN configuration.
  Different from a trunk interface, a hybrid interface allows untagged frames from multiple VLANs to pass through.

## Slide 24
Notes: Frame receiving through a hybrid interface:
  After receiving an untagged frame, the hybrid interface adds a tag with the VID being the PVID of the interface to the frame and then checks whether the VID is in the tagged or untagged VLAN ID list. If the VID is in the list, the interface forwards the tagged frame. Otherwise, the interface directly discards the tagged frame.
  After receiving a tagged frame, the hybrid interface checks whether the VID in the tag of the frame is in the tagged or untagged VLAN ID list. If the VID is in the tagged or untagged VLAN ID list, the interface forwards the tagged frame. Otherwise, the interface directly discards the tagged frame.
Frame sending through a hybrid interface:
  After receiving a tagged frame sent from another interface on the same switch, the hybrid interface checks whether the VID in the tag of the frame is in the tagged or untagged VLAN ID list. If the VID is not in any of the two lists, the interface directly discards the frame.
  After receiving a tagged frame sent from another interface on the same switch, the hybrid interface checks whether the VID in the tag of the frame is in the tagged or untagged VLAN ID list. If the VID is in the untagged VLAN ID list, the interface removes the tag from the frame and then sends the untagged frame out.
  After receiving a tagged frame sent from another interface on the same switch, the hybrid interface checks whether the VID in the tag of the frame is in the tagged or untagged VLAN ID list. If the VID is in the tagged VLAN ID list, the interface directly sends the frame out without removing the tag from the frame.

## Slide 25: Example for Frame Processing on Hybrid Interfaces
Describe how PCs access the server in this example.
PC1
PC2
Server
VLAN 10
VLAN 100
VLAN 20
PVID 10
PVID 1
PVID 1
10
20
SW1
SW2
Interface 1
List of VLAN IDs Permitted by Interfaces on SW1
Interface 1
PVID 20
Interface 2
PVID 100
Interface 1
Interface 3
Interface 3
Interface 2
Interface 3
List of VLAN IDs Permitted by Interfaces on SW2
Interface 1
Interface 3
Hybrid Interface
Untagged | 
VLAN ID | 1
 | 10
 | 100
Untagged | 
VLAN ID | 1
 | 20
 | 100
Tagged | 
VLAN ID | 10
 | 10
 | 100
Tagged | 
VLAN ID | 10
 | 20
 | 100
Untagged | 
VLAN ID | 1
 | 10
 | 20
 | 100
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: In this example, SW1 and SW2 connect to PCs through hybrid interfaces. The two switches are connected also through this type of interface. PVIDs are configured for the interfaces, as shown in the figure. The tables list the VLAN IDs permitted by the interfaces.
Describe how PCs access the server in this example.

## Slide 26: Summary
Access Interface
Frame receiving
  Untagged frame: adds a tag with the VID being the PVID of the interface and permits the frame.
  Tagged frame: checks whether the VID in the tag of the frame is the same as the PVID of the interface. If they are the same, permits the frame; otherwise, discards the frame.
Trunk Interface
Frame receiving
  Untagged frame: adds a tag with the VID being the PVID of the interface and checks whether the VID is in the list of permitted VLAN IDs. If yes, permits the frame. If not, discards it.
  Tagged frame: checks whether the VID is in the list of permitted VLAN IDs. If yes, permits the frame. If not, discards it.
Hybrid Interface
Frame receiving
  Untagged frame: adds a tag with the VID being the PVID of the interface and checks whether the VID is in the list of permitted VLAN IDs. If yes, permits the frame. If not, discards it.
  Tagged frame: checks whether the VID is in the list of permitted VLAN IDs. If yes, permits the frame. If not, discards it.
Frame sending
  Checks whether the VID in the tag of the frame is the same as the PVID of the interface. If they are the same, removes the tag and sends the frame out; otherwise, discards the frame.
Frame sending
  If the VID is in the list of permitted VLAN IDs and the same as the PVID of the interface, removes the tag and sends the frame out.
  If the VID is in the list of permitted VLAN IDs but different from the PVID of the interface, sends the frame out without removing the tag.
  If the VID is not in the list of permitted VLAN IDs, discards the frame.
Frame sending
  If the VID is not in the list of permitted VLAN IDs, discards the frame.
  If the VID is in the untagged VLAN ID list, removes the tag and sends the frame out.
  If the VID is in the tagged VLAN ID list, sends the frame out without removing the tag.
VLAN Identification
VLAN Assignment
VLAN Frame Processing
Notes: The processes of adding and removing VLAN tags on interfaces are as follows:
  Frame receiving:
    After receiving an untagged frame, access, trunk, and hybrid interfaces all add a VLAN tag to the frame. Then, trunk and hybrid interfaces determine whether to permit the frame based on the VID of the frame (the frame is permitted only when the VID is a permitted VLAN ID), whereas an access interface permits the frame unconditionally.
    After receiving a tagged frame, an access interface permits the frame only when the VID in the tag of the frame is the same as the PVID configured for the interface, while trunk and hybrid interfaces permit the frame only when the VID in the tag of the frame is in the list of permitted VLANs.
  Frame sending:
    Access interface: directly removes VLAN tags from frames before sending the frames.
    Trunk interface: removes VLAN tags from frames only when the VIDs in the tags are the same as the PVID of the interface.
    Hybrid interface: determines whether to remove VLAN tags from frames based on the interface configuration.
Frames sent by an access interface are all untagged. On a trunk interface, only frames of one VLAN are sent without tags, and frames of other VLANs are all sent with tags. On a hybrid interface, you can specify the VLANs of which frames are sent with or without tags.

## Slide 27
What Is VLAN
VLAN Principles
VLAN Applications
VLAN Configuration Examples

## Slide 28: VLAN Planning
VLAN assignment rules
  By service: voice, video, and data VLANs
  By department: e.g. VLANs for engineering, marketing, and financing departments
  By application: e.g. VLANs for servers, offices, and classrooms
Tips for VLAN assignment
  VLAN IDs can be randomly assigned within the supported range. To improve VLAN ID continuity, you can associate VLAN IDs with subnets during VLAN assignment.
Example for VLAN planning
  Assume that there are three buildings: administrative building with offices, classrooms, and financing sections, teaching building with offices and classrooms, and office building with offices and financing sections. Each building has one access switch, and the core switch is deployed in the administrative building.
  The following table describes the VLAN plan.
VLAN ID | IP Address Segment | Description
1 | X.16.10.0/24 | VLAN to which office users belong
2 | X.16.20.0/24 | VLAN to which the users of the financing department belong
3 | X.16.30.0/24 | VLAN to which classroom users belong
100 | Y.16.100.0/24 | VLAN to which the device management function belongs
Notes: You are advised to assign consecutive VLAN IDs to ensure proper use of VLAN resources. The most common method is interface-based VLAN assignment.

## Slide 29: Interface-based VLAN Assignment
Applicable scenario:
  There are multiple enterprises in a building. These enterprises share network resources to reduce costs. Networks of the enterprises connect to different interfaces of the same Layer 2 switch and access the Internet through the same egress device.
VLAN assignment:
  To isolate the services of different enterprises and ensure service security, assign interfaces connected to the enterprises' networks to different VLANs. In this way, each enterprise has an independent network, and each VLAN works as a virtual work group.
Internet
L3 switch
L2 switch
Enterprise 1
VLAN 2
Enterprise 2
VLAN 3
Enterprise 3
VLAN 4

## Slide 30: MAC Address-based VLAN Assignment
Applicable scenario:
  The network administrator of an enterprise assigns PCs in the same department to the same VLAN. To improve information security, the enterprise requires that only employees in the specified department be allowed to access specific network resources.
VLAN assignment:
  To meet the preceding requirement, configure MAC address-based VLAN assignment on SW1, preventing new PCs connected to the network from accessing the network resources.
001e-10dd-dd01
001e-10dd-dd04
SW1
PC1
PC2
PC3
VLAN 10
GE 0/0/2
Enterprise
network
GE 0/0/3
GE 0/0/4
PC4
001e-10dd-dd02
001e-10dd-dd03
GE 0/0/1

## Slide 31
What Is VLAN
VLAN Principles
VLAN Applications
VLAN Configuration Examples

## Slide 32: Basic VLAN Configuration Commands
[Huawei] vlan vlan-id
Create one or more VLANs.
This command creates a VLAN and displays the VLAN view. If the VLAN to be created already exists, this command directly displays the VLAN view.
  The value of vlan-id is an integer ranging from 1 to 4094.
[Huawei] vlan batch { vlan-id1 [ to vlan-id2 ] }
This command creates VLANs in a batch. In this command:
  batch: creates VLANs in a batch.
  vlan-id1: specifies a start VLAN ID.
  vlan-id2: specifies an end VLAN ID.
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: The vlan command creates a VLAN and displays the VLAN view. If the VLAN to be created already exists, this command directly displays the VLAN view.
The undo vlan command deletes a VLAN.
By default, all interfaces are added to the default VLAN with the ID of 1.
Commands:
  vlan vlan-id
    vlan-id: specifies a VLAN ID. The value is an integer ranging from 1 to 4094.
  vlan batch { vlan-id1 [ to vlan-id2 ] }
    batch: creates VLANs in a batch.
    vlan-id1 [ to vlan-id2 ]: specifies the IDs of VLANs to be created in a batch.
      vlan-id1: specifies a start VLAN ID.
      vlan-id2: specifies an end VLAN ID. The value of vlan-id2 must be greater than or equal to that of vlan-id1. The two parameters work together to define a VLAN range.
    If you do not specify to vlan-id2, the command creates only one VLAN with the ID being specified using vlan-id1.
    The values of vlan-id1 and vlan-id2 are both integers ranging from 1 to 4094.

## Slide 33: Basic Access Interface Configuration Commands
[Huawei-GigabitEthernet0/0/1] port link-type access
Set the link type of an interface.
In the interface view, set the link type of the interface to access.
[Huawei-GigabitEthernet0/0/1] port default vlan vlan-id
Configure a default VLAN for the access interface.
In the interface view, configure a default VLAN for the interface and add the interface to the VLAN.
  vlan-id: specifies an ID for the default VLAN. The value is an integer ranging from 1 to 4094.
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment

## Slide 34: Basic Trunk Interface Configuration Commands
[Huawei-GigabitEthernet0/0/1] port link-type trunk
Set the link type of an interface.
In the interface view, set the link type of the interface to trunk.
[Huawei-GigabitEthernet0/0/1] port trunk allow-pass vlan { { vlan-id1 [ to vlan-id2 ] } | all }
Add the trunk interface to specified VLANs.
In the interface view, add the trunk interface to specified VLANs.
[Huawei-GigabitEthernet0/0/1] port trunk pvid vlan vlan-id
(Optional) Configure a default VLAN for the trunk interface.
In the interface view, configure a default VLAN for the trunk interface.
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Command: port trunk allow-pass vlan { { vlan-id1 [ to vlan-id2 ] | all }
  vlan-id1 [ to vlan-id2 ]: specifies the IDs of VLANs to which a trunk interface needs to be added.
    vlan-id1: specifies a start VLAN ID.
    vlan-id2: specifies an end VLAN ID. The value of vlan-id2 must be greater than or equal to that of vlan-id1.
    The values of vlan-id1 and vlan-id2 are both integers ranging from 1 to 4094.
  all: adds a trunk interface to all VLANs.
The port trunk pvid vlan vlan-id command configures a default VLAN for a trunk interface.
  vlan-id: specifies the ID of the default VLAN to be created for a trunk interface. The value is an integer ranging from 1 to 4094.

## Slide 35: Basic Hybrid Interface Configuration Commands
[Huawei-GigabitEthernet0/0/1] port link-type hybrid
Set the link type of an interface.
In the interface view, set the link type of the interface to hybrid.
[Huawei-GigabitEthernet0/0/1] port hybrid untagged vlan { { vlan-id1 [ to vlan-id2 ] } | all }
Add the hybrid interface to specified VLANs.
In the interface view, add the hybrid interface to specified VLANs in untagged mode.
[Huawei-GigabitEthernet0/0/1] port hybrid pvid vlan vlan-id
(Optional) Configure a default VLAN for the hybrid interface.
In the interface view, configure a default VLAN for the hybrid interface.
[Huawei-GigabitEthernet0/0/1] port hybrid tagged vlan { { vlan-id1 [ to vlan-id2 ] } | all }
In the interface view, add the hybrid interface to specified VLANs in tagged mode.
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Command: port hybrid untagged vlan { { vlan-id1 [ to vlan-id2 ] } | all }
  vlan-id1 [ to vlan-id2 ]: specifies the IDs of VLANs to which a hybrid interface needs to be added.
    vlan-id1: specifies a start VLAN ID.
    vlan-id2: specifies an end VLAN ID. The value of vlan-id2 must be greater than or equal to that of vlan-id1.
    The values of vlan-id1 and vlan-id2 are both integers ranging from 1 to 4094.
  all: adds a hybrid interface to all VLANs.
Command: port hybrid tagged vlan { { vlan-id1 [ to vlan-id2 ] } | all }
  vlan-id1 [ to vlan-id2 ]: specifies the IDs of VLANs to which a hybrid interface needs to be added.
    vlan-id1: specifies a start VLAN ID.
    vlan-id2: specifies an end VLAN ID. The value of vlan-id2 must be greater than or equal to that of vlan-id1.
    The values of vlan-id1 and vlan-id2 are both integers ranging from 1 to 4094.
  all: adds a hybrid interface to all VLANs.
The port hybrid pvid vlan vlan-id command configures a default VLAN for a hybrid interface.
  vlan-id: specifies the ID of the default VLAN to be created for a hybrid interface. The value is an integer ranging from 1 to 4094.

## Slide 36: Case1:Configuring Interface-based VLAN Assignment
Networking requirements:
  On the network shown in the left figure, the switches (SW1 and SW2) of an enterprise are connected to multiple PCs, and PCs with the same services access the network using different devices. To ensure communication security, the enterprise requires that only PCs with the same service can directly communicate.
  To meet this requirement, configure interface-based VLAN assignment on the switches and add interfaces connected to PCs with the same service to the same VLAN. In this way, PCs in different VLANs cannot directly communicate at Layer 2, but PCs in the same VLAN can directly communicate.
Access interface
Trunk interface
SW1
PC1
PC2
PC3
PC4
VLAN 10
VLAN 10
VLAN 20
VLAN 20
SW2
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Configuration roadmap:
  Create VLANs and add interfaces connected to PCs to the VLANs to isolate Layer 2 traffic between PCs with different services.
  Configure interface types and specify permitted VLANs for SW1 and SW2 to allow PCs with the same service to communicate through SW1 and SW2.

## Slide 37: Creating VLANs
Create VLANs.
[SW1] vlan 10
[SW1-vlan10] quit
[SW1] vlan 20
[SW1-vlan20] quit
[SW2] vlan batch 10 20
SW1
PC1
PC2
PC3
PC4
VLAN 10
VLAN 10
VLAN 20
VLAN 20
SW2
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment

## Slide 38: Configuring Access and Trunk Interfaces
Configure access interfaces and add the interfaces to corresponding VLANs.
[SW1] interface GigabitEthernet 0/0/1
[SW1-GigabitEthernet0/0/1] port link-type access
[SW1-GigabitEthernet0/0/1] port default vlan 10
[SW1] interface GigabitEthernet 0/0/2
[SW1-GigabitEthernet0/0/2] port link-type access
[SW1] vlan 20
[SW1-vlan20] port GigabitEthernet0/0/2
[SW1-vlan20] quit
Note: The configuration on SW2 is similar to that on SW1.
Configure a trunk interface and specify a list of VLAN IDs permitted by the interface.
[SW1] interface GigabitEthernet 0/0/3
[SW1-GigabitEthernet0/0/3] port link-type trunk
[SW1-GigabitEthernet0/0/3] port trunk pvid vlan 1
[SW1-GigabitEthernet0/0/3] port trunk allow-pass vlan 10 20
PC1
PC4
VLAN 10
VLAN 20
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
SW1
PC2
PC3
VLAN 10
VLAN 20
SW2
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
GE 0/0/1
PVID 10
GE 0/0/3
PVID 1
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment

## Slide 39: Verifying the Configuration
[SW1]display vlan
The total number of vlans is : 3
-------------------------------------------------------------------------------
U: Up; D: Down; TG: Tagged; UT: Untagged;
MP: Vlan-mapping; ST: Vlan-stacking;
#: ProtocolTransparent-vlan; *: Management-vlan;
-------------------------------------------------------------------------------
VID Type Ports
-------------------------------------------------------------------------------
1 common UT:GE0/0/3(U) ……
10 common UT:GE0/0/1(U)
TG:GE0/0/3(U)
20 common UT:GE0/0/2(U)
TG:GE0/0/3(U)
……
VLAN 10
SW1
PC1
PC2
PC3
PC4
VLAN 10
VLAN 20
VLAN 20
SW2
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
GE 0/0/1
PVID 10
GE 0/0/2
PVID 20
GE 0/0/3
PVID 1
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Command: The display vlan command displays VLAN information.
Command output:
  Tagged/Untagged: Interfaces are manually added to VLANs in tagged or untagged mode.
  VID or VLAN ID: VLAN ID.
  Type or VLAN Type: VLAN type. The value common indicates a common VLAN.
  Ports: interfaces added to VLANs.

## Slide 40: Case2:Configuring Interface-based VLAN Assignment
Networking requirements:
  On the network shown in the left figure, the switches (SW1 and SW2) of an enterprise are connected to multiple PCs, and PCs in different departments need to access the server of the enterprise. To ensure communication security, the enterprise requires that PCs in different departments cannot directly communicate.
  To meet this requirement, configure interface-based VLAN assignment and hybrid interfaces on the switches to enable PCs in different departments to access the server but disable them from directly communicating at Layer 2.
Hybrid interface
PC1
PC2
Server
VLAN 10
VLAN 100
VLAN 20
PVID 10
PVID 1
PVID 1
GE 0/0/1
PVID 20
GE 0/0/2
PVID 100
GE 0/0/1
GE 0/0/3
GE 0/0/3
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
SW1
SW2
Notes: Configuration roadmap:
  Create VLANs and add interfaces connected to PCs to the VLANs to isolate Layer 2 traffic between PCs with different services.
  Configure interface types and specify permitted VLANs for SW1 and SW2 to allow PCs to communicate with the server through SW1 and SW2.

## Slide 41: Configuring Hybrid Interfaces (1)
SW1 configuration:
[SW1] vlan batch 10 20 100
[SW1] interface GigabitEthernet 0/0/1
[SW1-GigabitEthernet0/0/1] port link-type hybrid
[SW1-GigabitEthernet0/0/1] port hybrid pvid vlan 10
[SW1-GigabitEthernet0/0/1] port hybrid untagged vlan 10 100
[SW1-GigabitEthernet0/0/1] interface GigabitEthernet 0/0/2
[SW1-GigabitEthernet0/0/2] port link-type hybrid
[SW1-GigabitEthernet0/0/2] port hybrid pvid vlan 20
[SW1-GigabitEthernet0/0/2] port hybrid untagged vlan 20 100
[SW1-GigabitEthernet0/0/2] interface GigabitEthernet 0/0/3
[SW1-GigabitEthernet0/0/3] port link-type hybrid
[SW1-GigabitEthernet0/0/3] port hybrid tagged vlan 10 20 100
PC1
PC2
Server
VLAN 10
VLAN 100
VLAN 20
PVID 10
PVID 1
PVID 1
SW1
SW2
GE 0/0/1
PVID 20
GE 0/0/2
PVID 100
GE 0/0/1
GE 0/0/3
GE 0/0/3
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment

## Slide 42: Configuring Hybrid Interfaces (2)
SW2 configuration:
[SW2] vlan batch 10 20 100
[SW2] interface GigabitEthernet 0/0/1
[SW2-GigabitEthernet0/0/1] port link-type hybrid
[SW2-GigabitEthernet0/0/1] port hybrid pvid vlan 100
[SW2-GigabitEthernet0/0/1] port hybrid untagged vlan 10 20 100
[SW2-GigabitEthernet0/0/1] interface GigabitEthernet 0/0/3
[SW2-GigabitEthernet0/0/3] port link-type hybrid
[SW2-GigabitEthernet0/0/3] port hybrid tagged vlan 10 20 100
PC1
PC2
Server
VLAN 10
VLAN 100
VLAN 20
PVID 10
PVID 1
PVID 1
GE 0/0/1
PVID 20
GE 0/0/2
PVID 100
GE 0/0/1
GE 0/0/3
GE 0/0/3
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
SW1
SW2

## Slide 43: Verifying the Configuration
[SW1]display vlan
The total number of vlans is : 4
-----------------------------------------------------------------------------------------
U: Up; D: Down; TG: Tagged; UT: Untagged;
MP: Vlan-mapping; ST: Vlan-stacking;
#: ProtocolTransparent-vlan; *: Management-vlan;
-----------------------------------------------------------------------------------------
VID Type Ports
-----------------------------------------------------------------------------------------
1 common UT:GE0/0/1(U) GE0/0/2(U) GE0/0/3(U) ……
10 common UT:GE0/0/1(U)
TG:GE0/0/3(U)
20 common UT:GE0/0/2(U)
TG:GE0/0/3(U)
100 common UT:GE0/0/1(U) GE0/0/2(U)
TG:GE0/0/3(U)
……
PC1
PC2
Server
VLAN 10
VLAN 100
VLAN 20
PVID 10
PVID 1
PVID 1
GE 0/0/1
PVID 20
GE 0/0/2
PVID 100
GE 0/0/1
GE 0/0/3
GE 0/0/3
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
SW1
SW2

## Slide 44: Basic VLAN Configuration Commands
[Huawei-vlan10] mac-vlan mac-address mac-address [ mac-address-mask | mac-address-mask-length ]
Associate a MAC address with a VLAN.
This command associates a MAC address with a VLAN.
  mac-address: specifies the MAC address to be associated with a VLAN. The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits, such as 00e0 or fc01. If an H contains less than four digits, the left-most digits are padded with zeros. For example, e0 is displayed as 00e0. The MAC address cannot be 0000-0000-0000, FFFF-FFFF-FFFF, or any multicast address.
  mac-address-mask: specifies the mask of a MAC address. The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits.
  mac-address-mask-length: specifies the mask length of a MAC address. The value is an integer ranging from 1 to 48.
[Huawei-GigabitEthernet0/0/1] mac-vlan enable
Enable MAC address-based VLAN assignment on an interface.
This command enables MAC address-based VLAN assignment on an interface.
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Command: mac-vlan mac-address mac-address [ mac-address-mask | mac-address-mask-length ]
  mac-address: specifies the MAC address to be associated with a VLAN.
    The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits, such as 00e0 or fc01. If an H contains less than four digits, the left-most digits are padded with zeros. For example, e0 is displayed as 00e0.
    The MAC address cannot be 0000-0000-0000, FFFF-FFFF-FFFF, or any multicast address.
  mac-address-mask: specifies the mask of a MAC address.
    The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits.
  mac-address-mask-length: specifies the mask length of a MAC address.
    The value is an integer ranging from 1 to 48.
The mac-vlan enable command enables MAC address-based VLAN assignment on an interface.

## Slide 45: Example for Configuring MAC Address-based VLAN Assignment
Networking requirements:
  The network administrator of an enterprise assigns PCs in the same department to the same VLAN. To improve information security, the enterprise requires that only employees in the department be allowed to access the network resources of the enterprise.
  PCs 1 through 3 belong to the same department. According to the enterprise' requirement, only the three PCs can access the enterprise network through SW1.
  To meet this requirement, configure MAC address-based VLAN assignment and associate the MAC addresses of the three PCs with the specified VLAN.
SW1
PC1
PC2
PC3
001e-10dd-dd01
VLAN 10
GE 0/0/2
Enterprise
network
GE 0/0/3
GE 0/0/4
PC4
001e-10dd-dd02
001e-10dd-dd03
001e-10dd-dd04
GE 0/0/1
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Configuration roadmap:
  Create a VLAN, for example, VLAN 10.
  Add Ethernet interfaces on SW1 to the VLAN.
  Associate the MAC addresses of PCs 1 through 3 with the VLAN.

## Slide 46: Creating a VLAN and Associating MAC Addresses with the VLAN
Create a VLAN.
[SW1] vlan 10
[SW1-vlan10] quit
SW1
PC1
PC2
PC3
001e-10dd-dd01
VLAN 10
GE0/0/2
Enterprise
Network
GE0/0/3
GE0/0/4
001e-10dd-dd02
001e-10dd-dd03
GE0/0/1
Associate MAC addresses with the VLAN.
[SW1] vlan 10
[SW1-vlan10] mac-vlan mac-address 001e-10dd-dd01 [SW1-vlan10] mac-vlan mac-address 001e-10dd-dd02 [SW1-vlan10] mac-vlan mac-address 001e-10dd-dd03 [SW1-vlan10] quit
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment

## Slide 47: Adding Interfaces to the VLAN and Enabling MAC Address-based VLAN Assignment
Enable MAC address-based VLAN assignment on the specified interface.
[SW1] interface gigabitethernet 0/0/2
[SW1-GigabitEthernet0/0/2] mac-vlan enable
[SW1-GigabitEthernet0/0/2] quit
Note: The configuration of GE 0/0/3 and GE 0/0/4 is similar to that of GE 0/0/2.
SW1
PC1
PC2
PC3
001e-10dd-dd01
VLAN 10
GE0/0/2
Enterprise
Network
GE0/0/3
GE0/0/4
001e-10dd-dd02
001e-10dd-dd03
GE0/0/1
Add interfaces to the VLAN.
[SW1] interface gigabitethernet 0/0/1
[SW1-GigabitEthernet0/0/1] port link-type hybrid
[SW1-GigabitEthernet0/0/1] port hybrid tagged vlan 10
[SW1] interface gigabitethernet 0/0/2
[SW1-GigabitEthernet0/0/2] port link-type hybrid
[SW1-GigabitEthernet0/0/2] port hybrid untagged vlan 10
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: On access and trunk interfaces, MAC address-based VLAN assignment can be used only when the MAC address-based VLAN is the same as the PVID. It is recommended that MAC address-based VLAN assignment be configured on hybrid interfaces.

## Slide 48: Verifying the Configuration
[SW1]display vlan
The total number of vlans is : 2
-----------------------------------------------------------------------------------------------
U: Up; D: Down; TG: Tagged; UT: Untagged;
MP: Vlan-mapping; ST: Vlan-stacking;
#: ProtocolTransparent-vlan; *: Management-vlan;
-----------------------------------------------------------------------------------------------
VID Type Ports
-----------------------------------------------------------------------------------------------
1 common UT:GE0/0/1(U) GE0/0/2(U) GE0/0/3(U) ……
10 common UT:GE0/0/2(U) GE0/0/3(U) GE0/0/4(U)
TG:GE0/0/1(U)
……
[SW1]display mac-vlan mac-address all
----------------------------------------------------------------------
MAC Address MASK VLAN Priority
----------------------------------------------------------------------
001e-10dd-dd01 ffff-ffff-ffff 10 0
001e-10dd-dd02 ffff-ffff-ffff 10 0
001e-10dd-dd03 ffff-ffff-ffff 10 0
Total MAC VLAN address count: 3
Interface-based VLAN Assignment
MAC Address-based VLAN Assignment
Notes: Command: The display mac-vlan { mac-address { all | mac-address [ mac-address-mask | mac-address-mask-length ] } | vlan vlan-id } command displays the configuration of MAC address-based VLAN assignment.
  all: displays all VLANs associated with MAC addresses.
  mac-address mac-address: displays the VLAN associated with a specified MAC address.
    The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits.
  mac-address-mask: specifies the mask of a MAC address.
    The value is a hexadecimal number in the format of H-H-H. Each H contains one to four digits.
  mac-address-mask-length: specifies the mask length of a MAC address.
    The value is an integer ranging from 1 to 48.
  vlan vlan-id: specifies a VLAN ID.
    The value is an integer ranging from 1 to 4094.
Command output:
  MAC Address: MAC address
  MASK: mask of a MAC address
  VLAN: ID of the VLAN associated with a MAC address
  Priority: 802.1p priority of the VLAN associated with a MAC address

## Slide 49
(Multiple) Which of the following statements about the VLAN technology are incorrect? ( )
  The VLAN technology can isolate a large collision domain into several small collision domains.
  The VLAN technology can isolate a large Layer 2 broadcast domain into several small Layer 2 broadcast domains.
  PCs in different VLANs cannot communicate.
  PCs in the same VLAN can communicate at Layer 2.
If the PVID of a trunk interface is 5 and the port trunk allow-pass vlan 2 3 command is run on the interface, which VLANs' frames can be transmitted through the trunk interface?
Notes: AC
After the port trunk allow-pass vlan 2 3 command is run, the frames of VLAN 5 cannot be transmitted through the trunk interface. By default, the frames of VLAN 1 can be transmitted through the trunk interface. Therefore, the frames of VLANs 1 through 3 can all be transmitted through the interface.

## Slide 50
This course describes the VLAN technology, including the functions, identification, assignment, data exchange, planning, application, and basic configuration of VLANs.
The VLAN technology can divide a physical LAN into multiple broadcast domains so that network devices in the same VLAN can directly communicate at Layer 2, while devices in different VLANs cannot.