## Slide 1
HCDCA110
CE Switches
V2R9
2.00
Wangdong/wx270673
2016.10.27
Yanjiangang/00207709
New
Yuan Weihua/wx462781
2019.4.10
Liu Lican/00180730
Update

## Slide 2: Data Center Network Technology Application Basis
Huawei Data Center Series of Courses

## Slide 3
This course introduces the most basic networking technologies in the data center.
The principle of VLAN (Virtual Local Area Network) technology, and the application of VLAN technology in the network.
The basic principles and application scenarios of link aggregation.
The basic principles and applications of OSPF unicast routing protocols.
The basic principles and application scenarios of BGP.
Notes: As the network scale expands increasingly, users propose increasingly high requirements on Ethernet backbone network bandwidth and reliability. Originally, to increase the bandwidth, users use high-speed cards or devices supporting high-speed interface cards to replace old interface cards or devices. This solution, however, is costly and inflexible.
Link aggregation helps increase bandwidth by bundling a group of physical interfaces into a single logical interface, without having to upgrade hardware. In addition, link aggregation provides link backup mechanisms, greatly improving link reliability.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the principle of VLAN technology
  Describe the different port link types and characteristics
  Describe the functions and purpose of link aggregation
  Understand the basic principles of LACP
  Understand the basic principles of OSPF
  Describe the route calculation process of link state algorithm
  Describe the establishment of BGP neighbor relationships

## Slide 5
VLAN technology
  VLAN overview
  VLAN principle description
  Inter-VLAN communication
Link aggregation technology
OSPF protocol
BGP protocol

## Slide 6
No broadcast domain to manage expanding local networks.
LAN Limitations
Notes: As local networks expand, traffic increases and broadcasts become more common. There are no real boundaries within such an expanding network, causing interrupts and growing traffic utilization to occur. Traditionally, the alternative option was to implement a layer three device within the local network to generate broadcast domains, however in doing so additional expense was incurred and the forwarding behavior of such devices did not provide as efficient throughput as found with switches, leading to bottlenecks at transit points between broadcast domains.

## Slide 7
A VLAN enables logical isolation of traffic at the data link layer.
VLAN Technology
VLAN 1
VLAN 2
Notes: The principle of VLAN technology was introduced that enabled traffic isolation at the data link layer. VLAN technology has the added advantage of traffic isolation without the limitation of physical boundaries. Users can be physically dispersed but still be associated as part of a single broadcast domain, logically isolating users from other user groups at the data link layer. Today VLAN technology is applied as a solution to a variety of challenges.

## Slide 8
The virtual local area network (VLAN) technology groups devices on a physical LAN into different logical LAN segments.
What is VLAN
SWA
SWC
VLAN 2
SWB
VLAN 1
VLAN 3
Notes: Devices in a VLAN can directly communicate with each other, whereas devices in different VLANs cannot directly communicate with each other. Broadcast packets are forwarded within a VLAN, improving network security. For example, if different enterprise users located in the same business building construct their LANs separately, the investment is high; if these enterprise users share the same LAN of the business building, the information security cannot be ensured. If the VLAN technology is used, these enterprises can share the LAN resources without risks to their private information.
The preceding networking diagram shows a typical VLAN application network. SwitchA, SwitchB, and SwitchC are placed in different floors of a building. Each switch is connected to three PCs that belong to different VLANs.

## Slide 9
VLAN technology
  VLAN overview
  VLAN principle description
  Inter-VLAN communication
Link aggregation technology
OSPF protocol
BGP protocol

## Slide 10
CRC
DATA
TYPE
SA
DA
Format of the VLAN Frame
CRC
DATA
TYPE
SA
DA
TAG
Traditional Ethernet data frame
IEEE 802.1Q tagged frame format
PRI
VLAN ID
CFI
0x8100
TPID
TCI
Notes: The 802.1Q tag including the following fields:
TPID
Tag Protocol Identifier (TPID), indicating the frame type. The value 0x8100 indicates an 802.1Q-tagged frame. An 802.1Q-incapable device discards the 802.1Q frames.
IEEE 802.1Q protocol defines the value of the field as 0x8100. However, manufacturers can define their own TPID values and users can then modify the value to realize interconnection of devices from different manufacturers.
PRI
Priority. The length is 3 bits. The value ranges from 0 to 7. A larger value indicates a higher priority. If congestion occurs, the switch sends packets with higher priorities first.
CFI
Canonical Format Indicator (CFI). The length is 1 bit. This field indicates whether the MAC address is in the canonical format. If the CFI field is 0, the MAC address is in the canonical format. If the CFI field is 1, the MAC address is in the non-canonical format. This field is used to identify the Ethernet frame, fiber distributed digital interface (FDDI) frame, and token ring frame. The CFI field is 0 in the Ethernet frame.
VID
VLAN ID. The field is 12 bits. This field indicates to which VLAN the frame belongs. On S series mid-range and low-end switch, the value of the field ranges from 0 to 4095. VLAN IDs 0 and 4095 are reserved and unavailable to users.

## Slide 11
A trunk represents a backbone for the transmission of VLAN traffic between switches.
Link Types
Trunk
Access
VLAN3
VLAN2
Trunk
Trunk
Access
Access
Access
Access
Notes: Ethernet links fall into the following types, depending on the number of allowed VLANs:
  Access link: An access link can transmit data frames of only one VLAN. It connects a switch to a user terminal, such as a host, server, and simplified Layer 2 switch. Generally, user terminals do not need to know the VLANs to which they belong and cannot identify tagged frames; therefore, only untagged frames are transmitted along an access link.
  Trunk link: A trunk link can transmit data frames from multiple VLANs. It connects a switch to another switch or a router. Frames on a trunk link must be tagged so that other network devices can correctly identify VLAN information in the frames.

## Slide 12
PVID represents the default VLAN for each interface.
The PVID is set to VLAN 1 for all ports by default.
PVID
PVID1
PVID2
PVID2
PVID3
PVID3
PVID1
SWA
SWB
Host A
Host C
Host B
Host D
VLAN2
VLAN2
VLAN3
VLAN3
Notes: The default VLAN ID of an interface is called the port default VLAN ID (PVID). Frames processed in a switch all carry VLAN tags. When the switch receives an untagged frame, it adds a VLAN tag to the frame according to the default VLAN of the interface that receives the frame. The PVID is used in the following scenarios:
  When an interface receives an untagged frame, the interface adds a tag with the PVID to the frame and sends the frame to the switch for processing. When an interface receives a tagged frame, the switch does not add a tag with the PVID to the frame.
  When an interface sends a frame in which the VLAN ID is the same as the PVID, the switch removes the tag from the frame before sending it out from the interface.

## Slide 13
An access interface often connects to a user terminal.
Access interfaces can only receive and send untagged frames, and can add only a unique VLAN tag to untagged frames.
Port Types - Access
Host A
Host C
Host B
Untagged
Untagged
PVID10
PVID10
PVID2
Frame
10
SWA
G0/0/1
G0/0/2
G0/0/3
Notes: An access interface often connects to a user terminal such as a user host or server that cannot identify VLAN tags, or is used when VLANs do not need to be differentiated. Access interfaces can only receive and send untagged frames, and can add only a unique VLAN tag to untagged frames.
An access interface has the following characteristics:
  Only the frame whose VLAN ID is the same as the PVID of the access interface is allowed..
  When the access interface receives an untagged frame, the switch adds the PVID of the interface to the frame.
  The access interface sends only untagged frames to the peer device.
In the example，upon receiving the frame, the switch will associate the frame with VLAN 10 based on the PVID of the interface. The switch is able to identify at the port interface the PVID and make a decision as to whether the frame can be forwarded. In the case of Host C the PVID matches the VLAN ID in the VLAN tag, for which the tag is removed and the frame forwarded. For Host B however the frame and the PVID differ, and therefore the frame is restricted from being forwarded to this destination.

## Slide 14
A trunk interface often connects to a switch, router, AP, or voice terminal.
It allows tagged frames from multiple VLANs and untagged frames from only one VLAN.
Port Types - Trunk
Host A
Host C
Host B
Host D
Untagged
Untagged
Frame
20
Untagged
SWA
SWB
Untagged
Untagged
PVID10
PVID20
PVID10
PVID20
PVID10
PVID10
Notes: A trunk interface often connects to a switch, router, AP, or voice terminal that can receive and send tagged and untagged frames simultaneously. It allows tagged frames from multiple VLANs and untagged frames from only one VLAN.
A trunk interface has the following features:
  A trunk interface allows tagged frames from multiple VLANs to pass through.
  If a tagged frame sent out through a trunk interface carries a VLAN ID that is the same as the default one of the interface, the switch removes the VLAN tag from the frame. It is because the PVID of each interface is unique. Only in this case, frames forwarded by the trunk interface are untagged.
  If a tagged frame sent out through a trunk interface carries a VLAN ID that is different from the default one of the interface, the switch directly forwards the frame without performing any other actions.
The example demonstrates a trunk interface assigned with a PVID of 10, for which it should be assumed that all VLANs are permitted to traverse the trunk link. Only frames associated with VLAN 10 will be forwarded without the VLAN tag, based on the PVID. For all other VLAN frames, a VLAN tag must be included with the frame and be permitted by the port before the frame can be transmitted over the trunk link. Frames associated with VLAN 20 are carried as tagged frames over the trunk link.

## Slide 15
A hybrid interface can connect to not only a user terminal or network device.
It allows tagged frames from multiple VLANs.
Port Types - Hybrid
PVID10
Host A
Host C
Host B
Host D
Untagged
PVID10
Frame
20
Untagged
SWA
SWB
Untagged
Untagged
PVID10
PVID20
PVID10
PVID20
Hybrid Untagged
Hybrid Tagged
Untagged
Frame
10
Notes: A hybrid interface can connect to not only a user terminal (such as a user host or server) or network device (such as a hub or simplified Layer 2 switch) that cannot identify tags, but also a switch, router, voice terminal, or AP that can receive and send tagged and untagged frames. It allows tagged frames from multiple VLANs. Frames sent out from a hybrid interface are tagged or untagged according to the VLAN configuration.
Ports which are considered untagged will generally receive untagged frames from end systems, and be responsible for adding a tag to the frame based on the Port VLAN ID (PVID) of the port. One of the key differences is in the hybrid port’s ability to selectively perform the removal of VLAN tags from frames that differ from the PVID of the port interface. In the example, Host D is connected to a port which specifies a Port VLAN ID of 20, whilst at the same time is configured to allow for the removal of the tag from frames received from VLAN 10, thereby allowing Host D to receive traffic from both VLANs 10 & 20.
Hybrid Ports that are tagged will operate in a similar manner as a regular trunk interface, however one major difference exists. VLAN frames that both match the PVID and are permitted by the port will continue be tagged when forwarded.

## Slide 16
Assignment Method | VLAN 5 | VLAN 10
Port based | G0/0/1, G0/0/7 | G0/0/2 G0/0/9
MAC based | 00-01-02-03-04-AA 00-01-02-03-04-CC | 00-01-02-03-04-BB 00-01-02-03-04-DD
IP Subnet based | 10.0.1.* | 10.0.2.*
Protocol based | IP | IPX
Policy based | 10.0.1.* + G0/0/1+ 00-01-02-03-04-AA | 10.0.2.* + G0/0/2 + 00-01-02-03-04-BB
G0/0/1
Host A
10.0.1.1
Host D
10.0.2.2
Host B
10.0.2.1
Host C
10.0.1.2
G0/0/2
G0/0/7
G0/0/9
SWA
Five methods of VLAN assignment are possible.
Port based VLAN assignment is the default assignment method.
VLAN Assignment Methods
Notes: VLAN assignment can be implemented based on one of five different methods, including Port based, MAC based, IP Subnet based, Protocol based and Policy based implementations. The port based method represents the default and most common method for VLAN assignment. Using this method, VLANs are classified based on the port numbers on a switching device. The network administrator configures a Port VLAN ID (PVID), representing the default VLAN ID for each port on the switching device. When a data frame reaches a port, it is marked with the PVID if the data frame carries no VLAN tag and the port is configured with a PVID. If the data frame carries a VLAN tag, the switching device will not add a VLAN tag to the data frame even if the port is configured with a PVID.
Using the MAC address assignment method, VLANs are classified based on the MAC addresses of network interface cards (NICs). The network administrator configures the mappings between MAC addresses and VLAN IDs. In this case, when a switching device receives an untagged frame, it searches the MAC-VLAN table for a VLAN tag to be added to the frame according to the MAC address of the frame. For IP subnet based assignment, upon receiving an untagged frame, the switching Device adds a VLAN tag to the frame based on the IP address of the packet header.

## Slide 17
Notes: Where VLAN classification is based on protocol, VLAN IDs are allocated to packets received on an interface according to the protocol (suite) type and encapsulation format of the packets. The network administrator configures the mappings between types of protocols and VLAN IDs. The Policy based assignment implements a combination of criteria for assignment of the VLAN tag, including the IP subnet, port and MAC address, in which all criteria must match before the VLAN is assigned.

## Slide 18
VLAN technology
  VLAN overview
  VLAN principle description
  Inter-VLAN communication
Link aggregation technology
OSPF protocol
BGP protocol

## Slide 19
Attempts to limit broadcast domain size through VLAN implementation isolates users.
VLAN Disadvantages
VLAN 100
SWA
VLAN 200
Notes: The general principle of VLAN implementation is to isolate networks as a means of minimizing the size of the existing broadcast domain, however in doing so, many users are cut off from other users within other VLAN domains and require that layer three (IP) communication be established in order for those broadcast domains to re-establish communication through reachable routes. The implementation of a layer three switch offers an ideal means for supporting VLAN routing whilst reducing operating costs. One of the constraints however of VLAN routing is the need for strict IP address management.
Generally however the VLAN routing principle is applicable to small scale networks on which users belong to different network segments and IP addresses of users are seldom changed.

## Slide 20
Flows between different VLANs cannot directly cross VLAN boundaries, we can use routers so that messages can be forwarded from one VLAN to another VLAN.
Inter-VLAN Communication
SWA
RTA
Host A
Host B
VLAN 2
VLAN 3
Notes: Flows between different VLANs cannot directly cross VLAN boundaries, and route is needed to forward packet from one VLAN to another VLAN.

## Slide 21
A single trunk supports VLAN routes by using sub-interfaces.
Route Selection in Inter-VLAN Communication
Host A
SWA
Host B
VLAN Trunk
G0/0/1.1
G0/0/1.2
VLAN 2
VLAN 3
GW:192.168.2.254
GW:192.168.3.254
RTA
192.168.2.254
192.168.3.254
Notes: In order to allow communication over a single trunk interface, it is necessary to logically segment the physical link using sub-interfaces. Each sub-interface represents a logical link for the forwarding of VLAN traffic before being routed by the router via other logical sub-interfaces to other VLAN destinations. Each sub-interface must be assigned an IP address in the same network segment as the VLAN that it is created for as well as 802.1Q encapsulation to allow for VLAN association as traffic is routed between VLANs.
It is also necessary to configure the type of the Ethernet port of the switch that connects to the router as either a Trunk or Hybrid link type, and allow frames of the associated VLANs (VLAN 2 & VLAN 3 in this case) to pass.

## Slide 22
VLANIF are used by each VLAN as a route gateway.
L3 Switch Based VLAN Routing
Host A
Host D
Host B
Host C
VLAN 2
VLAN 3
GW:192.168.2.254
GW:192.168.3.254
GW:192.168.2.254
GW:192.168.3.254
VLANIF 2: 192.168.2.254/24
VLANIF 3: 192.168.3.254/24
SWA
Notes: The implementation of L3 switches brings about benefits to the process of VLAN routing that are not possible through the use of a router. One of those features is the ability to forward VLAN traffic with very little delay due to support of what is known as line speed forwarding as a result of bottom layer ASIC chips that allow traffic to be forwarded based on hardware rather than software. Along with this is the fact that a single device is used with no trunk link that may otherwise face congestion under heavy traffic loads. VLAN routing when using a layer 3 switch relies on the implementation of VLAN interfaces (VLANIF). If multiple users on a network belong to different VLANs, each VLAN requires a VLANIF that acts as the VLAN gateway and so must associate with an IP address relevant to the network of the VLAN. If a large number of VLANs exist however, this can tally up to a large number of IP addresses being required to support each VLANIF, as well as the hosts that are part of the VLAN with which the VLANIF is associated. Through the VLANIF, routing between different VLANs can be supported.

## Slide 23
VLAN technology
Link aggregation technology
  Basic concepts of link aggregation
  Link aggregation modes
  Application environments of link aggregation
OSPF protocol
BGP protocol

## Slide 24
If there are multiple links which are in the same broadcast domain between 2 switches, what will happen?
If STP is enabled, will these links be in forwarding state?
Link Aggregation Background
SWA
SWB
Notes: Multiple links between 2 switches will cause the broadcast storm.
If STP is enabled, there will be only one link in forwarding state.

## Slide 25
Ethernet link aggregation, also called Eth-Trunk, bundles multiple physical links to form a logical link to increase link bandwidth.
The bundled links back up each other, increasing reliability.
Basic Concepts of Link Aggregation
SWA
SWB
Eth-Trunk
Notes: LAG and LAG interface
  A link aggregation group (LAG) is a logical link bundled by multiple Ethernet links.
  Each LAG corresponds to a logical interface, that is, link aggregation interface or Eth-Trunk. The Eth-Trunk can be used as a common Ethernet interface. The only difference between the Eth-Trunk and common Ethernet interface is that the Eth-Trunk needs to select one or more member interfaces to forward traffic.
Active and inactive interfaces and links
  There are two types of interfaces in an LAG: active interface that forwards data and inactive interface that does not forward data.
  The link connected to an active interface is the active link, whereas the link connected to an inactive interface is the inactive link.

## Slide 26
Increased bandwidth
  The bandwidth of the link aggregation interface is the sum of bandwidth of member interfaces.
Higher reliability
  When an active link fails, traffic on this active link is switched to another active link, improving reliability of the link aggregation interface.
Load balancing
  In a link aggregation group (LAG), traffic is load balanced among active links of member interfaces.
Advantages of Link Aggregation
Notes: Before deploying link aggregation, if we want networks connected by 100 Mb/s interfaces to achieve faster transmission rate, we need to replace the physical hardware(like 1000 Mb/s interfaces). But this method may cost high which doesn’t apply to medium and small enterprise networks. We can use link aggregation to aggregate several interfaces together. In this way we can reduce the cost and fulfill the requirements of increasing interface bandwidth.
Meanwhile, there are more than one interface members in one aggregation link. When there is one member down, it will not cause the whole link to get down, which largely increase the reliability of the network.

## Slide 27
VLAN technology
Link aggregation technology
  Basic concepts of link aggregation
  Link aggregation modes
  Application environments of link aggregation
OSPF protocol
BGP protocol

## Slide 28
Based on whether LACP is used or not, link aggregation can be classified into manual mode and LACP mode.
Link Aggregation Modes
Manual Mode
LACP Mode
Active
Backup
SWA
SWB
SWA
SWB

## Slide 29
An Eth-Trunk is created between SWA and SWB. In manual mode, three active links participate in data forwarding and load balance traffic.
Link Aggregation in Manual Mode
Eth-trunk
Eth-trunk
SWA
SWB
SWA
SWB
A%
B%
C%
D%
E%
A%+B%+C%=100%
D%+E%=100%
Notes: In manual mode, you must manually create an Eth-Trunk and add member interfaces to the Eth-Trunk. In this mode, LACP is not required. The manual mode applies to the scenario where a high link bandwidth between two directly connected devices is required but the remote device does not support the LACP protocol. This mode can increase bandwidth, enhance reliability, and implement load balancing.
As shown in the above figure, an Eth-Trunk is created between SWA and SWB. In manual mode, three active links participate in data forwarding and load balance traffic. When one link becomes faulty, the remaining two links load balance traffic.

## Slide 30
In manual mode, can SWA detect the fault when an member interface on SWA is incorrectly connected to an interface on SWC?
Limitation of Manual Mode
SWA
SWB
Eth-Trunk
SWC
Notes: An Eth-Trunk in manual mode can increase the bandwidth. However, the manual mode can only detect member link disconnections, but cannot detect other faults such as link layer faults and incorrect link connections.
For example, in the above figure, four interfaces on SWA are bundled into an Eth-Trunk and the Eth-Trunk is connected to the corresponding interfaces on SWB. Because an interface on SWA is incorrectly connected to an interface on SWC, SWA may incorrectly send data destined for SWB to SWC. However, the Eth-Trunk in manual mode cannot detect this fault in a timely manner.
If LACP is enabled on SWA and SWB, the Eth-Trunk correctly selects active links to forward data after negotiation. Data sent by SWA can reach SWB.

## Slide 31
The Link Aggregation Control Protocol (LACP) can improve fault tolerance of the Eth-Trunk, provide backup, and ensure high reliability of member links.
Link Aggregation in LACP Mode
LACP Mode
Active
Backup
SWA
SWB
Notes: LACP uses a standard negotiation mechanism for a switching device so that the switching device can create and start the aggregated link based on its configuration. After the aggregated link is created, LACP maintains the link status. If an aggregated link's status changes, LACP adjusts or removes the link.
In LACP mode, LACP is used to negotiate parameters to determine active links in an LAG. This mode is also called the M:N mode, where M refers to the number of active links and N refers to the number of backup links. This mode guarantees high reliability and allows traffic to be load balanced among M active links.
  As shown in the above figure, M+N links with the same attributes (in the same LAG) are set up between two devices. When data is transmitted over the aggregated link, traffic is load balanced among M active links and no data is transmitted over N backup links. Therefore, the actual bandwidth of the aggregated link is the sum of the M links' bandwidth, and the maximum bandwidth of the aggregated link is the sum of the M+N links' bandwidth.
  If one of M links fails, LACP selects a link from N backup links to replace the faulty link. The actual bandwidth of the aggregated link is still the sum of M links' bandwidth, but the maximum bandwidth of the aggregated link is the sum of the (M+N-1) links' bandwidth.

## Slide 32
Notes:   M:N backup is mainly applied in situations where the bandwidth of M links must be assured and a fault tolerance mechanism is in place. If an active link fails, the system selects the backup link with the highest priority as the active link.If no available backup link is found and the number of active links is smaller than the lower threshold for the number of active interfaces, the system shuts down the LAG.

## Slide 33
LACP, as specified in IEEE 802.3ad, implements dynamic link aggregation and de-aggregation.
LACP allows both ends to exchange Link Aggregation Control Protocol Data Units (LACPDUs).
Implementation of LACP Mode
Notes: After member interfaces are added to an Eth-Trunk in LACP mode, each end sends LACPDUs to inform its remote end of its system priority, MAC address, member interface priorities, interface numbers, and keys. The remote end then compares this information with that saved on itself, and selects which interfaces to be aggregated. The two ends perform LACP negotiation to select active interfaces and links.
Active and inactive interfaces and links
  There are two types of interfaces in an LAG: active interface that forwards data and inactive interface that does not forward data.
  The link connected to an active interface is the active link, whereas the link connected to an inactive interface is the inactive link.
  Only when active interfaces fail, can inactive interfaces become new active interfaces.
LACP system priority
  LACP system priorities are set on devices at both ends of an Eth-Trunk. In LACP mode, active member interfaces selected by both devices must be consistent; otherwise, an LAG cannot be established. To keep active member interfaces consistent at both ends, set a higher priority for one end so that the other end selects active member interfaces based on the selection of the end with a higher priority. The smaller the LACP system priority value, the higher the LACP system priority.

## Slide 34
Notes: LACP interface priority
  Interface LACP priorities are set to prioritize interfaces of an Eth-Trunk. Interfaces with higher priorities are selected as active interfaces. The smaller the LACP interface priority value, the higher the LACP interface priority.
Upper threshold for the number of active interfaces
  When the number of active interfaces reaches this threshold, the bandwidth of an Eth-Trunk will not increase even if more member links go Up. This guarantees higher network reliability. When the number of active member interfaces reaches the upper threshold, additional active member interfaces are set to Down.
  For example, 8 trouble-free member links are bundled into an Eth-Trunk link and each link provides a bandwidth of 1 Gbit/s. The Eth-Trunk link only needs to provide a maximum bandwidth of 5 Gbit/s. You can set the maximum number of Up member links to 5 or larger. Then any unselected Up links automatically enter the backup state, improving reliability.
  NOTE: The upper threshold for the number of active interfaces is inapplicable to the manual load balancing mode.
Lower threshold for the number of active interfaces
  When the number of active interfaces falls below this threshold, an Eth-Trunk goes Down. This guarantees the Eth-Trunk a minimum available bandwidth.
  For example, if the Eth-Trunk is required to provide a minimum bandwidth of 2 Gbit/s and each member link's bandwidth is 1 Gbit/s, the minimum number of Up member links must be set to 2 or larger.

## Slide 35
Devices at both ends send LACPDUs to each other.
  As shown in the figure, you need to create an Eth-Trunk in LACP mode on SWA and SWB and add member interfaces to the Eth-Trunk. Then the member interfaces are enabled with LACP, and devices at both ends can send LACPDUs to each other.
Eth-Trunk Setting Up Process in LACP Mode (1)
SWA
SWB
LACPDU
LACPDU

## Slide 36
Devices at both ends determine the Actor and active links.
Eth-Trunk Setting Up Process in LACP Mode (2)
SWA
SWB
SWA
SWB
1
2
3
1
The device with higher system priority
LACP port priority
LACP port priority
LACP port priority
LACP port priority
The device with lower system priority
SWA
SWB
1
2
3
LACP port priority
LACP port priority
Actor
Compare system priority and determine the Actor
The Actor determines active links
3
2
1
2
3
3
2
1
3
2
1
Notes: As shown in the figure, devices at both ends receive LACPDUs from each other. For example, when SWB receives LACPDUs from SWA, SWB checks and records information about SWA and compares system priorities. If the system priority of SWA is higher than that of SWB, SWA acts as the Actor. If SWA and SWB have the same system priority, the device with a smaller MAC address functions as the Actor.
After devices at both ends select the Actor, they select active interfaces according to the priorities of the Actor's interfaces. Then active interfaces are selected, active links in the LAG are specified, and load balancing is implemented among these active links.

## Slide 37
Comparisons Between Link Aggregation Modes
Item | Manual Mode | LACP Mode
Definition | You must manually create an Eth-Trunk and add member interfaces to the Eth-Trunk. | An Eth-Trunk is created based on LACP. LACP provides a standard negotiation mechanism for a switching device.
Data forwarding | All links are active links. All active links participate in data forwarding. | Some links are active links. All active links participate in data forwarding. If an active link fails, the system selects a link among inactive links as the active link.
Fault detection | This mode can only detect member link disconnections. | This mode can detect member link disconnections and other faults such as link layer faults and incorrect link connections.

## Slide 38
Member interfaces cannot be configured with some services or static MAC address entries.
An Eth-Trunk cannot be added to another Eth-Trunk.
Member interfaces of an Eth-Trunk must use the same Ethernet type and rate.
Both devices of the Eth-Trunk must use the same number of physical interfaces, interface rate, duplex mode, and flow control mode.
Both devices of an Eth-Trunk must use the same link aggregation mode.
When the number of active interfaces falls below the lower threshold, the Eth-Trunk goes Down.
Configuration Notes Before an Eth-Trunk Is Configured
Notes: Member interfaces cannot be configured with some services or static MAC address entries. For example, when an interface is added to an Eth-Trunk, the interface must use the default link type.
Interfaces that use different Ethernet types and rates cannot join the same Eth-Trunk. For example, GE and FE interfaces cannot join the same Eth-Trunk, and GE electrical and optical interfaces can join the same Eth-Trunk.
If an interface of the local device is added to an Eth-Trunk, an interface of the remote device directly connected to the interface of the local device must also be added to an Eth-Trunk so that the two ends can communicate.

## Slide 39
VLAN technology
Link aggregation technology
  Basic concepts of link aggregation
  Link aggregation modes
  Application environments of link aggregation
OSPF protocol
BGP protocol

## Slide 40
Switches Are Directly Connected Using Link Aggregation
Access
Aggregation
Eth-Trunk1
…
…
Core
DATA
IPTV
VoIP
Notes: As shown in the above figure, traffic of services with different priorities is sent to the Internet through the access, aggregation and core layer devices. To ensure the bandwidth and reliability of the link between the aggregation and core layer devices, an LAG, Eth-Trunk 1, is established.
You can determine the working mode for the Eth-Trunk according to the following situations:
  If devices at both ends of the Eth-Trunk support LACP, the LACP mode is recommended.
  If the device at either end of the Eth-Trunk does not support LACP, you must use the manual mode.
QoS can be implemented on an Eth-Trunk as a common interface. At both ends of Eth-Trunk 1, traffic shaping, congestion management, and congestion avoidance can be performed for outgoing traffic, ensuring that packets of high priorities are sent in a timely manner.

## Slide 41
To improve the server bandwidth and reliability, two or more network adapters of the server are aggregated to form a network adapter group to implement load balancing or redundancy.
A Switch Connects to a Server Using Link Aggregation
Server
Eth-Trunk1
Switch
Network
Notes: Network adapters of the server must use the same type.
The link aggregation modes on the server and access device must be consistent.Intel network adapter is used as an example. A server often uses static or IEEE 802.3ad dynamic link aggregation. When the server uses static link aggregation, the access device must use the manual mode. When the server uses IEEE 802.3ad dynamic link aggregation, the access device must use the LACP mode.

## Slide 42
A Switch Connects to a Stack Using Link Aggregation
Access
Aggregation
Eth-Trunk1
Core
VLAN3
CSS
VLAN2
Notes: As shown in the above figure, the switch connects to a stack using link aggregation, and the Eth-Trunk is enabled to preferentially forward local traffic. Preferentially forwarding local traffic ensures reliable transmission, reduces the bandwidth burden between CSS devices, and improves the forwarding efficiency.

## Slide 43
VLAN technology
Link aggregation technology
OSPF protocol
  OSPF protocol overview
  Basic OSPF concepts
  OSPF neighbor and adjacency relationship
BGP protocol

## Slide 44
Supporting Classless Inter-Domain Routing (CIDR)
Free of routing loops
Fast convergence
Sending and receiving protocol data by using IP multicast
Supporting equal-cost routes
Supporting protocol packet authentication
Basic Characteristics of OSPF
Notes: Supporting Classless Inter-Domain Routing (CIDR)
As a routing protocol specially developed for TCP/IP environments, OSPF explicitly supports CIDR and Variable-Length Subnet Mask (VLSM).
Free of routing loops
OSPF calculates routes based on detailed link state information, namely, network topology information, to generate a shortest path tree (SPT) rooted on the local router. Therefore, the routes calculated by OSPF are loop-free.
Fast convergence
OSPF is based on triggered updates. Once a topological change occurs, the new link state information is flooded. Therefore, OSPF is sensitive to topological changes and converges quickly.
Sending and receiving protocol data by using IP multicast
OSPF routers send and receive protocol data by using multicast and unicast. Therefore, the network traffic generated is very low.
Supporting equal-cost routes
When multiple equal-cost paths exist to the same destination address, the traffic is evenly distributed on these equal-cost paths.
Supporting protocol packet authentication
All the packets exchanged between OSPF routers are authenticated. This ensures network security at the protocol level.

## Slide 45
Route Calculation Using the Link State Algorithm
Notes: OSPF route calculation is based on the link state algorithm. Before studying the OSPF routing protocol, you need to understand the process of route calculation using the link state algorithm.
1. Adjacency establishment
OSPF adjacencies are established among neighboring OSPF routers. The routers exchange LSAs only after adjacencies are established among them.
2. LSDB synchronization
After adjacencies are established, each router sends LSAs to its neighbors, receives LSAs from its neighbors, and sends the LSAs received from other routers to its neighbors. Each router stores received LSAs. All the LSAs build an LSDB.
3. Route calculation
After LSDB synchronization, each OSPF router, with itself as the root, runs the SPF algorithm to generate an SPT rooted on the router.
4. Routing table generation
According to the SPF tree, each router calculates routing information respectively and adds the routing information to its routing table.

## Slide 46
VLAN technology
Link aggregation technology
OSPF protocol
  OSPF protocol overview
  Basic OSPF concepts
  OSPF neighbor and adjacency relationship
BGP protocol

## Slide 47
In OSPF, an AS refers to a group of routers that exchange routing information by running the same routing protocol.
In this example, all the routers run OSPF and belong to the same AS.
AS (Autonomous System)
OSPF
Notes: An IGP runs within a certain scope. And this scope is named as AS (Autonomous System). As an IGP, OSPF runs within ASs.
Autonomous System ( AS )is a set of routers that exchange routing information using the same routing protocol.

## Slide 48
A router ID is a 32-bit integer that uniquely identifies an OSPF router in an AS. The format of a router ID is the same as that of an IP address.
In this example, run the router id 1.1.1.1 command to configure the router ID of the router as 1.1.1.1. After the router ID is configured, run the display router id command. The command output information shows that the router ID of the router is 1.1.1.1.
Router ID
[Quidway]router id 1.1.1.1
[Quidway]display router id
RouterID:1.1.1.1
Notes: During OSPF route calculation, each OSPF router needs to save the link state information about all the routers on the network. To distinguish the link state information about different routers in an LSDB, each router on the network is uniquely identified by a route ID in the LSDB.
A router ID can be configured manually. If no router ID is specified by using a command, the system automatically selects one of the existing interface IP addresses as the router ID.
The principle of selecting a router ID is as follows:
The highest IP address among the loopback addresses is preferentially selected as the router ID.
If no loopback interface is configured, the highest IP address among the physical interface addresses is selected as the router ID.
A new router ID is selected only after the interface IP address selected as the router ID is deleted.
It is recommended to use loopback 0 address as the router ID of a router.

## Slide 49
An OSPF cost is a 16-bit unsigned integer ranging from 1 to 65535.
  By default, the cost of an interface is calculated as 108/BW(bps)
  The cost of an OSPF interface can be configured manually
  Bandwidth reference values are configurable. When configuring bandwidth reference values, ensure that the bandwidth reference values of all the routers running the OSPF process are the same.
Cost
[Quidway-Ethernet0/0]ospf cost 100
[Quidway]ospf
[Quidway-ospf-1]bandwidth-reference 1000
Notes: If no cost is directly configured for an OSPF interface, OSPF automatically calculates the cost of the interface according to the bandwidth of the interface. The formula for calculating an interface cost is: interface cost = bandwidth reference value/interface bandwidth. The integer part of the result is used as the interface cost (if the result is less than 1, the interface cost is 1). You can change the interface cost by changing the bandwidth reference value.

## Slide 50
OSPF Area (1)
Area 0
Area 1
Area 2
Area 3
Area 4
Area 0 is Backbone area, for ABR at least one interface belongs to Area 0.
12.1.1.0/30
Notes: If OSPF is enabled on all the routers on a large network and the number of routers on the network keeps increasing, the following problems occur:
1.All the routers generate LSAs respectively and the LSDBs become very large. Therefore, LSDB synchronization takes long and occupies much memory space.
2.The running of the SPF algorithm is more complicated and occupies more CPU resources.
3.When the network size grows, the probability of topological changes also increases. As a result, a large number of OSPF packets are transferred on the network. This lowers the bandwidth utilization of the network.
4.Moreover, each change causes route recalculations on all the routers on the network.
OSPF solves these problems by dividing an AS into areas.
An area is a logical group of routers and is identified by an area ID. A network segment (link) belongs to only one area. In other words, the area to which an OSPF interface belongs must be specified.

## Slide 51
OSPF Area (2)
Area 0
Area 1
Area 2
Area 3
Area 4
12.1.1.0/30
[Quidway]ospf
[Quidway-ospf-1]area 2
[Quidway-ospf-1-area-0.0.0.2]network 12.1.1.0 0.0.0.3
Notes: 1.Area 0 is the backbone area. The backbone area is responsible for advertising the routing information (not detailed link state information) summarized by area boarder routers (ABRs) between non-backbone areas.
2.To prevent inter-area routing loops, OSPF disallows direct inter-area routing information advertisement between non-backbone areas. Therefore, an ABR must have at least one interface to the area 0. That is, each non-backbone area must be connected to the backbone area.
3.Each area has an LSDB unique to the area. A router maintains a separate LSDB for each area to which the router is connected. Detailed link state information is not advertised outside any area. Therefore, LSDB sizes are greatly reduced.

## Slide 52
OSPF Router Roles
Area 0
Area 1
Area 2
IR
ABR
BR
ASBR
Import ISIS route
ABR
Notes: Internal router (IR)
An IR is a router with all directly connected networks belonging to the same area. IRs that belong to the same area maintain the same LSDB.
Area border router (ABR)
An ABR is a router directly connected to multiple areas. An ABR maintains an LSDB for each area to which the ABR is directly connected.
Backbone router
A backbone router is a router that has at least one interface (or virtual link) to the backbone area. Backbone routers include all the ABRs and the routers with all their interfaces directly connected to the backbone area.
AS boundary router (ASBR)
An ASBR is a router that exchanges routing information with routers belonging to other ASs. An ASBR advertises AS-external routes throughout the entire AS.
An ASBR can be an IR or ABR. An ASBR can belong to or does not belong to the backbone area.

## Slide 53
VLAN technology
Link aggregation technology
OSPF protocol
  OSPF protocol overview
  Basic OSPF concepts
  OSPF neighbor and adjacency relationship
BGP protocol

## Slide 54
OSPF Packet Types
Type | Packet name | Packet function
1 | Hello | Discover /maintain neighbor
2 | Database Description | Summarize database contents
3 | Link State Request | Database download
4 | Link State Update | Database update
5 | Link State Ack | Flooding acknowledgement
Notes: There are five types of OSPF packets. By exchanging protocol packets, OSPF routers establish neighbor relationships among them and exchange link state information to complete route calculation. This section describes the functions of OSPF packets.
Hello packets are used to discover neighbors and maintain neighbor relationships.
Database description (DD) packets summarize link states by carrying LSA header information.
Link state (LS) request packets are used to request the LSAs that are discovered by receiving DD packets but not available on the local router.
Detailed LSAs are sent in LS Update packets to synchronize LSDBs.
LS Ack packets are flooded to guarantee reliable routing information exchange.

## Slide 55
OSPF Packet Header Authentication-Interface Authentication
Configure simple password "huawei"
Loopback0
1.1.1.1/32
RTA
RTB
Loopback0
2.2.2.2/32
E0/0
E0/0
10.1.1.1/30
.2
Area 1
[RTA-Ethernet0/0]ospf authentication-mode simple plain huawei
[RTB-Ethernet0/0]ospf authentication-mode simple plain huawei
Notes: OSPF supports packet header authentication to guarantee OSPF security. OSPF packets are accepted only after being authenticated. If the OSPF packet authentication fails, no neighbor relationship can be established.
The versatile routing platform (VRP) supports two authentication modes: area authentication and interface authentication. When area authentication is used, the authentication modes and passwords of all the routers belonging to the same area must be the same in the area. For example, for all the routers belonging to area 0, the authentication mode is configured as simple authentication and the password as abc. If both area authentication and interface authentication is configured, interface authentication is used preferentially.

## Slide 56
OSPF Packet Header Authentication-Area Authentication
[RTA-ospf-1-area-0.0.0.1]authentication-mode simple plain huawei
[RTB-ospf-1-area-0.0.0.1]authentication-mode simple plain huawei
Loopback0
1.1.1.1/32
RTA
RTB
Loopback0
2.2.2.2/32
E0/0
E0/0
10.1.1.1/30
.2
Area 1
Configure simple password "huawei"

## Slide 57
What Is Neighbor? What Is Adjacency?
Ethernet
10.1.1.1
10.1.1.2
10.1.1.3
10.1.1.4
RTA
I have 3 neighbors
Notes: OSPF is a dynamic routing protocol. Before two OSPF routers can exchange link state information and routing information, a neighbor relationship and adjacency need to be established between the routers.
Neighbor
Two routers directly connected to the same network segment are neighbors. Neighbor relationships are maintained by using OSPF Hello packets.
Adjacency
An adjacency is a neighbor relationship selected to exchange routing information.
Not all the neighbor relationships can become adjacencies. Whether an adjacency is established also varies with network types.
In this example, RTA and the other three routers are directly connected to the same network segment. As shown in the preceding figure, OSPF runs on all the interfaces of all the routers. According to the above-mentioned definitions, RTA establishes neighbor relationships with the other three routers. According to the principle of running OSPF on Ethernet, RTA establishes adjacencies with only the designated router (DR) and backup designated router (BDR).
The following topic describes the types of networks on which OSPF runs and the principles of establishing neighbor relationships and adjacencies on different types of networks.

## Slide 58
What Are the OSPF Network Types? - P2P and Broadcast
PPP
10.1.1.1
20.1.1.1
Point to Point Network
Ethernet
10.1.1.1
10.1.1.2
10.1.1.3
10.1.1.4
Broadcast Network
Notes: As mentioned in the preceding section, not all the neighbor relationships become adjacencies to allow the exchange of link state information and routing information. Whether an adjacency is formed depends on the network type. A network type refers to the Layer 2 link type of the network segment running OSPF.
In OSPF, four network types are defined: point-to-point (P2P), broadcast, non-broadcast multi-access (NBMA), and point-to-multipoint (P2MP).
P2P: A P2P network is a network where two routers are directly interconnected.
Broadcast: A broadcast network is a network that supports the interconnection of more than two routers and has broadcast capabilities.
NBMA: An NBMA network is a network that supports the interconnection of more than two routers but does not have any broadcast capability. On an NBMA network, OSPF simulates the operations performed on a broadcast network, but the neighbors of each router need to be configured manually. All the routers on an NBMA network must be fully-meshed.
P2MP: An entire non-broadcast network is considered as a group of P2P networks. The neighbors of each router can be discovered by using a lower-layer protocol, for example, inverse address resolution protocol (ARP).

## Slide 59
What Are the OSPF Network Types? - NBMA
ATM
10.1.1.1
10.1.1.2
10.1.1.3
VPI/VCI=0/102
VPI/VCI=0/103
VPI/VCI=0/201
VPI/VCI=0/301
0/203
0/302
Non-Broadcast Multiple Access（NBMA）
Full meshed ATM network
Notes: NBMA: An NBMA network is a network that supports the interconnection of more than two routers but does not have any broadcast capability. On an NBMA network, OSPF simulates the operations performed on a broadcast network, but the neighbors of each router need to be configured manually. All the routers on an NBMA network must be fully-meshed.

## Slide 60
What Are the OSPF Network Types? - P2MP
FR
10.1.1.1
10.1.1.2
10.1.1.3
DLCI = 102
DLCI = 103
DLCI = 201
DLCI = 301
Point-to-MultiPoint
Non-full meshed frame relay network
Notes: P2MP: An entire non-broadcast network is considered as a group of P2P networks. The neighbors of each router can be discovered by using a lower-layer protocol, for example, inverse address resolution protocol (ARP).

## Slide 61
Default Network Types Corresponding to Common Link Layer Protocols
Network type | Common data link layer protocols
Point-to-point | PPP, LAPE, HDLC
Broadcast | Ethernet
NBMA | Frame Relay, ATM
Notes: The table list default network types for common data link layer protocols.
Point-to-MultiPoint is not a default network type.

## Slide 62
DR and BDR
Ethernet
10.1.1.1
10.1.1.2
10.1.1.3
10.1.1.4
RTA
BDR
DR
I have 3 neighbors, but only 2 adjacencies
Notes: In a broadcast network or NBMA network, routing information needs to be transferred between any two routers. If n routers exist in the network, n ? (n-1)/2 adjacencies need to be established. As a result, a route change on any router needs to be transferred for multiple times and bandwidth resources are wasted. To solve this problem, DR is defined in the OSPF protocol and all the routers only need to send information to the DR for broadcasting the network link states.
If the DR fails due to a fault, all the routers in the network must re-elect the DR and be synchronized to the new DR. During this process, which takes quite long, route calculation may be incorrect. To shorten this process, the BDR concept is defined in OSPF.
DR: A DR is the router that maintains adjacencies with all the other OSPF routers on the same network segment and exchanges LSAs with these routers.
BDR: A BDR is a backup DR.
DR Other: A router that is neither a DR nor BDR is a DR Other. DR Others do not form adjacencies between themselves or exchange routing information. Therefore, the number of adjacencies formed between the routers on the broadcast network or NBMA network is reduced.

## Slide 63
Instead of being manually specified, the DR and BDR are elected among all the routers on the local network segment. The DR priority of a router interface determines the eligibility of the interface in the DR election and BDR election.
DR Election and BDR Election
Ethernet
10.1.1.3
10.1.1.2
10.1.1.1
90
BDR
DR
100
120
Router with highest Router Priority may not be DR/BDR
Red numbers indicate Router Priority of interface
Notes: Process Description
The DR and BDR are elected by the Hello protocol. The election procedure is as follows:
Each router writes the DR it votes for into a Hello packet advertised to other routers on the same network segment.
When two routers on the same network segment declare themselves the DR, the router with a higher DR priority wins.
If the DR priorities are the same, the router with a larger router ID wins.
A router with the priority 0 is not elected as DR or BDR.
Note the following points:
DR is elected only on broadcast or NBMA interfaces. No DR is elected on P2P or P2MP interfaces.
DR is based on the network segment and relative to a router interface. A router that functions as the DR on an interface may be a BDR or DR Other on another interface.
If the DR and BDR are elected, a newly added router, regardless of its DR priority, does not become the DR of the network segment immediately.
The DR is not necessarily the router with the highest DR priority. Likewise, the BDR is not necessarily the router with the second highest DR priority.
On the Ethernet shown in the preceding figure, the DR is 10.1.1.1 and the BDR is 10.1.1.2. If a router is added to the network, configure the priority of the added router as 120, which is greater than the priority of the original DR, 100, and the priority of the original BDR, 90. The added router does not become the new DR though it has the highest priority. This maintains the network stability.

## Slide 64
DR election and BDR election takes time and affects the speed of OSPF route convergence. During the actual OSPF application, the broadcast network and NBMA network types are often changed to the P2P type to prevent the election of the DR or BDR. The following command is used to change the network type of an OSPF network interface:
The following figure describes whether adjacencies are established with neighbors for different network types:
DR Election and BDR Election
[RTB-Ethernet0/0] ospf network-type p2p
Network Type | Establish Adjacency with Neighbor or not
Point-to-Point | Neighbors always become adjacent
Point-to-MultiPoint | Neighbors always become adjacent
Broadcast NBMA | DR is always adjacent to all the other routers including BDR; BDR is always adjacent to all the other routers including DR; Routers whose interface state is DR, Other is adjacent to only DR and BDR.

## Slide 65
Neighbor relationship establishment on a broadcast network:
Establishment of Neighbor Relationship (1)
RTA
RTB
1
Down
Hello (one-way)
Down
Init
2
Hello (two-way)
3
Hello (two-way)
Two-way
Two-way
Router id 1.1.1.1
Router id 2.2.2.2
Notes: In OSPF, whether neighbor relationships are established depends on network types. This topic describes the procedure of establishing neighbor relationships on P2P networks and broadcast networks, which are the most commonly used.
When the OSPF state becomes “Two-way” on a broadcast network, it means this Router’s neighbor relationship is established.
Process Description
1.Neighbor relationship establishment on a broadcast network.
2.Neighbor relationship establishment on a P2P network.

## Slide 66
The difference between the 1-way and 2-way states is as follows: If a Hello packet carrying the router's router ID has recently been seen from the neighbor, it indicates the 2-way state. Otherwise, it indicates the 1-way state.
Establishment of Neighbor Relationship (2)
[Quidway]display ospf peer
OSPF Process 1 with Router ID 4.4.4.4
Neighbors
Area 0.0.0.1 interface 10.1.1.4(Ethernet0/0)'s neighbor(s)
RouterID: 1.1.1.1 Address: 10.1.1.1
State: 2 Way Mode: None Priority: 1
DR: 10.1.1.2 BDR: 10.1.1.3
Dead timer expires in 37s
Neighbor has been up for 00:00:00

## Slide 67
Neighbor relationship establishment on a P2P network:
No DR or BDR needs to be elected on a P2P link, P2MP link, or virtual link.
Establishment of Neighbor Relationship (3)
RTA
RTB
1
Down
Hello
Down
Init
2
Hello
Init
Router id 1.1.1.1
Router id 2.2.2.2
Notes: No DR or BDR needs to be elected on a P2P link, P2MP link, or virtual link.
After the interface goes up, the interface states from DOWN state to point–to-point state and attempts to establish a neighbor relationship with its neighbor.
After the interface receives a Hello packet, the router enters the Init state. This process is different from that on a broadcast link or NBMA link.

## Slide 68
Adjacency Establishment Process (1)
RTA
RTB
Adjacency relationship
1
Router id 1.1.1.1
Router id 2.2.2.2
ExStart
ExStart  Exchange
ExStart
Exchange
ExStart  Exchange
DD, Seq=552A, I, M, MS
2
DD, Seq=5528, I, M, MS
3
DD, Seq=5528
4
5
Exchange
DD, Seq=5529, MS
DD, Seq=5529
Exchange
Exchange
Exchange  Loading
Exchange  Full
Master
Notes: Process Description:
1.After the neighbor state becomes ExStart, RTA sends RTB the first DD packet in which the DD sequence number is set to 552A (assumed). The Init bit is set to 1, indicating that this packet is the first in the sequence of DD packets. The More bit is set to 1, indicating that more DD packets are to follow. The Master/Slave bit is set to 1, indicating that the router is the master during the database exchange process.
2.After the neighbor state becomes ExStart, RTB sends RTA the first DD packet in which the DD sequence number is set to 5528 (assumed). As the router ID of RTB is larger than that of RTA, RTB should function as the master. After the router ID comparison is complete, RTA generates a NegotiationDone event. Therefore, the RTA neighbor state transitions from ExStart to Exchange.
3.After the neighbor state becomes Exchange, RTA sends a new DD packet carrying the LSDB summary information. The DD sequence number is set to that used by RTB in step 2. The More bit is set to 0, indicating that no more DD packet is needed to describe the LSDB. The Master/Slave bit is set t 0, indicating that RTA asserts itself as the slave. On receiving the DD packet, a NegotiationDone event is generated on RTB. Therefore, the state of RTB changes to Exchange.
4.After the neighbor state changes to Exchange, RTB sends a new DD packet that carries LSDB description information, with the DD sequence number set to 5529 (the previously used DD sequence number increase 1).

## Slide 69
Adjacency Establishment Process (2)
RTA
RTB
7
Loading
LS Request
Adjacency relationship
Full
8
LS Update
9
LS Ack
Full
Full
Loading  Full
Full
Router id 1.1.1.1
Router id 2.2.2.2
Notes: 5.RTA does not need any new DD packet to describe its LSDB. Functioning as the slave, however, RTA needs to acknowledge each DD packet sent by RTB, which is the master. Therefore, RTA sends RTB a new and empty DD packet whose sequence number is 5529.
6.After sending the last DD packet, RTA generates an ExchangeDone event to change the neighbor state to Loading. After RTB receives the last DD packet, if the LSDB of RTB is the most recent and RTB does not need to send any update request to RTA, RTB transits to the Full state.
7.After the neighbor state becomes Loading, RTA starts sending LSRs to RTB, asking for the link state information that is discovered by DD packets in the Exchange state but is not found in the local LSDB.
8.After receiving the LSR, RTB sends an LSU carrying the detailed information about the requested link state to RTA. On receiving the LSU, RTA changes the neighbor state from Loading to Full.
9.RTA sends LS Ack packets to RTB to ensure reliable information transmission. LS Ack packets are used to flood the acknowledgments of received LSAs.
10.The neighbor state becomes Full, indicating that an adjacency is fully established.

## Slide 70
Check Neighbor State of OSPF Router
[RTA]display ospf peer
OSPF Process 1 with Router ID 1.1.1.1
Neighbors
Area 0.0.0.0 interface 10.1.1.1(Ethernet0/0)'s neighbor(s)
RouterID: 2.2.2.2 Address: 10.1.1.2
State: Full Mode: Nbr is Master Priority: 1
DR: 10.1.1.1 BDR: 10.1.1.2
Dead timer expires in 35s
Neighbor has been up for 04:35:02

## Slide 71
Synchronized LSDBs are the basis for proper OSPF route calculation. When an adjacency is established, an OSPF router completes the LSDB synchronization with the adjacent router.
After an adjacency is established and LSDB synchronization is completed, LSAs are updated in the following ways:
  Periodic update: Every 30 minutes, an OSPF router floods the LSAs in the LSDB of the current area to the adjacent routers in the corresponding areas.
  Triggered update: When a network topology change occurs, the router generates new LSAs and floods them so that the topology information about the network remains correct and consistent.
LSDB Synchronization

## Slide 72
VLAN technology
Link aggregation technology
OSPF protocol
BGP protocol
  BGP Overview
  BGP Neighbor Relationship Establishment and Configuration
  BGP Route Advertisement Rules and Route Processing

## Slide 73
IGPs, such as OSPF, IS-IS, and RIP, are used within an AS to calculate and discover routes.
BGP is used between ASs to transmit and control routes.
Basic BGP Functions
AS 65001
AS 65000
BGP
BGP
IGP
BGP
AS 65002
AS 65003
IGP
Notes: EGP, the predecessor of BGP, is simple in design and can only transmit routing information between ASs and cannot select optimal routes or prevent routing loops between ASs. Therefore, EGP was replaced by BGP.
Compared with EGP, BGP has the following advantages:
  Discovers neighbors and establishes neighbor relationships.
  Selects optimal routes and advertises routes.
  Prevents routing loops, efficiently transmits routes, and maintains a large amount of routing information.
  Provides various route control capabilities between ASs that are not fully trusted.
Using BGP to transmit routing information, a routing domain functions as a whole to exchange routing information with another routing domain. This routing domain is an AS. An AS is a set of routers and networks that consist of these routers. These routers are under a single technical administration and use the same routing policies.
An AS is uniquely identified by an AS number, which is assigned by the Internet Assigned Numbers Authority (IANA). Before January 2009, only 2-byte AS numbers can be used, which range from 1 to 65535. AS numbers 1 to 64511 are public AS numbers, and AS numbers 64512 to 65534 are private AS numbers. After January 2009, the IANA decided to use 4-byte AS numbers, which range from 65536 to 4294967295.

## Slide 74
In the figure, two BGP routers can establish a neighbor relationship across multiple routers.
To implement on-demand route control and selection, various BGP attributes are designed and carried in routes.
BGP Characteristics
AS 65002
AS 65001
AS 65003
BGP
BGP
BGP
Notes: To ensure reliable data transmission between ASs, BGP uses TCP to establish connections. Therefore, BGP can establish a neighbor relationship across multiple routers, while IGP can only establish a neighbor relationship hop by hop.
Routers between ASs do not completely trust each other. To implement on-demand route control and selection, various BGP attributes are designed.

## Slide 75
VLAN technology
Link aggregation technology
OSPF protocol
BGP protocol
  BGP Overview
  BGP Neighbor Relationship Establishment and Configuration
  BGP Route Advertisement Rules and Route Processing

## Slide 76
The device that starts BGP first initiates a TCP connection. In the figure, RTB first starts BGP and uses a random port number to initiate a TCP connection with port 179 of RTA.
BGP Neighbor Discovery
RTA
1.1.1.1
RTB
2.2.2.2
TCP SYN
TCP ACK+SYN
TCP ACK
Notes: BGP is designed to run between ASs to transmit routers. There are WAN links between ASs, and unpredictable link congestion or packet loss may occur during packet transmission on WANs. Therefore, BGP uses TCP as the transport protocol to ensure reliability.
BGP uses TCP port 179 to establish neighbor relationships, and TCP establishes connections in unicast mode. Therefore, unlike RIP and OSPF, BGP does not discover neighbors in multicast mode. Establishing connections in unicast mode requires neighbors to be manually specified in BGP.

## Slide 77
BGP routers in different ASs establish EBGP neighbor relationships.
BGP Neighbor Type - EBGP
RTA
RTB
RTC
RTD
RTE
AS 100
AS 200
AS 300
OSPF
EBGP
EBGP
Notes: EBGP transmits routes only between different ASs. In the figure, RTB and RTC in AS 100 can learn different routes from AS 200 and AS 300 respectively. How to transmit routes of AS 200 and AS 300 within AS 100?
To meet this requirement, on RTB and RTC, import BGP routes into IGP (OSPF in the figure) and then import IGP routes back into BGP.
However, this method has the following disadvantages:
  There are a huge number of BGP routes on the public network. After these BGP routes are imported into IGP, IGP cannot support these BGP routes.
  When BGP routes are imported into IGP, strict control is required. This complicates the configuration and maintenance.
  When BGP attributes carried in BGP routes are imported into IGP, these attributes may be lost because they cannot be identified by IGP.
To overcome these disadvantages, BGP needs to be designed to transmit routes within an AS.

## Slide 78
BGP routers in the same AS establish IBGP neighbor relationships.
BGP Neighbor Type - IBGP
RTA
RTB
RTC
RTD
RTE
AS 100
AS 200
AS 300
OSPF
EBGP
EBGP
Notes: BGP uses TCP as the transport protocol. Therefore, BGP can establish neighbor relationships across multiple devices. In the figure, RTB and RTC establish an IBGP neighbor relationship and transmit the routes learned from other ASs to each other so that BGP routes can be transmitted within an AS.

## Slide 79
BGP Neighbor Relationship Configuration
RTA
RTB
RTC
RTD
RTE
AS 100
AS 200
AS 300
OSPF
EBGP
EBGP
IBGP
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
1.1.1.1
2.2.2.2
3.3.3.3
4.4.4.4
5.5.5.5
.3
.3
.5
.4
.2
.2
.1
.1
router id 3.3.3.3
bgp 100
peer 10.1.35.5 as-number 300
peer 10.1.12.2 as-number 100
router id 5.5.5.5
bgp 300
peer 10.1.35.3 as-number 100
Notes: Configuration procedure:
  Configure a router ID to identify a router.
  Configure an EBGP neighbor relationship to transmit routes between ASs.
  Configure an IBGP neighbor relationship to transmit routes within an AS.
Description:
  If no router ID is configured for a BGP router, it automatically selects a router ID according to the following rules:
    Selects the highest IP address among all loopback interfaces.
    Selects the highest IP address among all physical interfaces if it does not have loopback interfaces.
    Configuration command: router id X.X.X.X
  BGP neighbor relationship type is identified by the configured AS number. The parameter following the peer keyword indicates the interface IP address of the neighbor, and the parameter following the as-number keyword indicates the AS number of the neighbor. If two routers have the same AS number, they establish an IBGP neighbor relationship. If they have different AS numbers, they establish an EBGP neighbor relationship.

## Slide 80
Notes: The peer keyword indicates the IP address used by the neighbor to establish a BGP neighbor relationship, identifying the destination address of the TCP connection initiated with the neighbor. This address can be the IP address of the neighbor’s directly connected interface or the IP address of an indirectly connected loopback interface (ensure that this IP address is reachable). Loopback interface IP addresses are often used to establish IBGP neighbor relationships. This is because loopback interfaces are always Up after being enabled. As long as routes are reachable, IBGP neighbor relationships remain stable. Directly connected interface IP addresses are often used to establish EBGP neighbor relationships. This is because EBGP neighbor relationships are established between ASs and routes between indirectly connected interfaces are unreachable before the neighbor relationships are established.

## Slide 81
BGP Neighbor Relationship Configuration Optimization
RTA
RTB
RTC
RTD
RTE
AS 100
AS 200
AS 300
OSPF
EBGP
EBGP
IBGP
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.35.0/24
1.1.1.1
2.2.2.2
3.3.3.3
4.4.4.4
5.5.5.5
.3
.3
.5
.4
.2
.2
.1
.1
router id 5.5.5.5
bgp 300
peer 10.1.35.3 as-number 100
router id 3.3.3.3
bgp 100
peer 10.1.35.5 as-number 300
peer 2.2.2.2 as-number 100
Peer 2.2.2.2 connect-interface loopback 0
Notes: Directly connected interface IP addresses are often used to establish EBGP neighbor relationships, and loopback interface IP addresses are often used to establish IBGP neighbor relationships.

## Slide 82
BGP Neighbor Relationship Establishment
RTA
1.1.1.1
RTB
2.2.2.2
Idle
TCP SYN
TCP ACK+SYN
TCP ACK
Connect
Open报文
OpenSent
Idle
Connect
Open报文
OpenSent
Keepalive报文
OpenComfirm
Keepalive报文
OpenComfirm
Established
Established
Update，Keepalive，Route-refresh，Notification
Notes: BGP routers exchange BGP messages to establish neighbor relationships and update routing information. BGP messages are classified into Open, Update, Notification, Keepalive, and Route-refresh messages.
  Open message: is the first message sent after a TCP connection is established. It is used to establish a BGP connection between neighbors. After a BGP neighbor receives an Open message and negotiation succeeds, the neighbor sends a Keepalive message to confirm and retain the connection. Then BGP neighbors can exchange Update, Notification, Keepalive, and Route-refresh messages.
  Update message: is used to exchange routing information between BGP neighbors. It can advertise multiple reachable routes with the same route attributes and withdraw multiple unreachable routes.
    An Update message can advertise multiple reachable routes with the same route attributes. These routes can share a group of route attributes. All the route attributes carried in a specific Update message apply to all the destinations (specified by IP prefixes) of the Network Layer Reachability Information (NLRI) field in this Update message.
    An Update message can withdraw multiple unreachable routes. Each withdrawn route identified by a destination address (an IP prefix) is the route that was advertised between BGP routers.

## Slide 83
Notes: You can use an Update message just to withdraw routes so that this message does not need to contain the path attribute or NLRI. Alternatively, you can use an Update message just to advertise reachable routes so that this message does not need to contain withdrawn route information.
Notification message: is sent when a BGP router detects an error. Then a BGP connection is terminated immediately.
Keepalive message: is sent periodically from a BGP router to its neighbor to retain their connection.
Route-refresh message: is sent by a BGP router to request its neighbor to send routing information again after this router changes its routing policy.
During message exchange, the Idle state is the initial state of a BGP router. In Idle state, the BGP router rejects the connection request from its neighbor. Only after receiving the Start event of itself, the BGP router tries to establish a TCP connection with its neighbor and transitions to the Connect state.
In Connect state, the BGP router starts the Connect Retry timer, waiting for a TCP connection to be established.
If a TCP connection is established, the BGP router sends an Open message to its neighbor and transitions to the OpenSent state.
If a TCP connection fails to be established, the BGP router transitions to the Active state.
If the BGP router does not receive any response from its neighbor until the Connect Retry timer expires, the BGP router continues to try to establish a TCP connection with its neighbor and stays in the Connect state.
In Active state, the BGP router always tries to establish a TCP connection.
If a TCP connection is established, the BGP router sends an Open message to its neighbor, turns off the Connect Retry timer, and transitions to the OpenSent state.
If a TCP connection fails to be established, the BGP router stays in the Active state.
If the BGP router does not receive any response from its neighbor until the Connect Retry timer expires, the BGP router transitions to the Connect state.
In OpenSent state, the BGP router waits for an Open message from its neighbor and checks information carried in the Open message, including AS number, version number, and authentication password.
If the received Open message is correct, the BGP router sends a Keepalive message to its neighbor and transitions to the OpenConfirm state.

## Slide 84
Notes: If the received Open message is incorrect, the BGP router sends a Notification message to its neighbor and transitions to the Idle state.
In OpenConfirm state, the BGP router waits for a Keepalive or Notification message from its neighbor. If it receives a Keepalive message, it transitions to the Established state. If it receives a Notification message, it transitions to the Idle state.
In Established state, the BGP router can exchange Update, Keepalive, Route-refresh, and Notification messages with its neighbor.

## Slide 85
VLAN technology
Link aggregation technology
OSPF protocol
BGP protocol
  BGP Overview
  BGP Neighbor Relationship Establishment and Configuration
  BGP Route Advertisement Rules and Route Processing

## Slide 86
BGP routes are generated in either network or import mode. They are encapsulated in Update messages and advertised to neighbors. BGP advertises routing information only after a neighbor relationship is established.
Update messages are used to advertise reachable routes and withdraw unreachable routes. An Update message contains the following information:
  Network Layer Reachability Information (NLRI): advertises the IP prefix and prefix length.
  Path attribute: provides loop detection and controls optimal route selection.
  Withdrawn route: describes the prefix and prefix length of the unreachable withdrawn route.
BGP route advertisement must follow specific rules to prevent potential problems.
BGP Update Message

## Slide 87
BGP Route Advertisement Rule 1: Advertise Only the Optimal Route to Neighbors
BGP Route Advertisement Rule (1)
AS 100
AS 300
AS 200
RTA
RTB
RTC
RTD
10.1.12.0/24
10.1.13.0/24
10.1.24.0/24
10.1.34.0/24
EBGP
EBGP
IBGP
IBGP
EBGP
10.1.45.0/24
100.0.0.0/24
RTE
200.0.0.0/24
OSPF
<RTE>display bgp routing-table
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 100.0.0.0/24 10.1.45.4 0 200 100i
*> 200.0.0.0 10.1.45.4 0 0 200i
<RTD>display bgp routing-table
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 100.0.0.0/24 10.1.12.1 0 100 0 100i
* i 10.1.13.1 0 100 0 100i
*> 200.0.0.0 0.0.0.0 0 0 i
Notes: When multiple valid routes exist, a BGP router advertises only the optimal route to its neighbor.
  RTD can learn the route 100.0.0.0/24 from two BGP neighbors (RTB and RTC) and RTD advertises its directly connected route 200.0.0.0/24 into BGP. Run the display bgp routing-table command on RTD. The following command output is displayed:
  Run the display bgp routing-table command on RTE. The following command output is displayed. You can view that RTD has advertised the optimal route marked valid to its BGP neighbor RTE.
Fields in a BGP routing table include:
  Status codes: * - valid, > - best, d - damped, h - history, i - internal, s - suppressed, S - Stale
  Origin : i - IGP, e - EGP, ? – incomplete
  Network: network address
  NextHop: next-hop address
  MED: route metric
  LocPrf: local preference
  PrefVal: protocol preferred value
  Path/Ogn: AS_Path and Origin attribute
  Community: Community attribute information

## Slide 88
BGP Route Advertisement Rule 2: Advertise the Optimal Route Obtained Through EBGP to All BGP Neighbors.
BGP Route Advertisement Rule (2)
<RTD>display bgp routing-table
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 100.0.0.0/24 10.1.24.2 0 200 100i
AS 100
AS 200
AS 300
RTA
RTB
RTC
RTD
EBGP
EBGP
IBGP
10.1.23.0/24
10.1.12.0/24
10.1.24.0/24
100.0.0.0/24
<RTC>display bgp routing-table
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 100.0.0.0/24 10.1.12.1 0 100 0 100i
Notes: A BGP router advertises the optimal route obtained through EBGP to all BGP neighbors (including EBGP neighbors and IBGP neighbors).
  In the figure, RTA has a user network segment 100.0.0.0/24 and advertises this network segment to a BGP neighbor RTB through EBGP. After RTB receives this route from its EBGP neighbor, it advertises this route to its IBGP neighbor RTC and EBGP neighbor RTD.

## Slide 89
IBGP
IBGP
IBGP
10.1.12.0/24
10.1.23.0/24
10.1.13.0/24
RTA
RTB
RTC
AS 100
100.0.0.0/24
<RTB>display bgp routing-table 100.0.0.0
BGP local router ID : 2.2.2.2
Local AS number : 100
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 100.0.0.0/24:
From: 10.1.12.1 (1.1.1.1)
Route Duration: 00h01m39s
Relay IP Nexthop: 0.0.0.0
Relay IP Out-Interface: GigabitEthernet0/0/0
Original nexthop: 10.1.12.1
Qos information : 0x0
AS_Path Nil, origin igp, MED 0, localpref 100, pref-val 0, valid, internal, best, select, active, pre 255
Not advertised to any peer yet
<RTC>display bgp routing-table
Network NextHop MED LocPrf PrefVal Path/Ogn
*>i 100.0.0.0/24 10.1.13.1 0 100 0 i
BGP Route Advertisement Rule 3: Do Not Advertise the Optimal Route Obtained Through IBGP to Other IBGP Neighbors.
BGP Route Advertisement Rule (3)
Notes: A BGP router does not advertise the optimal route obtained through IBGP to other IBGP neighbors.
  In the figure, RTA has a user network segment 100.0.0.0/24. RTA, RTB, and RTC are IBGP neighbors. RTA advertises the route 100.0.0.0/24 to RTB and RTC through IBGP, but RTB does not advertise the received IBGP route to its IBGP neighbor RTC.
  This design prevents routing loops within an AS. As defined, when a BGP route is transmitted within an AS, its AS_Path attribute remains unchanged. In the figure, when RTA advertises the route 100.0.0.0/24 to RTB, the AS_Path attribute of this route remains unchanged and is empty. If RTB can advertise this IBGP route to RTC, RTC may also advertise this route to RTA because the AS_Path attribute of the route is still empty, and RTA will not reject this route. As a result, a routing loop occurs. Therefore, this route advertisement rule can prevent routing loops within an AS.

## Slide 90
BGP Route Advertisement Rule 4: Synchronize BGP and IGP.
BGP Route Advertisement Rule (4)
My routing table does not have the route to 100.0.0.0/24 and I don’t know how to reach 100.0.0.0/24 so I discard packets with an unreachable destination address
IBGP
OSPF
AS 200
AS 300
AS 100
RTB
RTC
RTD
RTE
RTA
100.0.0.0/24
EBGP
EBGP
Notes: RTA has a user network segment 100.0.0.0/24 and advertises it to RTB through EBGP. RTB and RTD establish an IBGP neighbor relationship. RTD learns this BGP route through IBGP and advertises it to the EBGP neighbor RTE.
When RTE accesses the network segment 100.0.0.0/24, it examines its routing table, finding that the next hop of the route to 100.0.0.0/24 is RTD. After RTE finds the outbound interface, it sends a packet to RTD. RTD receives the packet and examines its routing table, finding that the next hop of the route is RTB and the outbound interface is the interface connected to RTC and sends the packet to RTC. RTC receives the packet and examines its routing table, finding that there is no route to 100.0.0.0/24 and discards this packet. In this situation, the routing blackhole problem occurs.
BGP route advertisement rule: Before a BGP router advertises a route learned from an IBGP neighbor to another BGP neighbor, IGP must know this route. That is, BGP must synchronize with IGP.

## Slide 91
Notes: In the figure, after RTD receives an IBGP route from RTB, RTD needs to check whether IGP (OSPF) has learned this route before advertising this route to RTE. If OSPF can learn this route, RTD advertises it to RTE.
By default, synchronization check between BGP and IGP is disabled on Huawei routers to ensure normal IBGP route advertisement. However, disabling synchronization check will lead to the routing blackhole problem. To solve this problem, two methods are available:
Import BGP routes into IGP to ensure synchronization between BGP and IGP. However, the number of BGP routes on the Internet is huge and importing so many BGP routes into IGP will bring a huge processing and storage burden to an IGP router. If the IGP router is overloaded, it may crash.
IBGP routers must be fully meshed to ensure that all routers can learn advertised routes. This method can solve the routing blackhole problem occurring after synchronization check is disabled.

## Slide 92
When receiving an Update message from a BGP neighbor, a BGP router uses the route selection algorithm to determine the optimal route for each prefix.
The router stores the selected optimal route to the local BGP routing table (Local_RIB) and then submits it to the local IP routing table (IP_RIB) to determine whether to install it.
The router encapsulates the selected valid optimal route in an Update message and sends it to the BGP neighbor.
BGP Routing Information Processing
Update information received from a BGP neighbor
Route selection
Local_RIB
IP_RIB
Update information sent to a BGP neighbor
Notes: IP routing table (IP_RIB): global routing information database, including all IP routing information.
BGP routing table (Local_RIB): BGP routing information database, including routes selected by the local BGP router, neighbor table, and neighbor list.
After receiving an Update message from a BGP neighbor, a BGP router uses the route selection algorithm to determine the optimal route for each prefix and stores the selected optimal route to the local BGP routing table (Local_RIB).
If multipath is enabled on a BGP router, it submits the optimal route and all equal-cost routes to IP_RIB to determine whether to install them. In addition to the optimal route received from BGP neighbors, Local_RIB also includes the routes injected by the router. These routes are called locally originated routes.
In Local_RIB, a router encapsulates only the optimal prefix in an Update message and advertises it to BGP neighbors.

## Slide 93
What is the principle of VLAN?
What is the value of link aggregation technology?
What is the core idea of the OSPF routing protocol?
Notes: What is the principle of VLAN?
  The virtual local area network (VLAN) technology groups devices on a physical LAN into different logical LAN segments.。
What is the value of link aggregation technology?
  Increased bandwidth
    The bandwidth of the link aggregation interface is the sum of bandwidth of member interfaces.
  Higher reliability
    When an active link fails, traffic on this active link is switched to another active link, improving reliability of the link aggregation interface.
  Load balancing
    In a link aggregation group (LAG), traffic is load balanced among active links of member interfaces.
What is the core idea of the OSPF routing protocol?
  The most notable feature of OSPF is the use of link state algorithms to maintain routing tables.

## Slide 94
VLAN technology
Link aggregation technology
OSPF protocol
BGP protocol

## Slide 95
Huawei's official websites:
  Enterprise business: http://e.huawei.com/en/
  Technical support: http://support.huawei.com/enterprise/en/
  Online learning: http://learning.huawei.com/en/
Document tool
  HedEx Lite
Simulator
  eNSP

## Slide 96
Huawei E-Learning website:
  http://support.huawei.com/learning/Index!toTrainIndex
Huawei support case library:
  http://support.huawei.com/enterprise/servicecenter?lang=en