## Slide 1
HCDCA110
AC
1.00
1.00
Cai Wenjun/wx440054
2017.08.15
Liu Lican/00180730
New
Yuan Weihua/wx462781
2019.4.10
Liu Lican/00180730
Update

## Slide 2: Data Center SDN Network Basics
Huawei Data Center Series of Courses

## Slide 3
This course describes data center SDN network basics, helping you learn about challenges faced by cloud data centers and the industry's SDN development and technologies.

## Slide 4
Upon completion of this course, you will be able to:
  Describe new challenges for cloud data center networks.
  Describe the industry's SDN development and technical roadmap.
  Understand Huawei's CloudFabric Solution.

## Slide 5
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 6
Traditional Distributed Network
Data plane
Control plane
Management plane
PEA
Data plane
Control plane
Management plane
PEB
Data plane
Control plane
Management plane
PEC
Control plane
Forwarding tables,
protocols, and algorithms
Data plane
Forwarding
Configuration commands
Receive frames
Send frames
Forwarding behavior
Unknown data frames
Management plane

## Slide 7
Problems Faced by Traditional Networks
?
Congested networks
Difficult O&M
Complex devices
Slow service provisioning

## Slide 8
Congested Networks
Question 1: The link between router A and router B is the shortest path. Packet loss is going to occur on this link. However, other links are idle. Why not adjust traffic to the path from router A to router C and then to router B?
A
B
C
D
E
6G/5G
1G/5G
2G/10G
Congested
Not congested
Occupied bandwidth/Total bandwidth
A
B
D
C
E
F
G
H
Total link bandwidth: 10 Gbit/s
1
2
3
Based on the sequence
Global calculation
A
B
D
C
E
F
G
H
1
3
2
Service requirements:
1. A->E: 6 Gbit/s; 2. C->G: 4 Gbit/s; 3. C->D: 8 Gbit/s. (Bandwidth of each link is 10 Gbit/s. The above topology shows the service setup sequence.)
Question 2: In traditional mode, services are deployed based on the sequence, and service 3 fails to be set up. Why not use global calculation to ensure that all services are successfully set up?

## Slide 9
If you want to become an IP expert, you will probably have to read more than 2,500 RFCs about network devices — that would take over six years if you read one a day. And that only accounts for a third of all RFCs, the number of which continues to grow.
Complex Network Devices from Multiple Vendors
Chart: Number of new RFCs about network devices
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
网络设备相关RFC增长数量 | 79 | 212 | 152 | 129 | 124 | 150 | 242 | 205 | 185
1 0 0 0 0
If you want to have expert knowledge of a vendor's devices, you will need to master more than 10,000 commands — a number that is constantly growing.

## Slide 10
Numerous Network Protocols, Difficult Network Management and O&M
PE1
PE3
PE2
PE4
CE1
CE2
Example for deploying L3VPN for an enterprise:
IGP needs to be configured.
MPLS needs to be configured.
VPNv4 needs to be configured.
The PE-CE protocol needs to be configured.
MP-BGP needs to be configured.
Notes: Approximately 50 configuration commands for a single PE:
1 Configure IGP
[~PE1] interface loopback 1
[~PE1-LoopBack1] ip address 1.1.1.9 32
[~PE1] interface gigabitethernet3/0/0
[~PE1-GigabitEthernet3/0/0] ip address 172.1.1.1 24
[~PE1] ospf
[~PE1-ospf-1] area 0
[~PE1-ospf-1-area-0.0.0.0] network 172.1.1.0 0.0.0.255
[~PE1-ospf-1-area-0.0.0.0] network 1.1.1.9 0.0.0.0
[~PE1-ospf-1-area-0.0.0.0] quit
2 Configure MPLS
[~PE1] mpls lsr-id 1.1.1.9
[~PE1] mpls
[~PE1] mpls ldp
[~PE1] interface gigabitethernet 3/0/0
[~PE1-GigabitEthernet3/0/0] mpls
[~PE1-GigabitEthernet3/0/0] mpls ldp

## Slide 11
Notes: 3 Configure VPNV4
[~PE1] ip vpn-instance vpna
[~PE1-vpn-instance-vpna] ipv4-family
[~PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[~PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[~PE1-vpn-instance-vpna-af-ipv4] quit
[~PE1] ip vpn-instance vpnb
[~PE1-vpn-instance-vpnb] ipv4-family
[~PE1-vpn-instance-vpnb-af-ipv4] route-distinguisher 100:2
[~PE1-vpn-instance-vpnb-af-ipv4] vpn-target 222:2 both
[~PE1-vpn-instance-vpnb-af-ipv4] quit
[~PE1] interface gigabitethernet 1/0/0
[~PE1-GigabitEthernet1/0/0] ip binding vpn-instance vpna
[~PE1-GigabitEthernet1/0/0] ip address 10.1.1.2 24
[~PE1-GigabitEthernet1/0/0] quit
[~PE1] interface gigabitethernet 2/0/0
[~PE1-GigabitEthernet2/0/0] ip binding vpn-instance vpnb
[~PE1-GigabitEthernet2/0/0] ip address 10.2.1.2 24
[~PE1-GigabitEthernet2/0/0] quit
[~PE1] commit
4 Configure PE-CE part
[~PE1] bgp 100
[~PE1-bgp] ipv4-family vpn-instance vpna
[~PE1-bgp-vpna] peer 10.1.1.1 as-number 65410
[~PE1-bgp] ipv4-family vpn-instance vpnb
[~PE1-bgp-vpnb] peer 10.2.1.1 as-number 65420
[~PE1-bgp] quit
5 Configure MBGP
[~PE1] bgp 100
[~PE1-bgp] peer 3.3.3.9 as-number 100
[~PE1-bgp] peer 3.3.3.9 connect-interface loopback 1
[~PE1-bgp] ipv4-family vpnv4
[~PE1-bgp-af-vpnv4] peer 3.3.3.9 enable
[~PE1-bgp] quit

## Slide 12
Slow Provisioning of Innovative Network Services
Standardization
Requirement proposing
Vendor support
Large-scale deployment
2 years
1 year
1 year
It takes at least 3-5 years to complete deploying an innovative application.

## Slide 13
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 14
Software-Defined Networking (SDN) is a new innovative network architecture that was proposed in the Clean Slate program at Stanford University.
As the core technology of SDN, OpenFlow separates network devices' control plane from the data plane to implement flexible network traffic control. SDN provides a well designed platform for core network and application innovations.
Origin of SDN
Networking devices
SDN controller
SDN application
Data plane
Control plane
Control plane
Data plane
Notes: SDN is oringal of data plane and control plane separation, but is not limited to it.
With the development of technology, overlay and traffic optimization solutions are also treated as SDN.

## Slide 15
Architecture of SDN Data Center Networks
3rd-party cloud platform
Agile Controller orchestration
L3 network
vSwitch
vSwitch
vSwitch
LB
Firewall
Spine
Leaf
vFW
Physical server
VM
VM
VM
FusionCompute
VMM
Network
control layer
Fabric
network
layer
Service
presentation/
collaboration
layer
Virtualization
platform
layer
vSwitch
Notes: Overlay solution is the best practice in data center.
Service presentation/collaboration layer
  Provides service portals for carriers, enterprises, VPCs, and RSPs.
  Provides customizable service portals.
Network control layer
  The network control platform is the SDN controller (Agile Controller), which implements network modeling and network instantiation.
  Northbound open APIs can be deployed for rapid customization and automatic provisioning of services.
  Southbound OpenFlow/NETCONF interfaces can be deployed for centrally managing and controlling physical and virtual networks.
Fabric network layer
  Physical devices set up a basic physical network to support the overlay network.
  The hardware VXLAN gateway improves service performance.
  The fabric network is compatible with traditional VLANs.
Virtualization platform layer
  vSwitches manage network configurations and policies for local VM access.
  vFWs enforce security policy control and load balancing based on software firewalls.

## Slide 16
Interface Relationship Between Components
3rd-party cloud
platform
Agile Controller
orchestration
L3 network
vSwitch
vSwitch
vSwitch
LB
Firewall
Spine
Leaf
vFW
Physical server
VM
VM
VM
VMM
Network
control layer
Fabric
network layer
Service
presentation/
collaboration layer
Virtualization
platform layer
vSwitch
RESTFul API
NETCONF
OpenFlow/OVSDB
RPC/Java SDK
NETCONF/OpenFlow
FusionCompute

## Slide 17
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 18
Optimizing Network Paths and Traffic
A
E
B
D
F
C
35%
35%
15%
30%
90%
30%
90%
30%
25%
30%
45%
20%
50%
40%
92%
80%
95%
35%
10%
85%
E2E
Controller 1
Controller 2
Controller 3
A->B
E->F
C->D
Traffic optimization solution is preferred in WAN network.
Google increased its average link utilization from 30% to almost 95% through SDN.

## Slide 19
By centralizing network control and separating the forwarding and control planes, SDN simplifies networks and eliminates deployment of many IETF protocols, lowering the costs of learning and O&M, and increasing the service deployment speed.
Simplifying Networks
Device
SDN controller
SDN application
Control
Forwarding
Forwarding
Forwarding
Device
Device

## Slide 20
The programmability and openness of SDN accelerate service development and innovation.
When deploying new services on a network, you can modify or enhance SDN software to achieve fast network programmability and provisioning and verification of new services.
Fast Network Innovation
Fast Service Provisioning Is Carriers' Pain Point
Access
User
Aggregation
SR/BRAS
Work order
Services
Policies
VLAN/Port
Allocation
S/C-VLAN
VLAN
S/C-VLAN
Today
Provisioning of the enterprise private line service takes three to six months.
Tomorrow
Work order
The Agile Controller automatically establishes E2E service paths after the administrator sets the BNG, port, and VLAN parameters.
Agile Controller

## Slide 21
If interfaces between controllers and forwarders are standardized based on the SDN architecture (for example, the OpenFlow protocol matures gradually), the white-box trend of network devices is possible.
White-Box Trend of Network Devices
Branded devices
White-box devices

## Slide 22
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 23
Different Opinions on SDN
... separated control and forwarding planes, OpenFlow ...
… operate the network like a "programmable patch panel"…
ONF
Guido Appenzeller, Former CEO of Big Switch
... separated control and forwarding planes and open programmable interfaces ...
Gartner
... open programmable interfaces and the resulting service agility ...
Light Reading network expert
... overlay virtualized network ...
Richard Huang, CEO of QingCloud
VMware
Definitions of SDN differ. ... What matters is the value that SDN brings.

## Slide 24
Major Schools of Thought in SDN
Each of the schools is trying to establish dominance in the industry chain while SDN is flourishing, and for that reason it is difficult in the short term to create uniform industry standards.
Characteristics:
1. Separated forwarding and control planes.
2. Standardized forwarding plane.
3. OpenFlow standardization.
Challenges:
1. Costs in unifying forwarding devices.
2. Difficulty in evolving the live network.
Revolutionary School: Based on OpenFlow
Members:
1. Google
2. Ericsson
3. NEC
Reformist School: Improve
the Existing System
Characteristics:
1. Open capabilities of network devices.
2. Standardized APIs.
3. Emphasis on smooth device evolution.
Members:
1. Cisco
2. Juniper
Challenges:
1. Insufficient programmability.
IT School: Based on COTS
Characteristics:
1. Software-based network functions.
2. Unified hardware platform.
Members:
1. VMware
NFV ISG
Challenges:
1. Performance problem of software-based network functions.

## Slide 25
SDN Open Source Communities
OpenDaylight Open Source SDN Controller
Characteristics:
1. Open source SDN controller.
2. SAL is compatible with multiple protocols, including OpenFlow, BGP, PCEP, I2RS, SNMP, and NETCONF.
3. Declared orientation to carriers and data centers.
Challenges:
1. De facto standards are controlled by some vendors.
2. Sustainability of the open source system.
ONOS Open Source SDN Controller
Characteristics:
1. Open source SDN controller.
2. Southbound interfaces of the controller mainly support OpenFlow.
3. Declared orientation to carriers.
Challenges:
1. Implementation of OpenFlow.
2. Sustainability of the open source system.

## Slide 26
OpenDaylight Members
Platinum
Silver
Gold

## Slide 27
Partners
  Alcatel-Lucent, AT&T, China Unicom, Ciena, Cisco, Ericsson, Fujitsu, Huawei, Intel, NEC, NTT, SK Telecom, Verizon.
Collaborators
  AARNET, Adara, Airhop Communications, Akamai, AmLight, BlackDuck, BTI Systems, Beijing University of Posts and Telecommunications, Cavium, ClearPath Networks, CNIT, CREATE-NET, Criterion Networks, CSIRO, ECI Telecom, ETRI, Consortium GARR, GEANT, Happiest Mind, Internet2, KAIST, KREONET, KISTI, NAIM Networks, NetCracker, OpenFlow Korea, Oplink Communications, ONF, Postech, Radisys, SRI International.
ONOS Members

## Slide 28
Huawei Actively Promotes SDN Standardization (1)
BOD
TAG
CAB
AFWG
Migration
Extensibility
Config
FAWG
Testing
OTWG
TSC
INF
MAN
PER
REL
SWA
SEC
MANO
Chair/Vice Chair of Multiple ONF WGs
Vice Chair of the NFV Architecture WG,
Contributing the Most Articles
Huawei
Huawei

## Slide 29
Huawei Actively Promotes SDN Standardization (2)
Main battlefield
BBF: SIMR WG
IETF
ALTO/PCE/I2RS
ITU-T SG11/SG13
SDN JCA
Huawei is the chair of the Service Innovation WG, and is the first to propose multi-layer and multi-domain carrier SDN architecture and scenario. Huawei leads the carrier SDN and carrier cloud project initiation.
Huawei is the co-chair of the joint WG on SDN.
Huawei cooperates with the industry's leading ALTO/PCE experts to formulate standards and prototype, and participates in I2RS standardization.
Huawei joins the community, signs the enterprise contribution agreement, and promotes cloud interconnection/cloud access VPN APIs and Huawei device plug-ins.
Huawei joined OpenDaylight as a Silver member in June 2013.
Huawei is the chair of the Architecture WG. Huawei carries out joint innovation on NFV with the industry's leading carriers, and is the first to launch the technical prototype demo for SoftBNG and vHGW.
ONF
(control plane)
OpenStack
Neutron (collaboration layer)
ETSI
NFV
(service processing)
Huawei is the chair of the Migration WG, vice chair of the Optical Transport WG, vice chair of the Security WG, and member of the Chip Advisory Board. Huawei is the first to propose the POF concept and demonstrate the prototype, and is a main contributor to the Forwarding Abstractions WG, Protocol Extension WG, and Architecture WG.

## Slide 30
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 31
Cloud-based Management of Government/Enterprise Campus Networks
…
…
Management of traditional campus networks:
Networks are complex, requiring professional maintenance.
Heavy manual configuration workloads lead to slow service provisioning.
Branches rely on on-premises maintenance.
OPEX accounts for up to 70% of the total cost.
WAN/Internet
Cloud-based
management
Cloud-based management of campus networks:
High efficiency: Networks are managed on the cloud.
Human labor saving: Professional maintenance tools and capabilities are deployed on the cloud.
Quick provisioning: New services and functions are provided on the cloud.
Maintenance-free: Devices support plug-and-play deployment, and multiple service modes are enabled.
Notes: Application Scenarios
  Medium-sized enterprises who expect to focus on their core business but are unwilling and have no capability to build an independent IT team
  Branches and edge nodes of large enterprises
Benefits to Customers
  Reduce OPEX and save approximately 83% of human labor costs.
  Increase IT-based innovative services by over 40%.
Solution Description
  Network planning: efficient and professional network planning and visualized and predictable WLAN planning without coverage holes
  Network deployment: plug-and-play deployment of devices and cross-NAT management
  Service provisioning: device group management and quick template configuration to enable fast service provisioning
  Network monitoring: GIS-based visible network status and mobile O&M app to enable network monitoring anytime, anywhere
  Fault location: multiple online location tools and one-click fault diagnosis
Highlights
  3D cloud-based network planning, cloud-based PMI, and mobile O&M

## Slide 32
Data Center Architecture Reconstruction
Leaf
Leaf
VXLAN gateway
Physical server
Virtual server
Leaf
VM
VM
vSwitch
VM
VM
vSwitch
ServerSAN/IP SAN
LB
Leaf
Leaf
Spine
L4-L7
VTEP
VTEP
Switching layer
Gateway layer
Spine
Management/control
node
Internet
WAN
Private line access
WAN egress router
VTEP
VTEP
Leaf
Leaf
LB
FW
Internet egress router
VXLAN domain
ManageOne
FW
Flat topology structure
Network traffic
trend transferring

## Slide 33
Network and Service Automation for a Bank
A Bank's Architecture Requirements
FW
FW
Spine x N
Public
Intranet
E1
I1
10G OVS
VM
VM
VM
Fabric network
GW (including VXLAN GW)
LB
LB
Leaf + ServerSAN computing node GW
Leaf +
storage node GW
10G
ServerSAN
10G OVSbare metal server(new)
VXLAN
L2 GW
Multiple LB groups
SDN controller
VXLAN L2 GW +
ServerSAN computing node GW
B1
B5
I1
E1
Public
Core
Public
Core
FW
FW
Overlay L2 interconnection
Storage network L3 interconnection
AZ2
N5000+N2000 or C6500/C4500
1000M OVS
VM
VM
VM
1000M OVS bare metalserver (new)
1000Mmidrange computer
Network with an old architecture
SAN
N5000+N2000 or C6500/C4500
ServiceCenter (Intelligent O&M Platform)
AZ1
OpenStack
Notes: Service Automation Capability
  The ServiceCenter delivers services to the OpenStack cloud platform and Agile Controller, achieving E2E automated delivery of network services.
SDN+VXLAN Solution
  The solution uses the overlay hierarchical network technology, supports large L2 communication between the new and old networks, resource sharing, and flexible scheduling, and achieves converged carrying of data access, management, and storage services with the fabric architecture.
SDN-based Security Service Automation Solution
  The ServiceCenter uniformly delivers security policies, achieving automated provisioning of security services.
Current status and problems:
17 cabinets, 4,570 servers, 27 physical network partitions, and 107 firewalls
Long service TTM: The network is highly coupled with applications. The service TTM is as long as 90 days.
Low resource utilization: Data center resources are distributed in different physical partitions, resulting in low resource utilization.
Difficult security management: 20,000 security policies and 10,000 changes each year.

## Slide 34
Highly Efficient Network Operations for an e-Commerce Platform
WAN
Egress router
VXLAN
GW
VTEP
Physical server
40GE
N x POD
40GE
40GE
10GE
BGP
Public L3 GW
Private L3 GW
BGP
Agile Controller
Notes: An e-Commerce Platform's Cloud Network Development Requirements
  Fast service delivery: Efficient provisioning of new services must be supported.
  Highly reliable, stable, and flexible network: Smooth service running must be ensured.
  Automated network O&M: Manually upgrading network devices takes at least one year.
Value of Huawei's SDN Solution
  Controller level: The Agile Controller is responsible for underlay network control and collaboration and achieves automated network deployment.
  Fabric level: The solution provides high-performance physical VXLAN L3 gateways, implements collaboration of the virtual overlay network and physical underlay network, and simplifies O&M.

## Slide 35
Notes: Standardization
Maximize ROI and control investment
Low-cost operations
Network architecture standardization
VAS pooling
Virtualization
Resource and business combination
Fast resource supply
Improve resource utilization
Green and energy-saving
Cloud-oriented
Flexible and fast response to changes
Proactive detection of service requirements
Self-service
Automated deployment

## Slide 36
Traffic Scheduling Between Multiple Data Centers for an Internet Company
An Internet Company's Network Development Requirements
10+ cities, 60+ IDC clusters, 300,000+ servers, 20,000 Gbit/s+ IDC bandwidth, and 5,000 GB+ CDN traffic
  Problems:
  The overall private line utilization was low. However, local capacity expansions frequently occurred.
  The business department suffered from insufficient WAN bandwidth and poor flexibility.
Notes: Solution Description
  The SDN controller and routers run IS-IS/SNMP. The controller collects network topology and bandwidth information.
  The SDN controller completes path computation based on information transferred using IS-IS/SNMP and delivers path computation results to routers using PCEP.
Solution Value
  The service provisioning efficiency is increased 10-fold, and the network-wide DCI link utilization is increased to 80%.
  The service scheduling time is decreased from minutes to seconds.
  Centralized path computation reduces resource occupancy and accelerates network convergence.

## Slide 37
What are the routes from SDN to development and commercial application?
Why is overlay technology a best practice in data center networks?
Notes: What are the routes from SDN to development and commercial application?
  SDN originated from the laboratory openflow control separation, commercial applications developed a variety of routes such as traffic tuning, overlay and so on.
Why is overlay technology a best practice in data center networks?
  The overlay is compatible with traditional network technologies, and the evolution is smooth. It is better to implement service separation and rapid deployment of service networks to cope with daily network changes.

## Slide 38
Limitations of Traditional Networks
SDN Overview
SDN Value
SDN Standards Organizations
SDN Applications

## Slide 39
Huawei's official websites:
  Enterprise business: http://e.huawei.com/en/
  Technical support: http://support.huawei.com/enterprise/en/
  Online learning: http://learning.huawei.com/en/
Document tool
  HedEx Lite
Simulator
  eNSP

## Slide 40
Huawei E-Learning website:
  http://support.huawei.com/learning/Index!toTrainIndex
Huawei support case library:
  http://support.huawei.com/enterprise/servicecenter?lang=en