## Slide 1
HCDCA109
OceanStor V5
V5R2
1.0
Cai Wenjun/WX440054
2017.11.11
Liu Lican/00180730
New
Yuan Weihua/WX462781
2019.4.10
Liu Lican/00180730
Update

## Slide 2: Huawei Data Center Storage System Product Introduction and Maintenance
Huawei Data Center Series of Courses

## Slide 3
This chapter introduces Huawei data center storage products, Including familiarizing with the OceanStor V5 product positioning, hardware architecture, and daily operation and maintenance.

## Slide 4
After completing this course, you will be able to know:
  Positioning of OceanStor V5 converged storage systems.
  Hardware architecture of OceanStor V5 converged storage systems.
  Features of OceanStor V5 converged storage systems.
  The basic daily operation and maintenance operations.

## Slide 5
Product introduction
Hardware introduction
Daily operation and maintenance

## Slide 6
Storage solution
  OceanStor 18000 V5
  OceanStor 6800 V5
  OceanStor 5300/5500/5600/5800 V5
  OceanStor Dorado 2100 G2/5100
Huawei Storage Products

## Slide 7
High specifications
Large capacity, high cache speed, and large number of ports
OceanStor V5 converged storage systems
Wide channel
Latest 16 Gbit/s Fibre Channel, 12 Gbit/s SAS, and PCIe 3.0
Virtualization
Block-level virtualization, heterogeneous virtualization, and computing virtualization
Brand-new hardware architecture delivering industry-leading performance and specifications: The V5 converged storage systems employ 16 Gbit/s Fibre Channel and 10 Gbit/s FCoE host ports and provide up to 768 GB/s system bandwidth, 16 TB cache capacity, and 27 PB storage capacity.
Convergence of SAN and NAS: SAN and NAS are converged to provide elastic storage, simplify service deployment, improve storage resource utilization, and reduce total cost of ownership (TCO).
Outstanding scalability and reliability: Up to eight controllers and linear growth of performance and capacity are supported. Loads are balanced among controllers that serve as hot backup for each other, achieving higher reliability. Resources are centrally stored, simplifying resource management.
Centralized
storage
Tiered
storage
High-density
virtualization
Data disaster
recovery (DR)
Online deduplication and compression
Higher storage resource utilization
Up to sixteen controllers
IP Scale-out and load balancing
Product Positioning

## Slide 8
18800 V5
6800 V5
High-end
storage
Model
Large-scale consolidation
Layer 1 application
virtualization
Mixed workloads
Multiple application
programs
High-performance
application programs
5800 V5
5600 V5
5500 V5
5300 V5
Mid-range
storage
Entry-level
storage
Unified storage
Stable performance
Large capacity and
flexible scalability
Maximum capacity
optimization
High efficiency
Flash memory optimization
Good performance and
sufficient capacity
Ease-of-use
Cost-effective
Enterprise application
programs (Oracle
databases/emails/SAP)
Storage consolidation
Server virtualization
Advanced storage tiering
Data protection
File sharing
Feature
Unified storage
High performance
Large capacity and
flexible scalability
Maximum capacity
optimization
High efficiency
Flash memory optimization
Application
Scenario
2600 V5
2200 V5
Type
Basic consolidation
Microsoft application
Programs
Entry-level server
virtualization
iSCSI SAN
Video surveillance
Large enterprises
Medium enterprises
Small enterprises
High-end storage
Functions first
Mid-range storage
Functions and
prices balanced
Entry-level
storage
Price first
Product Positioning

## Slide 9
High-Performance Applications
  On-Demand System Performance Boost
  Dynamic Storage Tiering for Hotspot Data
High-Availability Applications
  In-Service Routine Maintenance
  Tolerance of Single Points of Failures
  Resilience Against Disasters
High-Density and Multi-Service Applications
  High-Density Virtual Machine Applications
  Multi-Service Applications
Application scenario

## Slide 10
Product positioning
Hardware introduction
  Hardware
  Interface modules
Daily operation and maintenance

## Slide 11
OceanStor V5 converged storage systems adopt brand-new hardware platform.
  2200/2600/5300/5500 V5: disk and controller integration (2 U).
  5600/5800 V5: disk and controller separation (3 U independent engine).
  6800 V5: disk and controller separation (6 U independent engine).
  Active-active controllers.
Product Form
S5500T
6800 V5
5600/5800 V5
2200/2600 V5
5300/5500 V5

## Slide 12
High performance
  PCIe 3.0 high-speed bus and SAS 3.0 high-speed I/O channel
Flexible scalability
  Hot-swappable I/O interface modules
  Support for 4 interface modules and 2 onboard interface modules (2 U)
  Support for 16 interface modules (3 U)
  Support for 24 interface modules (6 U)
Product Features
Robust reliability
  Full redundancy design
  Built-in BBUs+data coffer
  Various data protection technologies
Energy saving
  Intelligent CPU frequency control
  Delicate fan speed control

## Slide 13
SmartThin：Storage space is allocated when it is written. SmartThin allows a host to allocate real space to a Thin LUN when writing data to a Thin LUN.
SmartTier：An intelligent data storage tiering feature can help select an appropriate storage tier for each data block based on the data activity level. This feature improves the storage system performance and lowers the total cost of ownership.
SmartQoS：SmartQoS is an intelligent QoS control feature developed by Huawei that dynamically allocates a storage system's resources to meet specific performance goals of certain applications.
SmartPartition： It allows you to assign cache partitions of different sizes to different applications. The system provides the cache capacity specified by a partition for the corresponding applications, thereby ensuring the performance of the applications in the partition.
Common Storage Advanced Technology

## Slide 14
Power-fan module
1+1 redundancy
AC or 240 V high-voltage DC
Port module
One hot-swappable I/O module slot only on the front end
Port type: 8 x 8 Gbit/s Fibre Channel, GE, 10GE electrical port, SmartIO card (16 Gbit/s Fibre Channel, 8 Gbit/s Fibre Channel, 10 Gbit/s FCoE (VN2VF), and 10 Gbit/s ETH (optical port))
Onboard port
Four GE ports on each OceanStor 2200 V5 controller
SAS expansion port
Each controller provides two SAS expansion ports.
Filler panel
OceanStor 2200 V5 Controller Enclosure

## Slide 15
Port module
Two hot-swappable I/O module slots only on the front end
Port type: 8 Gbit/s Fibre Channel (4 x 8 Gbit/s Fibre Channel or 8 x 8 Gbit/s Fibre Channel), GE, 10GE electrical port, SmartIO card (16 Gbit/s Fibre Channel, 8 Gbit/s Fibre Channel, 10 Gbit/s FCoE (VN2VF), and 10 Gbit/s ETH (optical port)
Power-fan module
1+1 redundancy
AC, -48 V DC, or 240 V high-voltage DC
Onboard port
Four GE ports on each OceanStor 2600 V5 controller
SAS expansion port
Each controller provides two SAS expansion ports.
OceanStor 2600 V5 Controller Enclosure

## Slide 16
5300/5500 V5 Controller Enclosure (25 disk slots)
Notes: Note: The disk slots of a 2 U 25-disk-slot controller enclosure are numbered from 0 to 24 from left to right. Coffer disks are in slots 0 to 3.

## Slide 17
5300/5500 V5 Controller Enclosure (12 disk slots)
Notes: Note: The disk slots of a 2 U 12-disk-slot controller enclosure are numbered from 0 to 11 from left to right and then from top to bottom. Coffer disks are in slots 0 to 3.

## Slide 18
Power-BBU-fan module
1+1 redundancy
Up to 94% power conversion efficiency
Independent BBUs
Support for -48 V and 240 V DC power.
Interface module
Two interface module slots for each controller
Hot-swappable
Rich port types: 16 Gbit/s Fibre Channel, 12 Gbit/s SAS, GE, 10GE TOE, 10GE FCoE, and 8 Gbit/s Fibre Channel
SAS expansion port
Two SAS expansion ports for each controller
USB port
One USB port for each controller (reserved)
Management network port
Configuration network port
Serial port
Onboard port
5300 V5: 4 x GE ports
5500 V5: SmartIO ports
5300/5500 V5 Rear Panel
Notes: Onboard GE ports are supported by the OceanStor 5300 V5 and onboard SmartIO ports are supported by the OceanStor 5500 V5.
A controller enclosure supports 8 Gbit/s Fibre Channel interface modules, GE electrical interface modules, 10GE electrical interface modules, 16 Gbit/s Fibre Channel interface modules, 10 Gbit/s TOE, 10 Gbit/s FCoE (two ports), 10 Gbit/s FCoE (four ports), 56 Gbit/s IB interface modules, SmartIO interface modules, High-Density 8 Gbit/s Fibre Channel interface modules and 12 Gbit/s SAS expansion modules. The following figure uses a 16 Gbit/s Fibre Channel interface module of OceanStor 5500 V5 as an example.
When the maintenance network port is used for management and maintenance, the maintenance network port can only be used by Huawei technical support for emergency maintenance and cannot be connected to the same network with the management network port. Otherwise, a network loopback may occur, causing a network storm. The initial value for the IP address of the maintenance network port is 172.31.128.101 or 172.31.128.102. The default subnet mask is 255.255.0.0. You are advised to only connect the management network port to the network.

## Slide 19
5600/5800 V5 Controller Enclosure
Controller module
Support for dual controllers and four controllers
Mainstream server platform
Automatic frequency control and energy saving
Fan module (integrated into a controller module but maintained independently)0
BBU module
5600 V5: 1+1 redundancy (remaining two slots inserted by filler BBU modules); 5800 V5: 2+1 redundancy (remaining one slot inserted by a filler BBU module)
DC/AC power failure protection
Power module
1+1 redundancy
Up to 94% power conversion efficiency
240 V high-voltage DC
Interface module
16 interface module slots
A maximum of 1250 disks
Hot-swappable
Rich port types: 16 Gbit/s Fibre Channel, 12 Gbit/s SAS, GE, 10GE TOE, 10GE FCoE, and 8 Gbit/s Fibre Channel
Management module
1+1 redundancy
Hot-swappable
Support for multi-controller Scale-out interconnection with a heartbeat mechanism

## Slide 20
1
2
3
5
4
6
7
8
9
Power module
1
Management board
2
USB port (reserved)
3
Management network port
4
Maintenance network port
5
Serial port
6
12 Gbit/s mini SAS HD
7
8 Gbit/s Fibre Channel port
8
GE port
9
5600/5800 V5 Ports

## Slide 21
Controller module
Support for dual controllers and four controllers
Mainstream server platform
Automatic frequency control and energy saving
Fan module (integrated into a controller module but maintained independently)
BBU module
3+1 redundancy
DC/AC power failure protection
6800 V5 Controller Enclosure (1)

## Slide 22
Interface module
Dual controllers: 12 interface module slots; four controllers: 24 interface module slots
A maximum of 2000 disks
Hot-swappable
Rich port types: 16 Gbit/s Fibre Channel, 12 Gbit/s SAS, GE, 10GE TOE, 10GE FCoE, and 8 Gbit/s Fibre Channel
Management module
1+1 redundancy
Hot-swappable
Support for multi-controller Scale-out interconnection with a heartbeat mechanism
Power module
1+1 redundancy
Up to 94% power conversion efficiency
240 V high-voltage DC
6800 V5 Controller Enclosure (2)

## Slide 23
USB port (reserved)
1
Management network port 0
2
Management network port 1
3
Management network port 2
4
Maintenance network port
5
Serial port
6
12 Gbit/s mini SAS HD
7
8 Gbit/s Fibre
Channel port
8
GE port
9
1
7
2
3
4
5
6
8
9
6800 V5 Ports

## Slide 24
600 W power module
1+1 redundancy
Fan modules integrated into a disk enclosure (1+1 fan redundancy, namely, each power module equipped with one fan module)
DC/AC power supplies
Expansion module
Dual expansion modules
12 Gbit/s SAS uplink and downlink
2.5-inch disk unit
No disk connector
Support for 6 Gbit/s SAS disks, NL-SAS disks, and 6 Gbit/s SAS SSDs
2
1
3
Serial port
1
mini SAS HD expansion port
2
Disk enclosure ID display
3
2 U 2.5-inch Disk Enclosure

## Slide 25
4 U 3.5-inch Disk Enclosure
3.5-inch disk unit
No disk connector
Support for 6 Gbit/s NL-SAS disks
600 W power module
1+1 redundancy
Fan modules integrated into a disk enclosure
Support for DC (-48 V)/AC (90 V to 240 V)
Support for 240 V high-voltage DC
Fan module
2 fan modules (2 fan modules and 2 power modules compose a heat dissipation module.)
5+1 redundant fan modules in a disk enclosure
High-speed fans
Expansion module
Dual expansion modules
12 Gbit/s SAS uplink and downlink

## Slide 26
Support for power-on and power-off of a single disk unit
75 disks arranged in 5 lines and 15 rows
4 U 3.5-inch High-density Disk Enclosure (1)

## Slide 27
FRU PSU: 2+2 redundancy
FRU cooling module redundantly configured
16-level intelligent fan speed control, reducing power consumption and noise
FRU SAS expansion module: 1+1 redundancy
Four 4-channel wide 6 Gbit/s SAS data links provided by each I/O module; mini SAS HD port
4 U 3.5-inch High-density Disk Enclosure (2)

## Slide 28
Disk enclosure cover
4 U 3.5-inch High-density Disk Enclosure (3)

## Slide 29
IP Scale-out (2 U)
Front-end service port
Scale-out port
Back-end port
The smart I/O interface module is required by Scale-out and must be inserted into slot 1.
A1
B1
2600 V5
5300/5500 V5

## Slide 30
IP Scale-out (3 U)
5600/5800 V5
The smart I/O interface module is required by Scale-out and must be inserted into slot 3.
Front-end service port
Back-end port
Scale-out port
A3
B3

## Slide 31
IP Scale-out (6 U)
6800 V5
6900 V5
Front-end service port
Back-end port
Scale-out slots (fixed)
A3
B3
The smart I/O interface module is required by Scale-out and must be inserted into slot 3.

## Slide 32
Product introduction
Hardware instruction
  Hardware
  Interface modules
Daily operation and maintenance

## Slide 33
Smart I/O Interface Module
1
2
3
4
5
1 | Power indicator/Hot Swap button
2 | 16 Gbit/s Fibre Channel/8 Gbit/s Fibre Channel/FCoE/iWARP(Scale-Out)
3 | Port indicator (Link/Active/Mode indicator)
4 | Module handle
5 | Port working mode silkscreen
Notes: Power indicator:
  Green on: The module is working properly.
  Blinking green: The module needs to be hot-swapped.
  Red on: The module is faulty.
  Off: The module is not powered on.
Port indicator (Link/Active/Mode indicator):
  Blinking blue slowly: The module is working in FC mode with link down.
  Blinking blue quickly: The module is working in FC mode with link up and data is being transmitted.
  Steady blue: The module is working in FC mode with link up but no data is being transmitted.
  Blinking green slowly: The module is working in FCoE/iWARP mode with link down.
  Blinking green quickly: The module is working in FCoE/iWARP mode with link up and data is being transmitted.
  Steady green: The module is working in FCoE/iWARP mode with link up but no data is being transmitted.

## Slide 34
Onboard Smart I/O Interface Module
1 | 16 Gbit/s Fibre Channel/8 Gbit/s Fibre Channel/FCoE
2 | Port indicator (Link/Active/Mode indicator)
3 | Module handle
4 | Port working mode silkscreen
1
3
2
4
Notes: Port indicator (Link/Active/Mode indicator):
  Blinking blue slowly: The module is working in FC mode with link down.
  Blinking blue quickly: The module is working in FC mode with link up and data is being transmitted.
  Steady blue: The module is working in FC mode with link up but no data is being transmitted.
  Blinking green slowly: The module is working in FCoE mode with link down.
  Blinking green quickly: The module is working in FCoE mode with link up and data is being transmitted.
  Steady green: The module is working in FCoE mode with link up but no data is being transmitted.

## Slide 35
The interface module provides two 4 x 8 Gbit/s Fibre Channel physical ports. The two ports are converted into eight 8 Gbit/s Fibre Channel optical ports using dedicated optical cables (no optical module connected to the eight ports). The eight ports are used as service ports to connect application servers to storage systems and used to receive data exchange commands from application servers.
The interface module contains two 4 x 10 Gbit/s QSFP+ optical modules.
The interface module is equipped with 15 m four-in-one dedicated optical cables.
8 Gbit/s Fibre Channel High-density Interface Module (1)
1 | Power indicator/Hot Swap button
2 | 8 Gbit/s Fibre Channel port
3 | Port Link/Active indicator
4 | Module handle/Silkscreen
1
2
3
4
Notes: Power indicator:
  Green on: The module is working properly.
  Blinking green: The module needs to be hot-swapped.
  Red on: The module is faulty.
  Off: The module is not powered on or can be hot-swapped.
Port Link/Active indicator:
  Blue on: Data is being transmitted at the rate of 8 Gbit/s between the storage system and application servers.
  Blinking blue: Data is being transmitted.
  Green on: Data is being transmitted at the rate of 4 Gbit/s or 2 Gbit/s between the storage system and application servers.
  Blinking green: Data is being transmitted.
  Red on: A port fault occurs.
  Off: The port link is down.

## Slide 36
8 Gbit/s Fibre Channel High-density Interface Module (2)

## Slide 37
10 Gbit/s ETH Electrical Interface Module
1 | Power indicator/Hot Swap button
2 | 10 Gbit/s Ethernet port
3 | Port Link/Active indicator
4 | Port Speed indicator
5 | Module handle
1
2
3
5
4
Notes: Power indicator:
  Green on: The module is working properly.
  Blinking green: The module needs to be hot-swapped.
  Red on: The module is faulty.
  Off: The module is not powered on.
Port Link/Active indicator:
  Green on: The connection between the interface module and application servers is normal.
  Blinking green: Data is being transmitted.
  Off: The connection between the interface module and application servers is abnormal.
Port Speed indicator:
  Orange on: Data is being transmitted at the rate of 10 Gbit/s between the storage system and application servers.
  Off: Data is being transmitted at the rate of lower than 10 Gbit/s between the storage system and application servers.

## Slide 38
56 Gbit/s IB Interface Module
1 | Power indicator/Hot Swap button
2 | 4 lane x 14 Gbit/s IB electrical port
3 | Port Link indicator
4 | Port Active indicator
5 | Module handle/Silkscreen
1
2
3
5
4
Notes: Power indicator:
  Green on: The module is working properly.
  Blinking green: The module needs to be hot-swapped.
  Red on: The module is faulty.
  Off: The module is not powered on or can be hot-swapped.
Port Link indicator:
  On: The connection between the module and application servers is normal.
  Off: The port link is down.
Port Active indicator:
  Blinking: Data is being transmitted.
  Steady on: No data is being transmitted.

## Slide 39
Deduplication and Compression Acceleration Interface Module (ACC)
1 | Power indicator/Hot Swap button
2 | Port Active indicator
3 | Module handle/Silkscreen
1
2
3
Notes: Power indicator:
  Green on: The module is working properly.
  Blinking green: The module needs to be hot-swapped.
  Red on: The module is faulty.
  Off: The module is not powered on or is removable.
Port Active indicator:
  Green on: No data is being processed.
  Blinking green: Data is being processed.
  Off: The module is not working properly.

## Slide 40
Product introduction
Hardware introduction
Daily operation and maintenance
  Information collection tool
  Inspection tool
  Upgrade tool
  FRU replacement tool

## Slide 41
Adding devices: Add devices whose information you want to collect.
Setting collection items: Select desired collection items.
Selecting devices: Select devices whose information you want to collect.
Collecting information: Run the commands to collect information and package collected information.
Information collection completed: After the information collection is complete, you can click Open Directory to view collected information.
Working Process
Adding devices
Setting collection items
Selecting devices
Collecting information
Completing information collection

## Slide 42
Adding Devices

## Slide 43
Collecting Information

## Slide 44
Product introduction
Hardware introduction
Daily operation and maintenance
  Information collection tool
  Inspection tool
  Upgrade tool
  FRU replacement tool

## Slide 45
Selecting the inspection type: Select the inspection type for specific scenarios.
Selecting devices: Select devices that you want to inspect.
Selecting check items: Select desired check items.
Setting a check policy: Set a location for saving inspection reports.
Starting the inspection: Run the commands to start the inspection.
Working Process
Selecting the inspection type
Selecting devices
Selecting check items
Setting a check policy
Starting the inspection

## Slide 46
Selecting the Inspection Type

## Slide 47
Selecting Devices
4

## Slide 48
Selecting Check Items
5

## Slide 49
Setting a Check Policy
7

## Slide 50
Starting Inspection

## Slide 51
Product introduction
Hardware introduction
Daily operation and maintenance
  Information collection tool
  Inspection tool
  Upgrade tool
  FRU replacement tool

## Slide 52
Selecting devices: Select devices that you want to upgrade.
Setting upgrade information: Set a path for saving the upgrade package, a path for saving backup data, and an upgrade mode (online or offline).
Importing the upgrade package: Import the upgrade package into the storage array.
Performing pre-upgrade check: Check whether issues that may affect the upgrade exist.
Backing up data: Back up the database data.
Performing the upgrade: Notify the storage array to perform the upgrade.
Verifying the upgrade: Check whether issues exist.
Working Process
Selecting devices
Importing the upgrade package
Performing pre-upgrade check
Backing up data
Performing the upgrade
Verifying the upgrade
Setting upgrade information

## Slide 53
Selecting Devices (1)

## Slide 54
Selecting Devices (2)
4
5

## Slide 55
Selecting Devices (3)

## Slide 56
Setting Upgrade Information
8
7

## Slide 57
Clicking Perform Upgrade

## Slide 58
Importing the Upgrade Package

## Slide 59
Performing Pre-upgrade Check

## Slide 60
Backing Up Data

## Slide 61
Upgrading the Devices

## Slide 62
Verifying the Upgrade

## Slide 63
Product introduction
Hardware introduction
Daily operation and maintenance
  Information collection tool
  Inspection tool
  Upgrade tool
  FRU replacement tool

## Slide 64
Selecting an FRU: Select an FRU that you want to replace. Replace faulty FRUs first.
Checking status before replacement: Check whether the FRU needs to be replaced. If the FRU does not need to be replaced, an error will be reported.
Replacing the FRU: Replace the FRU following the procedure described in the replacement guide.
Checking status after replacement: Check whether the new FRU is working correctly. If the new FRU is working incorrectly, an error will be reported.
Replacement completed: A message is displayed indicating that the replacement is completed.
Working Process
Selecting an FRU
Checking status before replacement
Replacing the FRU
Checking status after replacement
Completing the replacement

## Slide 65
Power modules are used as an example.
Selecting an FRU
By default, only faulty components are displayed. If you want to select other components, deselect Show faulty components only.
Component silkscreens such as CTE0.PSU0 are used to distinguish FRUs.
You can click Next to start the pre-replacement check only after selecting the FRUs that you want to replace.

## Slide 66
The number of check items varies with the impact scope of FRUs.
If the check result of one item is negative, causes and recommended actions are displayed. After troubleshooting, you can click Recheck to start the check from the item.
You can click Next to replace FRUs only after the results of all check items are positive.
Checking Status Before Replacement

## Slide 67
Replacing the FRU
You can click Replacement Guide to read the replacement guide of the FRU to be replaced.
Strictly follow instructions in the Replacement Guide to replace the FRU.
After the replacement is complete, you can click Replaced to start the post-replacement check.

## Slide 68
Checking Status After Replacement
The number of check items varies with the impact scope of FRUs.
If the check result of one item is negative, causes and recommended actions are displayed. After troubleshooting, you can click Recheck to start the check from the item.
You can click Next to complete the FRU replacement only after the results of all check items are positive.

## Slide 69
Completing the Replacement
A message is displayed indicating that the FRU replacement is complete.
Click Finish to exit.

## Slide 70
What are the common storage technologies used in Huawei's storage solutions?
What is the product positioning of OceanStor V5 storage?
Notes: What are the common storage technologies used in Huawei's storage solutions?
  SmartThin
  SmartTier
  SmartQoS
  SmartPartition
What is the product positioning of OceanStor V5 storage?
  Brand-new hardware architecture delivering industry-leading performance and specifications；Convergence of SAN and NAS；Outstanding scalability and reliability；Up to sixteen controllers，etc.

## Slide 71
Product positioning
Hardware introduction
Routine Operation and Maintenance of the Information Collection Tool.
Routine Operation and Maintenance of the Inspection Tool.
Routine Operation and Maintenance of the FRU Replacement Tool.
Routine Operation and Maintenance of the Upgrade Tool.

## Slide 72
Huawei Learning Website
  http://support.huawei.com/learning/Index!toTrainIndex
Huawei Support Case Library
  http://support.huawei.com/enterprise/servicecenter?lang=zh

## Slide 73
Cloud DC solution
  http://e.huawei.com/cn/solutions/business-needs/data-center