## Slide 1
Storage
5.0
5.0
Tang Jiaojiao/WX498299
2020.5.30
Shui Shaolan/00329529
New
Xu Ningyang/WX1146004
2020.07.03
Shui Shaolan/00329529
Update
Dong Yuyuan/WX889475
2020.07.06
Shui Shaolan/00329529
Update
Ma Deliang/WX1031102
2022.07.01
Liang Shuai/00569373
Update
Update

## Slide 2: Storage Network Architecture

## Slide 3
With the development of host, disk, and network technologies, the storage system architecture evolves, and the storage network architecture also develops to meet service requirements. This course introduces the storage network architecture.

## Slide 4
Upon completion of this lesson, you will be able to understand:
  Storage network architecture evolution
  Storage network technology evolution

## Slide 5
DAS
NAS
SAN
Distributed Architecture

## Slide 6: DAS
File server
Storage device
Application server
Storage
device
Database server
Storage
device
LAN
Data flow
Data flow
Data flow
Client
SCSI
SCSI
SCSI
Notes: Storage devices are directly connected to hosts.
Decentralized data management
Low storage capacity utilization
Poor scalability
DAS is applicable to small- and medium-sized LANs that have general storage capacity requirements and only a few number of servers. The advantages of DAS are easy deployment and small investment.

## Slide 7: DAS
RAID
JBOD
CPU
Disk
RAM
Server
SCSI card
External disk array (DAS)
Disk
CPU
RAM
Server
SCSI card
Controller
Smart disk array (DAS)
Notes: Direct-attached storage (DAS) connects one or more specified storage devices to servers. These storage devices provide block-level data access for the servers.
Based on the locations of storage devices and servers, DAS is classified into internal DAS and external DAS.
External disk array
  JBOD, short for Just a Bunch Of Disks, logically connects several physical disks in series to increase capacity but does not provide data protection. JBOD can resolve the insufficient capacity expansion issue caused by limited disk slots of internal storage. However, it offers no redundancy, resulting in poor reliability.
Smart disk array
  A controller provides RAID and large-capacity cache, enables the disk array to have multiple functions, and is equipped with dedicated management software.
SCSI cables are used to connect hosts and storage devices.

## Slide 8: Challenges for DAS
Challenges | Description
Low Scalability | Limited number of ports that can be connected to a host.
 | Limited number of addressable disks.
 | Limited distance.
Inconvenient Maintenance | The system needs to be powered off during maintenance.
Insufficient Resource Sharing | Front-end ports and storage space are difficult to share.
 | Resource silos: For example, the DAS with insufficient storage space cannot share the remaining space of the DAS with excessive storage resources.
Notes: DAS relies on the server host operating system to perform data I/O read/write and storage maintenance and management. Data backup and recovery occupy server host resources (including CPU and system I/O). Data flows need to flow back to the host and then to the tape library connected to the server. Data backup usually occupies 20% to 30% of server host resources, therefore, routine data backup of many enterprise users is usually performed at midnight or during off-peak hours of the service system to ensure the normal running of the service system. For the DAS storage, larger data amount leads to longer-time backup or recovery and stronger dependence on the server hardware.
SCSI channels are used to connect DAS to servers. The bandwidth is 10 MB/s, 20 MB/s, 40 MB/s, or 80 MB/s. As the processing capability of the server CPU becomes stronger, the storage disk space becomes larger, and the number of disks in the array increases, SCSI channels will become the I/O bottleneck. The SCSI ID resources of the server host are limited, and the SCSI channel connections that can be established are limited.
Expansion of DAS or the server, expansion from one server to a cluster consisting of multiple servers, or expansion of the storage array capacity will cause the service system to be shut down, which brings economic losses to enterprises. This is unacceptable for mission-critical service systems that provide 24/7 services in industries such as banking, telecommunications, and media. In addition, the upgrade and expansion of DAS or server hosts can only be provided by the original device vendor, which is restricted by the original device vendor.

## Slide 9
DAS
NAS
SAN
Distributed Architecture

## Slide 10: NAS
Network-attached storage (NAS) connects storage devices to the live network and provides data and file services.
The most commonly used network sharing protocols for NAS are Common Internet File System (CIFS) and Network File System (NFS).
OS: Windows
OS: Linux
OS: MAC OS
Switch
NAS device
Benefits:
  Improved efficiency
  Improved flexibility
  Centralized storage
  Simplified management
  High scalability
  High availability
  Security (user authentication and authorization)
Notes: Enterprises need to store a large amount of data and share the data through a network. Therefore, NAS is a good choice. For a server or host, NAS is an external device and can be flexibly deployed through the network. In addition, NAS provides file-level sharing rather than block-level sharing, which makes it easier for clients to access NAS over the network.
  NAS provides storage resources through file-level data access and sharing, enabling customers to quickly share files with minimum storage management costs.
  NAS is a preferred file sharing storage solution that does not require multiple file servers.
  NAS also helps eliminate bottlenecks in user access to general-purpose servers.
  NAS uses network and file sharing protocols for archiving and storage. These protocols include TCP/IP for data transmission as well as CIFS and NFS for providing remote file services.
UNIX and Microsoft Windows users can seamlessly share data through NAS or File Transfer Protocol (FTP). When NAS sharing is used, UNIX uses NFS and Windows uses CIFS.
NAS is actually an optimized file server.

## Slide 11: General-Purpose Server and NAS Devices
Network
OS
File system
Network
OS
File system
Printer driver
Application
General-purpose server
(Windows or UNIX)
Uni-functional NAS device
Notes: NAS devices are optimized based on general-purpose servers, such as file service functions, storage, and retrieval.
As shown in the figure, a general-purpose server can be used to carry any application and run a general-purpose operating system. Unlike general-purpose servers, NAS is dedicated to file services and provides file sharing services for other operating systems using open standard protocols. To improve the high availability of NAS devices, some NAS vendors also support the NAS clustering function.
The components of a NAS device are as follows:
  NAS engine (CPU and memory)
  One or more NICs that provide network connections, for example, GE NIC and 10GE NIC.
  An optimized operating system for NAS function management
  NFS and CIFS protocols
  Disk resources that use industry-standard storage protocols, such as ATA, SCSI, and FC
The NAS environment includes clients that access NAS devices over IP networks using standard protocols.

## Slide 12: NAS Protocols
FS
CACHE
POOL
IP
IP
IP
IP
Linux
Enterprise office
IP
IP
IP
IP
Windows
Enterprise office
NFS
CIFS
FTP
HTTP
NDMP
NFS
CIFS

## Slide 13
Notes: NFS is a traditional file sharing protocol in the UNIX environment.
CIFS is a file sharing protocol in the traditional Microsoft environment. It is based on the Server Message Block (SMB) protocol.
Based on the network, CIFS has high requirements on network transmission reliability. Therefore, it usually uses TCP/IP. NFS is used for independent transmission. Therefore, it uses TCP or UDP.
One disadvantage of NFS is that clients must be equipped with dedicated software. CIFS is integrated into the operating system and does not require additional software.
NFS is a stateless protocol, whereas CIFS is a stateful protocol. The NFS connection can be automatically recovered after a fault occurs, while the CIFS connection cannot. CIFS sends only a small amount of redundant information. Therefore, it has higher transmission efficiency than NFS.
File Transfer Protocol (FTP) is one of the protocols in the TCP/IP protocol suite. It consists of two parts: FTP server and FTP client. The FTP server is used to store files. Users can use the FTP client to access resources on the FTP server through FTP.
Hypertext Transfer Protocol (HTTP) is an application-layer protocol used to transfer hypermedia documents (such as HTML). It is designed for communication between a Web browser and a Web server, but can also be used for other purposes.
Network Data Management Protocol (NDMP) enables data to be directly written to tapes without being backed up by backup servers, improving the speed and efficiency of NAS data protection.

## Slide 14: Working Principles of NFS
Client program
RPC
RPC
NFS processes:
rpc.nfsd and Rpc.mountd
POR TMAP
Port mapping table
NFS share information
1. RPC request
2. RPC response
3. Communication
Client
Server
Registration
Request
Notes: One program can use remote procedure call (RPC) to request a service from a program located in another computer on a network without having to understand the network's details. RPC runs on top of other transmission protocols such as Transmission Control Protocol (TCP) or User Datagram Protocol (UDP), which carry the message data between communicating programs. In the OSI network communication model, RPC traverses the transport layer and application layer. RPC simplifies development of applications such as a network distributed multi-program.
RPC works based on the client/server model. The requester is a client, and the service provider is a server. The client sends a call request with parameters to the RPC server and waits for a response. On the server side, the process remains in a sleep state until the call request arrives. Upon receipt of the call request, the server obtains the process parameters, outputs the calculation results, and sends the reply to the client. Then, the server waits for the next call request. The client receives the reply and obtains call results.

## Slide 15: Typical Application of NFS: Shared Storage for Cloud Computing
Cloud computing uses the NFS server as the internal shared storage.
Cloud computing server
Internal IP network
NFS client
Converged storage
NFS server
Cloud computing server
Cloud computing server
External IP network
Firewall
Notes: Cloud virtualization software (such as VMware) optimizes the NFS client, so that the VM storage space can be created on the shared space of the NFS server.
The NFS client optimized based on cloud computing provides better performance and reliability.

## Slide 16: Working Principles of CIFS
Client
Server
SMB NEGOTIATE Request
SMB NEGOTIATE Response
SMB SESSION_SETUP Request
SMB SESSION_SETUP Response
SMB TREECONNECT Request
SMB TREECONNECT Response
SMB TREE_DISCONNECT Request
SMB TREE_DISCONNECT Response
Protocol negotiation
Protocol handshake
Security authentication
Share connection
File operation
Disconnection
Session setup
Tree connection
Network file operation
Disconnection
......
Notes: Authentication modes: NTLM and Kerberos
Network communication may be implemented over TCP or in another manner such as RDMA.
Network file operations are processed and then transferred to the actual file system.
NT LAN Manager Security Support Provider (NTLMSSP): Introduced in Windows NT, NTLM employs a 64-bit encryption algorithm to provide authentication to users.
Kerberos network authentication: Kerberos is a computer network authentication protocol. It is designed to provide strong authentication for client/server applications using secret-key cryptography.

## Slide 17: Typical Application of CIFS: File Sharing Service
The file sharing service applies to scenarios such as enterprise file servers and media assets.
LAN
AD server
DNS
Windows
Performance monitoring
Service management
Share management
User management
Enterprise office
IP
IP
IP
IP
NAS service
Management
IP
IP
Authentication flow
Management flow
Data flow
Notes: Domain Name Service (DNS) is used to implement the mapping between domain names and IP addresses.
Active directory (AD) provides directory services.
The CIFS protocol applies to file sharing. Two typical application scenarios are as follows:
  File sharing service
    CIFS is commonly used in file sharing service scenarios such as the file sharing of enterprise file servers and media, providing the file sharing service for users.
  Hyper-V scenarios
    SMB can be used to share mirrors of Hyper-V virtual machines promoted by Microsoft. In this scenario, the failover feature of SMB 3.0 is required to ensure service continuity upon a node failure and reliability of VMs.

## Slide 18
DAS
NAS
SAN
  IP SAN Technologies
  FC SAN Technologies
  Comparison Between IP SAN and FC SAN
Distributed Architecture

## Slide 19: NIC + Initiator Software
Internal bus
Ethernet
The initiator software converts iSCSI packets into TCP/IP packets, which consumes host resources.
TCP/IP-based Ethernet connection
Storage device
IP SAN
NIC
Notes: Host devices such as servers and workstations use standard NICs to connect to Ethernet switches. iSCSI storage devices are also connected to the Ethernet switches or to the NICs of the hosts. The initiator software installed on hosts virtualizes NICs into iSCSI cards. The iSCSI cards are used to receive and transmit iSCSI data packets, implementing iSCSI and TCP/IP transmission between the hosts and iSCSI devices. This mode uses standard Ethernet NICs and switches, eliminating the need for adding other adapters. Therefore, this mode is the most cost-effective. However, this mode occupies host resources when converting iSCSI packets into TCP/IP packets, increasing host operation overheads and degrading system performance. The NIC + initiator software mode is applicable to the scenarios that require the relatively low I/O and bandwidth performance for data access.

## Slide 20: TOE NIC + Initiator Software
The initiator software implements the functions of the iSCSI layer, which consumes host resources.
TCP/IP-based Ethernet connection
The TOE NIC implements TCP/IP conversion, which does not consume host resources.
Internal bus
Ethernet
Storage device
IP SAN
TOE NIC
Notes: The TOE NIC processes the functions of the TCP/IP protocol layer, and the host processes the functions of the iSCSI protocol layer. Therefore, the TOE NIC can greatly improve the data transmission rate. Compared with the pure software mode, this mode reduces host operating overheads and requires only a little additional network construction cost. This is a trade-off solution.

## Slide 21: iSCSI HBA
TCP/IP-based Ethernet connection
The iSCSI HBA converts iSCSI packets into TCP/IP packets, which does not consume host resources.
Internal bus
Ethernet
Storage device
IP SAN
iSCSI HBA
Notes: An iSCSI HBA is installed on the host to implement efficient data exchange between the host and switch and between the host and storage device. Functions of the iSCSI protocol layer and TCP/IP protocol stack are handled by the host HBA, consuming the least CPU resources. This mode delivers the best data transmission performance while requiring the highest cost.
The iSCSI communication system inherits part of SCSI's features. The iSCSI communication involves an initiator that sends I/O requests and a target that responds to the I/O requests and executes I/O operations. After a connection is set up between the initiator and target, the target controls the entire process as the primary device. The target includes the iSCSI disk array and iSCSI tape library.
The iSCSI protocol defines a set of naming and addressing methods for iSCSI initiators and targets. All iSCSI nodes are identified by their iSCSI names. Such method distinguishes iSCSI names from host names.
iSCSI uses iSCSI Qualified Name (IQN) to identify initiators and targets. Addresses change with the relocation of initiator or target devices, but their names remain unchanged. When setting up a connection, an initiator sends a request. After the target receives the request, it checks whether the iSCSI name contained in the request is consistent with that bound with the target. If the iSCSI names are consistent, the connection is set up. Each iSCSI node has a unique iSCSI name. One iSCSI name can be used in the connections from one initiator to multiple targets. Multiple iSCSI names can be used in the connections from one target to multiple initiators.

## Slide 22: Logical Port
Logical ports are created based on bond ports, VLAN ports, or Ethernet ports. The logical ports are virtual ports that carry host services.
A unique IP address is allocated to each logical port for carrying its services.
1
Ethernet port
Logical port
Bond port
VLAN
Many to one
One to many
One to many
One to many
One to many
One to many
2
3
4
5
6
No. | Description
1 | Indicates that multiple Ethernet ports are bonded to form a bond port.
2 | Indicates that an Ethernet port is added to multiple VLANs.
3 | Indicates that a bond port is added to multiple VLANs.
4 | Indicates that a bond port is used to create multiple logical ports.
5 | Indicates that a VLAN port is used to create multiple logical ports.
6 | Indicates that an Ethernet port is used to create multiple logical ports.
Notes: Ethernet port: Physical Ethernet ports on an interface module of a storage system. Bond ports, VLANs, and logical ports are created based on Ethernet ports.
Bond port: To improve reliability of paths for accessing file systems and increase bandwidth, you can bond multiple Ethernet ports on the same interface module to form a bond port.
VLAN: VLANs logically divide the physical Ethernet ports or bond ports of a storage system into multiple broadcast domains. On a VLAN, when service data is being sent or received, a VLAN ID is configured for the data so that the networks and services of VLANs are isolated, further ensuring service data security and reliability.

## Slide 23: VLAN Configuration
VLAN is a technology that logically divides a physical LAN into multiple broadcast domains.
Ethernet ports or bond ports in a storage system can be added to multiple independent VLANs. You can configure different services in different VLANs to ensure the security and reliability of service data.
VLAN 1
ID = 1
VLAN 2
ID = 2
VLAN 3
ID = 3
VLAN k
ID = k
......
P0
P1
P2
P3
Storage device
Ethernet port
Adding ports to VLANs
Bond port
Notes: VLAN: virtual local area network.
LAN: local area network.
The ID of each VLAN can be a number ranging from 1 to 4094.

## Slide 24: IP Address Failover
IP address failover indicates that a logical IP address fails over from a faulty port to an available port. In this way, services are switched from the faulty port to the available port without interruption. The faulty port can take over services back after being recovered.
During the IP address failover, services are switched from the faulty port to the available port, ensuring service continuity and improving reliability of paths for accessing file systems. This process is transparent to users.
The essence is a service switchover between ports. The ports can be Ethernet ports, bond ports, or VLAN ports.
Notes: A failover group is a combination of ports that are used for IP address failover in a storage system.
Failback: After a faulty port recovers, it takes over its services. This task can be completed automatically or manually.
IP address failover applies to IP SAN and NAS.

## Slide 25: Ethernet Port–based IP Address Failover
To improve reliability of paths for accessing file systems, you can create logical ports based on Ethernet ports.
When the Ethernet port that corresponds to a logical port fails, the system will:
  Locate an available Ethernet port of the same type.
  Delete the logical port from the faulty Ethernet port.
  Create the same logical port on the available Ethernet port to carry services.
  Ensure service continuity.
Logical port A
(IP address a)
Ethernet port A
Logical port A
Ethernet port A
Logical port A
(IP address a)
Ethernet port B
Search
Port switchover
Port fault
Notes: Host services are running on logical port A of Ethernet port A. The corresponding IP address is a. Ethernet port A fails and thereby cannot provide services. After IP address floating is enabled, the storage system will automatically locate available Ethernet port B, delete the configuration of logical port A that corresponds to Ethernet port A, and create and configure logical port A on Ethernet port B. In this way, host services are quickly switched to logical port A on Ethernet port B. The service switchover is executed quickly. It is transparent to users.

## Slide 26: Bond Port–based IP Address Failover
To improve reliability of paths for accessing file systems, you can bond multiple Ethernet ports to form a bond port.
When the Ethernet ports that are used to create the bond port fails, the system will:
Search
Port switchover
Port fault
Logical port A
(IP address a)
Ethernet port A
Bond port A
Ethernet port B
Ethernet port B
Logical port A
Ethernet port A
Bond port A
Ethernet port D
Ethernet port C
Logical port A
(IP address a)
Bond port A
High-speed data transmission
  Locate an available port.
  Delete the logical port created on the faulty port.
  Create a logical port with the same IP address on the available port.
  Switch services to the available port.
  After the faulty port recovers, it can take over services again.
Notes: When an Ethernet port that is used to create the bond port fails, services are still running on the bond port. The IP address fails over only when all Ethernet ports that are used to create the bond port fail.
Multiple Ethernet ports are bonded to form bond port A. Logical port A created based on bond port A can provide high-speed data transmission. When both Ethernet ports A and B fail due to various causes, the storage system will automatically locate bond port B, delete logical port A, and create the same logical port A on bond port B. In this way, services are switched from bond port A to bond port B. After Ethernet ports A and B recover, services will be switched back to bond port A. The service switchover is executed quickly and thereby transparent to users.

## Slide 27: VLAN-based IP Address Failover
You can create VLANs to isolate different services.
When an Ethernet port on a VLAN fails, the system will:
Search
Port switchover
Port fault
Logical port A
(IP address a)
Ethernet port A
VLAN A
ID = 1
Logical port A
Ethernet port A
VLAN A
ID = 1
Logical port A
(IP address a)
Ethernet port B
VLAN B
ID = 1
  Locate an available port of the same type.
  Delete the logical port from the faulty port.
  Create the same logical port on the available port.
  Switch services to the available port.
Notes: To implement VLAN-based IP address failover, you must create VLANs, allocate a unique ID to each VLAN, and use the VLANs to isolate different services. When an Ethernet port on a VLAN fails, the storage system will automatically locate an available Ethernet port with the same VLAN ID and switch services to the available Ethernet port. After the faulty port recovers, it takes over its services again.
VLAN names, such as VLAN A and VLAN B, are automatically generated when VLANs are created. The actual VLAN names depend on the storage system version.
Ethernet ports and their corresponding switch ports are divided into multiple VLANs, and different IDs are allocated to the VLANs. The VLANs are used to isolated different services. VLAN A is created on Ethernet port A, and the VLAN ID is 1. Logical port A that is created based on VLAN A can be used to isolate services. When Ethernet port A fails due to various causes, the storage system will automatically locate VLAN B and the port whose VLAN ID is 1, delete logical port A, and create the same logical port A based on VLAN B. In this way, the port where services are running is switched to VLAN B. After Ethernet port A recovers, the port where services are running will be switched back to VLAN A.
An Ethernet port can belong to multiple VLANs. When the Ethernet port fails, all VLANs will fail. You must switch services to ports of other available VLANs. The service switchover is executed quickly. It is transparent to users.

## Slide 28
DAS
NAS
SAN
  IP SAN Technologies
  FC SAN Technologies
  Comparison Between IP SAN and FC SAN
Distributed Architecture

## Slide 29: FC HBA
Fibre Channel protocol-based
The FC HBA converts SCSI packets into Fibre Channel packets, which does not consume host resources.
Internal bus
FC network
Storage device
FC SAN
FC HBA

## Slide 30: FC Network
Notes: Fibre Channel Routing (FCR) provides connectivity to devices in different fabrics without merging the fabrics. Different from E_Port cascading of common switches, after switches are connected through an FCR switch, the two fabric networks are not converged and are still two independent fabrics. The link switch between two fabrics functions as a router.
FC Router: a switch running the FC-FC routing service.
EX_Port: A type of port that functions like an E_Port, but does not propagate fabric services or routing topology information from one fabric to another.
Backbone fabric: fabric of a switch running the FC router service.
Edge fabric: a fabric that connects a Fibre Channel router.
Inter fabric link (IFL): the link between an E_Port and an EX-Port, or a VE_Port and a VEX-Port.

## Slide 31: Zoning
Storage 2
Server 1
Server 3
Server 2
Storage 1
Storage 3
Zone 1: Server 1 can access Storage 1.
Zone 2: Server 2 can access Storage 2.
Zone 3: Server 3 can access Storage 1 and Storage 2.
Notes: A zone is a set of ports or devices that can communicate with each other.
A zone member can only access other members of the same zone.
A device can reside in multiple zones.
Basic Zones are configured to control the access permission of each device or port.
Traffic Isolation Zones: When there are multiple ISLs (E_Ports), an ISL only transmits the traffic destined for ports that reside in the same traffic isolation zone.

## Slide 32
DAS
NAS
SAN
  IP SAN Technologies
  FC SAN Technologies
  Comparison Between IP SAN and FC SAN
Distributed Architecture

## Slide 33: IP SAN and FC SAN
FC
FC
FC
FC
FC SAN
iSCSI
iSCSI
IP SAN
IP
IP
Notes: To solve the poor scalability issue of DAS, storage devices can be networked using FC SAN to support connection to more than 100 servers.
IP SAN is designed to solve the price and management issues of FC SAN.
SAN: Storage Area Network
  Protocol: Fibre Channel/iSCSI. The SAN architectures that use the two protocols are FC SAN and IP SAN.
  Raw device access: suitable for traditional database access.
  Dependence on the application host to provide file access. Share access requires the support of cluster software, which causes high overheads in processing access conflicts, resulting in poor performance. In addition, it is difficult to support sharing in heterogeneous environments.
  High performance, high bandwidth, and low latency, but high cost and poor scalability

## Slide 34: Comparison Between IP SAN and FC SAN
Item | IP SAN | FC SAN
Network architecture | Existing IP networks | Dedicated Fibre Channel networks and HBAs
Transmission distance | Not limited theoretically | Limited by the maximum transmission distance of optical fibers
Management and maintenance | As simple as operating IP devices | Complicated technologies and management
Compatibility | Compatible with all IP network devices | Poor compatibility
Cost | Lower purchase and maintenance costs than FC SAN, higher return on investment (ROI) | High purchase (Fibre Channel switches, HBAs, Fibre Channel disk arrays, and so on) and maintenance (staff training, system configuration and supervision, and so on) costs
Disaster recovery (DR) | Local and remote DR available based on existing networks at a low cost | High hardware and software costs for DR
Security | Relatively low | Relatively high
Notes: IP SAN requires only a few hardware configurations and the hardware is widely used. Therefore, the cost of IP SAN is much lower than that of FC SAN. Most hosts have been configured with appropriate NICs and switches, which are also suitable (although not perfect) for iSCSI transmission. High-performance IP SAN requires dedicated iSCSI HBAs and high-end switches.

## Slide 35: Comparison Between DAS, NAS, and SAN
Storage System Architecture | DAS | NAS | SAN
Data transmission protocol | SCSI/FC/ATA | TCP/IP | FC
Transport object | Data block | File | Data block
Using standard file sharing protocols | No | Yes (NFS/CIFS......) | No
Centralized management | Not sure. | Yes | Management tools required
Improving server efficiency | No | Yes | Yes
Disaster tolerance | Low | High | High, dedicated solution
Application scope | SME servers and JBOD | SME, monitoring, and broadcasting | Large enterprises and data centers
Application environment | LAN Documents are seldom shared, the operation platform is independent, and the number of servers is small. | LAN Documents are highly shared, and different media formats have high storage requirements. | Fibre channel storage domain network Complex network environment, high degree of document sharing, heterogeneous operating system platform, and a large number of servers.
Capacity expansion capability | Low | Medium | High

## Slide 36
DAS
NAS
SAN
Distributed Architecture

## Slide 37: Scale-out Storage Networking
Front-end service network
Management network
Back-end storage network
Node 1
Node 2
Node 3
Node 4
Node 5
Notes: A scale-out storage system organizes local HDDs and SSDs of general-purpose servers into large-scale storage resource pools, and then distributes data to multiple data storage servers.
10GE, 25GE, and IB networks are generally used as the backend networks of scale-out storage. The front-end network is usually a GE, 10GE, or 25GE network.

## Slide 38: Networking Overview
Front-end service/Tenant network
  The front-end service/tenant network is used to interconnect the scale-out storage with the customer network. It provides the tenant UI for tenant users to complete operations such as resource application and usage query, and processes service requests sent by tenant clients or APIs.
Back-end storage network
  The back-end storage/internal management network is used for internal interconnection between nodes. It provides heartbeat communication between high availability (HA) components such as the data service subsystem (DSS), and internal communication and data interaction between components.
Management network
  The management network is used to interconnect with the customer's maintenance network. It provides a management UI for the system administrator to perform service operations such as system configuration, tenant management, resource management, and service provisioning, as well as maintenance operations such as alarm, performance, and topology management. In addition, the Mgmt ports of all physical nodes can be aggregated to provide remote device maintenance capabilities, such as remotely logging in to the virtual KVM of a device and viewing hardware running data such as temperature and voltage.

## Slide 39: Network Planes
Management
node
Compute node
Storage node
FSM
VBS
EDS
OSD
REP
Application
DR site
Third-place quorum server
Private client access mode
Management
node
Compute node
Storage node
FSM
VBS/HDFS-SVR
EDS
OSD
REP
Application
DR site
Third-place quorum server
Standard protocol access mode
Management plane:
Storage plane:
Replication plane:
Arbitration plane:
Service plane:

## Slide 40
Notes: Management plane: interconnects with the customer's management network for system management and maintenance.
BMC plane: connects to Mgmt ports of management or storage nodes to enable remote device management.
Storage plane: an internal plane, used for service data communication among all nodes in the storage system
Service plane: interconnects with customer applications and accesses storage devices through standard protocols such as iSCSI and HDFS.
Replication plane: enables data synchronization and replication among replication nodes.
Arbitration plane: communicates with the HyperMetro quorum server. This plane is planned only when the HyperMetro function is planned for the block service.
FSM: a management process of Huawei scale-out storage that provides operation and maintenance (O&M) functions, such as alarm management, monitoring, log management, and configuration. It is recommended that this module be deployed on two nodes in active/standby mode.
Virtual Block Service (VBS): a process that provides the scale-out storage access point service through SCSI or iSCSI interfaces and enables application servers to access scale-out storage resources
Object Storage Device (OSD): a component of Huawei scale-out storage. It stores user data of distributed clusters.
REP: data replication network.
Enterprise Data Service (EDS): performs I/O operations after receiving I/O services from VBS.

## Slide 41: Networking Rules
Nodes must be placed in a cabinet from bottom to top.
A deployment solution is usually chosen based on project requirements. The total power consumption and weight of the storage nodes, switches, and KVM in a cabinet must be calculated and the number of nodes that can be housed by a cabinet must be determined based on the equipment room conditions.
In typical configuration, nodes and switches in the base cabinet are connected through network cables and SFP+ cables, and nodes in an expansion cabinet connect to switches in the base cabinet through network cables and optical fibers.

## Slide 42
1. Which of the following are included in scale-out storage networking?
  Management network
  Front-end service network
  Front-end storage network
  Back-end storage network
2. Which of the following protocols are commonly used in SAN networking?
  FC
  iSCSI
  CIFS
  NFS
Notes: Answers:
  ABD
  AB

## Slide 43
Storage network
architecture evolution
NAS
SAN
Distributed architecture
IP SAN
FC SAN
DAS
Comparison between IP SAN and FC SAN

## Slide 44
Huawei official websites
  Enterprise business: https://e.huawei.com/en/
  Technical support: https://support.huawei.com/enterprise/en/index.html
  Online learning: https://www.huawei.com/en/learning
Popular tools
  HedEx Lite
  Network Document Tool Center
  Information Query Assistant
Notes: Popular tools
  HedEx Lite: Huawei product document management tool, which allows users to browse, search for, update, and manage product documentation.
  eStor: A graphic storage simulation platform. Through simulation of Huawei OceanStor all-flash storage devices, the platform helps ICT practitioners and customers quickly get familiar with Huawei storage products, and understand and master their operations and configurations.
  Network Documentation Tool Center: The documentation tool for network products is a good assistant for bidding support, network planning, project delivery, and upgrade and maintenance.
  Information Query Assistant: provides command and alarm information query for Huawei products.

## Slide 45: Acronyms and Abbreviations
Direct Attached Storage (DAS): An external storage device is directly connected to a computer through a cable.
Redundant Array of Independent Disks (RAID): It is a technology that provides a disk group (logical disk) consisting of multiple disks (physical disks) combined in different modes. The disk group features higher storage performance over a single disk and supports data redundancy.
Redirect on write (ROW): A core technology used to create file system snapshots. When a source file system receives a write request to modify existing data, the storage system writes the new data to a new location and directs the BP of the modified data block to the new location.
Virtual Local Area Network (VLAN): A VLAN is a group of hosts with a common set of requirements that communicate as if they were attached to the same broadcast domain, regardless of their physical location. VLAN membership can be configured through software instead of physically relocating devices or connections.
HBA: Host Bus Adapter
KVM: keyboard, video, and mouse. You can use the KVM to remotely view the screen of the terminal host or use the local mouse and keyboard to remotely control the terminal host. In this way, the administrator can remotely solve the problems that occur on the terminal host.